## Slide 1: Testing the Transferability of Activity-Based Model Parameters
TRB Planning Applications Conference
May 10, 2011
Andrew Rohne, OKI Regional Council
Vince Bernardin Jr., Bernardin, Lochmuller & Associates

## Slide 2: The Question…
Can we eliminate the need
for expensive travel surveys
in similar metropolitan areas?
Notes: The OKI Household Travel Survey was $1.3 million, and the transit survey was another $300k.
By eliminating the need, I’m not talking about NOT doing them altogether, but instead doing one throughout a state (perhaps one would cover Cincinnati, Columbus, Cleveland, and Dayton), and we would share the data AND the cost.
For this project, I used Cincinnati vs. Columbus, since Columbus has an activity based model, we are developing one, and our HHTS is almost complete. However, because of the timing of the household travel survey data, I was only able to use a draft dataset.

## Slide 3: The Test…
Take the Mid-Ohio Regional Planning Commission AB/TB Model…
Use it to create a synthesized HH set for Cincinnati…
Test Auto Ownership and Activity Models…

## Slide 4: Cincinnati ≈ Columbus
Similar Population
Similar Modal Alternatives
100 miles away
Notes: Cincinnati and Columbus are very similar. Both are around 2 million people (Cincinnati is slightly larger). Both have similar modal alternatives – non-motorized, driving, and express bus; no light rail or commuter rail. Also, the share of people riding transit is similar for both metropolitan areas. Being so close – only around 100 miles apart, means that there are few (if any) immeasurable issues (such as significant differences caused by political mindsets, religion).

## Slide 5: Cincinnati ≠ Columbus
Cincinnati is Multi-State
Columbus is the State Capitol
OSU vs. UC+Xavier+Miami+NKU
Buckeyes vs. cats
Notes: There are a few differences. 40% of the Cincinnati Metropolitan Region is outside the state of Ohio. Columbus is the state Capitol, so there are a lot more government-based jobs.
Also, Columbus has the largest public university in north America; Cincinnati has three different major universities. When it comes to fans, though, Cincinnati has a lot of Buckeye fans, but also a lot of UK Wildcat fans (as well as UC fans!)

## Slide 6: Original Methodology
Run Auto Ownership and Activity Generation Models
MORPC’s Coefficients and Constants
MORPC’s Coefficients, calibrate Constants
MORPC’s models, calibrate Coefficients and Constants
Full Re-Estimation
OKI data => MORPC Population Synthesizer
Synthesize
OKI Pop. & HHs
Notes: I started out by adapting OKI’s SEDATA into the formats acceptable for MORPC’s population synthesizer. This gave me a synthetic population for the OKI region. Once I had that, I ran with MORPC’s auto ownership and activity generation models “out of the box”, calibrating the constants, calibrating the coefficients and constants, and re-estimating the model.

## Slide 7: Revised Methodology
Run Auto Ownership and Activity Generation Models
MORPC’s Coefficients and Constants
MORPC’s Coefficients, calibrate Constants
MORPC’s models, calibrate Coefficients and Constants
Full Re-Estimation
OKI data => MORPC Population Synthesizer
NOTES
Draft HHTS Data
Removed certain variables from model specs
Calibrate
OKI Pop. & HHs
Synthesize
OKI Pop. & HHs
Notes: Due to timing of the household survey delivery, I was unable to do a large part of this… yet.

## Slide 8: Number of HHs by Autos Owned
Chart: 
| 4+ Autos | 3 Autos | 2 Autos | 1 Auto | 0 Autos
Calibrate Constants | 49227 | 120075 | 289772 | 262147 | 99529
As-Is | 49757 | 96448 | 312195 | 294668 | 67682
ACS | 48131 | 109708 | 292966 | 242303 | 64189
DRAFT HHTS Data
Notes: For the next few slides, I will be showing the number of households by the autos owned. In all cases, I am showing the ACS 2005-2007 data (the input data was for 2005), As-Is, which is MORPC’s coefficients and constants, and Calibrating the constants. I calibrated the constants by ‘gaming’ them, so they are not perfect.
This slide shows the regional number of Autos owned by county. The calibration scenario was better for the 1-4+ auto categories, but there are more 0 auto households.

## Slide 9: HHs by Autos Owned, Hamilton Co.
Chart: 
| 4+ Autos | 3 Autos | 2 Autos | 1 Auto | 0 Autos
Calibrate Constants | 5326 | 5030 | 182576 | 155727 | 25038
As-Is | 5857 | 7675 | 179179 | 171419 | 9567
ACS | 17311 | 40309 | 112855 | 119471 | 41760
DRAFT HHTS Data
Notes: Hamilton County is where the City of Cincinnati resides, and is the most urban and dense county in the region. This graph shows that both the As-Is and Calibrate Constants scenarios did poorly for this county.

## Slide 10: HHs by Autos Owned, Butler Co.
Chart: 
| 4+ Autos | 3 Autos | 2 Autos | 1 Auto | 0 Autos
Calibrate Constants | 27076 | 27364 | 30334 | 32878 | 24497
As-Is | 26009 | 27224 | 33532 | 36538 | 18846
ACS | 8848 | 19947 | 54524 | 39152 | 7260
DRAFT HHTS Data
Notes: Butler County is the fastest growing county in the region. It is located between Dayton and Cincinnati, and has trips going to both metropolitan areas. As you can see from this, both scenarios are pretty bad except for 1 auto.

## Slide 11: HHs by Autos Owned Suburban Counties
Chart: 
| 4+ Autos | 3 Autos | 2 Autos | 1 Auto | 0 Autos
Calibrate Constants | 29596 | 92268 | 88822 | 84652 | 60735
As-Is | 31292 | 68617 | 109910 | 98246 | 48008
ACS | 23157 | 51855 | 141576 | 101348 | 19818
DRAFT HHTS Data
Notes: This is the HHs by autos owned for the 4 suburban counties in the region (Butler, Campbell, Clermont, and Kenton counties). These counties are mostly suburban (at least 40%).

## Slide 12: HHs by Autos Owned, Dearborn Co.
Chart: 
| 4+ Autos | 3 Autos | 2 Autos | 1 Auto | 0 Autos
Calibrate Constants | 0 | 7578 | 3835 | 4512 | 2858
As-Is | 0 | 7360 | 4155 | 5125 | 2143
ACS | 2644 | 4005 | 6677 | 3937 | 880
DRAFT HHTS Data
Notes: Dearborn County is the most rural county in the region, and this graph shows some pretty extreme over-estimation of 0 auto households and a pretty extreme underestimation of 4+ autos (the graph is NOT an error – there are actually 0 HHs with 4+ autos assigned).

## Slide 13: Conclusions and Lessons Learned
We still need travel surveys
Trip-Based Model Calibration Process Still Applies (in Concept)
Regional Calibration ≠ Local Calibration
Don’t submit an abstract until you have the data!!!
Notes: We still need to have travel surveys for parts of the model, at least for the auto ownership.
The same concept of model calibration, which is basically a step-by-step calibration sequentially through all model phases still applies to tour based models. You can’t expect a good auto ownership pattern (or activity generation pattern) if your synthesized household table is all wrong.
Just because something looks good regionally does NOT mean it looks good locally. Ideally, calibrating model steps should be done at sub-county levels, perhaps by area type within counties or sub-county districts.
And of course, make sure you have the data BEFORE you submit the abstract.

## Slide 14: Questions?
Andrew Rohne
OKI Regional Council
arohne@oki.org
@okiandrew
(513) 621-6300
Vince Bernardin
Bernardin, Lochmuller
& Associates
vbernardin2@bla.com
(812) 479-6200
Acknowledgements
Thanks to Rebekah Anderson (Ohio DOT) and Zhuojun Jiang (MORPC) for answering lots and lots and lots of questions from me about data, and for providing me with test data, documentation, and everything else I needed to run MORPC’s model.