## Slide 1: Evaluating and Communicating Model Results: Guidebook for Planners
13th TRB National Transportation Planning Applications Conference
May 11, 2010
Dan Goldfarb, P.E.
NCHRP Project 08-36, Task 89

## Slide 2: Background
AASHTO Requested
NCHRP Funded
Contributors
  Dalia Leven, AICP
  Rob Schiffer, AICP
  Jay Evans, P.E., AICP
Project Manager
  Lori Sundstrom, NCHRP Senior Program Officer

## Slide 3: Why?
Evolving Roles of Travel Demand Forecasting Models
Stakeholder Involvement
Audience
Guidebook Objectives
  Clear and concise
  What questions to ask
  Reasonableness and sensitivity
  Communicating results

## Slide 4: What’s Missing?
FHWA
  Introduction to Travel Demand Forecasting Self Instructional CD-ROM (TMIP)
  Introduction to Urban Travel Demand Forecasting (NHI)
  Travel Demand Forecasting: A Compilation of Plans, Reports, and Data (BTS)
State
  Florida Standard Urban Transportation Model Structure Online Training
MPO
  PSRC – Transportation 2040 Guide
Non-Governmental Organizations (NGOs)
  Inside the Black Blackbox: Making Transportation Models Work for Livable Communities (EDF)

## Slide 5: Why?
Evolving Roles of Travel Demand Forecasting Models
Stakeholder Involvement
Audience
Guidebook Objectives
  Clear and concise
  What questions to ask
  Reasonableness and sensitivity
  Communicating results
  Informative
  Unbiased

## Slide 6: Approach

## Slide 7: Organization
Overview
Role
Process
Dissect
Applications
Results

## Slide 8: Chapter 1 - Introduction
Purpose
Audience
Organization

## Slide 9: Chapter 2 - Role of TDF Model
Definition of TDF Model
Model Uses
Model Classifications
Model Limitations
Basic Terminology

## Slide 10: Chapter 2 (continued)
Long Term
Short Term
Time Frame
Travel Demand
Forecasting Model
Growth Trends
Tool
Regional
Corridor
Subarea
Site

## Slide 11: Chapter 2 (continued)
Terms
  Links & Nodes
  TAZ
  Centroid Connector
  Trip
  Trip Ends
  Trip Table
Glossary

## Slide 12: Chapter 3 - TDF Model Process
TDF Model Structures
Current Practice
Model Development Process

## Slide 13: Chapter 3 (continued)
 | Trip-End-Based | Tour-Based | Activity-Based
Accommodates latent demand based on changes in the transportation system |  |  | X
Accounts for complex intrahousehold travel interactions (limited vehicle availability, etc.) |  |  | X
Accounts for complex travel patterns and trip chains |  | X | X
Accounts for home end of trips | X | X | X
Advanced time-of-day analysis |  | X | X
Allows for more disaggregate data inputs and analysis |  |  | X
Analysis of nonmotorized trips | X | X | X
Ease of data collection | X |  | 
Minimizing computational resources | X |  | 

## Slide 14: Chapter 3 (continued)
Calibration
Validation
Application
Reasonableness Checking
Estimation
Model Development Process

## Slide 15: Chapter 4 - Sequential Travel Demand Forecasting
TDF Model Inputs
Trip Generation
Trip Distribution
Mode Choice
Assignment

## Slide 16: Chapter 4 (continued)

## Slide 17: Chapter 4 (continued)

## Slide 18: Chapter 5 - Applications of TDF Models
Historical Applications
Current Applications
Evolving Applications

## Slide 19: Chapter 6 - TDF Model Results
Interpretation
Communicating

## Slide 20: Chapter 6 (continued)

## Slide 21: Chapter 7 - Reasonableness and Sensitivity
Reasonableness Checks
Sensitivity Tests
Additional Resources

## Slide 22: Chapter 7 (continued)
Sources of Error
  Coding Errors – Errors in coding the highway and transit networks, and errors in recording survey results.
  Sample Errors – Errors from bias that occur in the survey sample frame. An example is a telephone survey where only land lines are reached for the survey calls. This would miss households without land lines, potentially resulting in a demographic bias in the observed travel patterns (i.e., missing low income housheholds with no phone, young or very active persons with cell phones only, etc.).
  Computation Errors – Errors which occur in developing the model programs.
  Specification Errors – Errors from improper structure of the model where key variables or parameters are overlooked in the estimation phase. Errors from transferring model parameters from one region to another.
  Data Errors – Error in underlying model data or through aggregation of data where key elements are overlooked.

## Slide 23: Chapter 7 (continued)
City | Transit | Carpool | Drive Alone
Dallas, Texas | 4% | 15% | 81%
Pasadena, California | 5% | 16% | 79%
Houston, Texas | 5% | 15% | 80%
Atlanta, Georgia | 10% | 14% | 76%
Baltimore, Maryland | 14% | 14% | 72%
Oakland, California | 15% | 15% | 70%
Pittsburgh, Pennsylvania | 20% | 13% | 68%
Boston, Massachusetts | 40% | 10% | 50%
San Francisco, California | 41% | 16% | 43%
New York City, New York | 61% | 9% | 30%

## Slide 24: Chapter 7 (continued)
Average Wednesday Freeway Traffic by Month | Average | % of AADT
January | 87,580 | 89.28
February | 95,187 | 97.03
March | 100,925 | 102.88
April | 101,038 | 103.00
May | 100,278 | 104.84
June | 104,857 | 106.89
July | 107,144 | 109.22
August | 106,330 | 108.39
September | 100,586 | 102.54
October | 100,117 | 102.06
November | 101,430 | 103.40
December | 99,496 | 101.43

## Slide 25: Chapter 7 (continued)
Chart: Percent Decrease in Time
| 2.0000000000000011E-2 | 4.0000000000000022E-2 | 6.0000000000000032E-2 | 8.0000000000000043E-2 | 0.1 | 0.12000000000000002 | 0.14000000000000001 | 0.16000000000000006 | 0.18000000000000016 | 0.20000000000000004 | 0.22000000000000006 | 0.24000000000000013 | 0.26 | 0.28000000000000008 | 0.30000000000000032
Combined Wait Time | 0.0103 | 0.0206 | 0.0309 | 0.0412 | 0.0515 | 0.0618 | 0.0721 | 0.0824 | 0.0927 | 0.103 | 0.1133 | 0.1236 | 0.1339 | 0.1442 | 0.1545
Transfer Wait Time | 0.00536 | 0.01072 | 0.01608 | 0.02144 | 0.0268 | 0.03216 | 0.03752 | 0.04288 | 0.04824 | 0.0536 | 0.05896 | 0.06432 | 0.06968 | 0.07504 | 0.0804
Initial Wait Time | 0.00494 | 0.00988 | 0.01482 | 0.01976 | 0.0247 | 0.02964 | 0.03458 | 0.03952 | 0.04446 | 0.0494 | 0.05434 | 0.05928 | 0.06422 | 0.06916 | 0.0741
Elasticity for Wait Time to Mode Share

## Slide 26
http://apps.trb.org/cmsfeed/TRBNetProjectDisplay.asp?ProjectID=2636

## Slide 27
http://apps.trb.org/cmsfeed/TRBNetProjectDisplay.asp?ProjectID=2636