## Slide 1: Validation and Sensitivity Considerations For Statewide Models
NCHRP 836-B Task 91
13th TRB National Transportation Planning Applications Conference
January 25, 2011
Robert G. Schiffer, AICP, Principal

## Slide 2: Statewide Model Validation and Sensitivity Presentation Outline
Introduction/Background
Market Segments Found in Statewide Models
Model Validation and Reasonableness Checking
Modal Issues
Statewide Freight Models
Summary and Conclusions

## Slide 3: Statewide Model Validation and Sensitivity Introduction/Background
Prior studies
  NCHRP Synthesis 358
Rationale for statewide models
  Intercity travel/corridors
  Rural travel demand
  MPO external trips
  Freight trips
Common applications for statewide models
Source: A. Horowitz, Statewide Travel Forecasting Models, NCHRP Synthesis 358 (2006), with recent updates.
Operational (28)
Dormant (3)
No model (11)
Developing (8)
Neither Alaska nor Hawaii have statewide models at present

## Slide 4: Statewide Model Validation and Sensitivity Market Segments Found in Statewide Models
Segmenting trips
Trip purposes
Travel periods
Transportation modes
Freight simulation
 | Statewide Model (Where Trip Purpose Information Was Available) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Trip Purpose | AL | AZ | CA | CT | DEa | FL 2000 | IN | KY | LA | MA | MS | NH | NJb | OH | OR | RI | TN | TX | UT | VA | VT
Home-Based Work | ● | ● |  | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● |  | ● | ● | ● | ● | ● | ●
Home-Based Other/Nonwork | ● | ● |  |  | ● | ● | ● |  | ● | ● | ● | ● | ● |  | ● | ● | ● | ● | ● | ● | ●
Home-Based Shop/Regional Shop |  |  |  |  | ● | ● |  |  |  | ● |  | ● | ● | ● |  |  |  |  |  |  | ●
Home-Based Regional Shop |  |  |  |  | ● |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Home-Based Social/Recreation |  |  |  |  | ● | ● |  |  |  | ● |  | ● |  | ● |  |  |  |  |  |  | 
Home-Based School |  |  |  |  |  |  |  |  |  | ● |  | ● | ● | ● |  |  |  |  |  |  | ●
Chauffeuring |  |  |  |  |  |  |  |  |  |  |  | ● |  |  |  |  |  |  |  |  | 
Nonhome-Based | ● | ● |  | ● |  | ● | ● |  | ● |  | ● |  |  |  |  | ● | ● | ● | ● | ● | ●
Nonhome-Based Work |  |  |  | ● | ● |  |  |  |  | ● |  |  | ● |  | ● |  |  |  |  |  | 
Nonhome-Based Other |  |  |  |  | ● |  |  |  |  | ● |  |  | ● |  | ● |  |  |  |  |  | 
Short-Distance Business |  |  | ● |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Short-Distance Commute |  |  | ● |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Short-Distance Recreation |  |  | ● |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Other Personc |  |  |  |  |  |  |  | ● |  |  |  |  |  |  |  |  |  |  |  |  | 
Commute Low, Medium, High |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ● |  |  |  |  |  | 
Continued on next slide…
Trip Purposes by Statewide Model

## Slide 5: Statewide Model Validation and Sensitivity Market Segments Found in Statewide Models
 | Statewide Model (Where Trip Purpose Information Was Available) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Trip Purpose | AL | AZ | CA | CT | DEa | FL 2000 | IN | KY | LA | MA | MS | NH | NJb | OH | OR | RI | TN | TX | UT | VA | VT
Other |  |  | ● |  |  |  |  |  |  |  |  |  |  | ● |  |  |  | ● |  |  | 
Long-Distance |  | ● |  |  |  |  | ● |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Long-Distance Business |  |  | ● |  |  | ● |  |  | ● |  | ● |  |  |  |  |  |  |  |  | ● | 
Long-Distance Commute |  |  | ● |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Long-Distance Personal Business |  |  |  |  |  |  |  |  |  |  | ● |  |  |  |  |  |  |  |  | ● | 
Long-Distance Recreation |  |  | ● |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Long-Distance Tourist |  |  |  |  |  |  |  | ● | ● |  | ● |  |  |  |  |  |  |  |  | ● | 
Long-Distance Work |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ● | ● |  | 
Long-Distance Nonwork/Other |  |  | ● |  |  |  |  |  | ● |  |  |  |  |  |  |  |  | ● | ● |  | 
Truck | ● |  |  |  |  |  |  | ● | ● |  |  |  |  |  |  |  |  |  |  |  | ●
Light Truck |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ● |  |  |  |  |  | 
Heavy Truck |  |  |  |  |  |  |  |  |  |  |  |  | ● |  | ● |  |  |  |  |  | 
Commercial |  |  |  |  |  |  |  |  |  |  |  |  | ● |  |  |  |  |  |  |  | 
Container |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ● |  |  |  |  |  | 
Single-Unit Truck |  | ● |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Multi-Unit Truck |  | ● |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
External-External | ● |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Internal-External | ● |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Internal-External Business |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ● |  | 
Internal-External Other |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ● |  | 
Internal-External Short-Distance |  |  |  |  |  | ● |  |  |  |  |  |  |  |  |  |  |  | ● |  |  | 
Internal-External Long-Distance |  |  |  |  |  |  |  | ● |  |  |  |  |  |  |  |  |  | ● |  |  | 
… Continued
a Based on CADSR Transportation Survey (1995 to 2002).
b Also includes 16 recreational trip purposes (HBCasino Access, NHBCasino Visit, Casino Bus, HBEvent, HBBeach Access, HBBeach, HBBoardwalk, HBShop, HBDine, HBO, NHBEvent, NHBBeach, NHBBoardwalk, NHBShop, NHBDine, and NHBO).
c Other Person (a combination of NHB and HBO).
d The Florida Turnpike, Georgia, and Tennessee Models use origin-destination matrix estimation (ODME) to generate trips and therefore do not include trips by purpose.
Trip Purposes by Statewide Model

## Slide 6: Statewide Model Validation and Sensitivity Model Validation and Reasonableness Checking
Data Sources
Model Validation Techniques
Structural Metrics
Reasonableness Checks
Relationships between Urban and Statewide Models
Model Forecasting and Sensitivity Testing
 | AL | AZ | CA | FL | TN | TX | UT | WI
Highway Performance Monitoring System (HPMS) |  | ● |  |  |  |  |  | ●
American Travel Survey (ATS) |  |  | ● |  |  |  |  | ●
Census Transportation Planning Package (CTPP) |  |  | ● |  |  |  | ● | ●
State Data Sources | ● |  | ● |  | ● | ● |  | ●
National Household Travel Survey (NHTS) |  |  |  | ● |  |  | ● | ●
Freight Analysis Framework (FAF) |  |  |  |  | ● |  |  | 
Reebie/TRANSEARCH |  |  |  |  | ● | ● |  | ●
Study
Area
Urban
Model
Area
Study
Area
Urban
Model
Area 1
Study Area
Within One
Model Area
Urban
Model
Area 2
Study Areas
Within Two
Model Areas
Study
Area
Urban
Model
Area
Study
Area
Statewide Model
Study Area
Outside Urban
Model Areas
Statewide Model
Statewide Model
Data Used for Model Validation

## Slide 7: Statewide Model Validation and Sensitivity Model Validation and Reasonableness Checking
Reasonableness Checks
  Trip Generation
  Trip Distribution
  Auto Occupancy
  Trip Assignment
 | AL | AZ | CA | FL | IN | LA | MS | OH | TN | TX | WI
Trip Generation |  |  |  |  |  |  |  |  |  |  | 
Aggregate Trip Rates |  |  |  | ● |  |  |  |  |  |  | ●
Trips by Purpose |  |  |  | ● |  |  |  |  |  | ● | ●
Trip Distribution |  |  |  |  |  |  |  |  |  |  | 
Travel Time |  | ● |  |  |  |  |  |  |  |  | ●
Average Trip Lengths |  |  |  | ● |  |  |  |  |  | ● | ●
Mode Choice |  |  |  |  |  |  |  |  |  |  | 
Auto Occupancy |  |  | ● | ● |  | ● | ● |  |  | ● | 
Mode Share |  |  | ● |  |  |  |  |  |  |  | 
Traffic Assignment |  |  |  |  |  |  |  |  |  |  | 
Area Type (Volume-Over-Count) |  | ● | ● | ● | ● |  |  |  | ● | ● | 
Corridor (Volume-Over-Count) |  |  |  |  | ● |  |  | ● |  |  | 
District/Region (Volume-Over-Count) |  |  | ● | ● |  | ● | ● |  | ● | ● | ●
Facility Type (Volume-Over-Count) | ● | ● | ● | ● | ● | ● | ● |  | ● | ● | ●
Intercity Transit Ridership |  |  |  |  |  |  |  |  |  |  | ●
GEH |  |  |  |  |  |  |  |  |  |  | ●
Long-Distance Trips by Purpose |  |  |  |  |  |  |  |  |  |  | ●
RMSE by Volume Group |  | ● |  | ● | ● |  |  | ● | ● |  | ●
R-squared |  | ● |  |  |  |  |  |  |  |  | 
Screenline (Volume-Over-Count) |  | ● |  | ● | ● | ● | ● | ● | ● | ● | ●
Tonnage/Commodity Flows |  |  |  | ● |  |  |  |  |  | ● | ●
Total Volume |  |  |  | ● |  |  |  |  |  |  | ●
Truck (Volume-Over-Count) |  |  |  | ● |  |  |  |  |  |  | ●
VHT (Volume-Over-Count) |  |  |  | ● |  |  |  |  |  |  | 
VMT (Volume-Over-Count) |  | ● |  | ● | ● | ● | ● | ● | ● | ● | ●
Volume Group (Volume-Over-Count) | ● |  |  | ● | ● |  |  | ● | ● |  | ●
Statewide Model Validation Criteria by model Step

## Slide 8: Statewide Model Validation and Sensitivity Model Validation and Reasonableness Checking
Trip Generation
  Aggregate trip rates varied widely…
  Conversely, percent trips by purpose are in similar ranges among statewide models
 | Statewide Model Results |  |  |  |  |  | Guidance Documents |  |  | 
 | CAd | FL 2000 | MA | UT | VA | WI | FDOT |  | NCHRP | 
 |  |  |  |  |  |  | Lowa | Higha | Lowb | Highb
Person Trips/TAZ | – | 13,026 | 7,489 | 2,134 | 16,197 | 12,788 | – | 15,000 | – | –
Person Trips/Person | 1.95 | 3.26 | 3.62 | 3.08 | 3.62 | 4.25 | 3.3 | 4 | – | –
Person Trips/Household (DU)c | 5.41 | 8.21 | 9.4 | 8.94 | 9.5 | 10.33 | 8 | 10 | 6.8 | 12.4
HBW Person Trips/Household | – | – | 1.73 | 1.38 | 1.38 | 1.73 | – | – | – | –
Person Trips/Employee | 4.41 | 7.38 | 7.26 | 6.54 | 7.23 | 8.76 | – | – | 1.29 | 1.4
Aggregate Trip Rates for Statewide Models
a As documented by Cambridge Systematics, Inc. in 2008 Model Calibration and Validation Standards Final Report for Florida DOT, results from models throughout the U.S. (see Bibliography for all document titles).
b 1998 NCHRP Report 365 Travel Estimation Techniques for Urban Planning, trips/HH.
c Reported statistics are for motorized trips only.
d California High-Speed Rail Model, figures based on intraregional trips.

## Slide 9: Statewide Model Validation and Sensitivity Model Validation and Reasonableness Checking
Trip Purpose | Statewide Model Results |  |  |  |  |  |  |  | Travel Survey Data |  |  |  | Guidance Documents |  |  | 
 | AL | FL 2000 | LA | MA | MS | UT | VT | DE | Wisconsin |  | NHTS |  | FDOT |  | NCHRP | 
 |  |  |  |  |  |  |  |  | Short-Distanceb | Long-Distanceb | Urbanc | Ruralc | Lowd | Highd | Lowe | Highe
Home-Based Work | 19.19% | 19.14% | 19.00% | 18.41% | 16.06% | 15.50% | 23.30% | 34.00% | 18.04% | – | 11.15% | 11.36% | 12.00% | 24.00% | 17.00% | 23.00%
Home-Based Nonwork | 46.22% | 55.47% | 47.70% | 52.06% | 49.17% | 45.10% | – | – | – | – | – | – | 45.00% | 60.00% | – | –
Home-Based Other | – | 27.92% | 47.70% | 19.38% | 49.17% | 45.10% | 32.20% | 18.00% | 9.47% | – | 21.52% | 21.73% | 14.00% | 28.00% | 52.00% | 60.00%
Home-Based Shop | – | 15.76% | – | 11.73% | – | – | 12.80% | 17.00% | 15.26% | – | 22.94% | 20.40% | 10.00% | 20.00% | – | –
Home-Based Social/Recreation | – | 11.79% | – | 13.95% | – | – | – | 10.00% | 11.91% | – | 13.78% | 12.87% | 9.00% | 12.00% | – | –
Home-Based School | – | – | – | 7.00% | – | – | 5.80% | – | 19.03% | – | – | – | 5.00% | 8.00% | – | –
Nonhome-Based | – |  |  |  |  |  | 25.80% | – | – | – | – | – | – | – | – | –
Nonhome-Based Work | – | – | – | 10.27% | – | – | – | 11.00% | – | – | – | – | – | – | – | –
Nonhome-Based Nonwork | – | – | – | 14.41% | – | – | – | 6.00% | – | – | – | – | – | – | – | –
Other | 21.80% | – | – | – | – | – | – | – | – | – | – | – | – | – | – | –
Truck | 7.79% | – | 1.70% | – | – | – | – | – | – | – | – | – | – | – | – | –
Long-Distance Business | – | – | 0.20% | 2.84% | 0.11% | – | – | – | – | 24.80% | – | – | – | – | – | –
Long-Distance Tourist | – | – | 0.10% | 0.27% | 0.00% | – | – | – | – | – | – | – | – | – | – | –
Long-Distance Work | – | – | – | 1.05% | – | 0.30% | – | – | – | – | – | – | – | – | – | –
Long-Distance Nonwork/Other | – | – | 0.30% | – | 0.11% | 0.60% | – | – | – | – | – | – | – | – | – | –
Internal-External Business | – | – | – | – | 0.44% | – | – | – | – | – | – | – | – | – | – | –
Internal-External Tourist | – | – | – | – | 0.44% | – | – | – | – | – | – | – | – | – | – | –
Internal-External Other | – | – | – | – | 0.77% | – | – | – | – | – | – | – | – | – | – | –
External | 0.75% | – | – | 0.67% | – | – | – | – | – | – | – | – | – | – | – | –
Trip Purpose by Percentage Found in Statewide Modelsa
a Percentages based on proportion of total trips.
b Wisconsin short- and long-distance trips from the 2001 NHTS Add-On.
c As calculated from 2001 NHTS data (full national sample) by Cambridge Systematics, Inc. and documented in 2006 Model Parameters Final Report for the Florida DOT (see Bibliography for all document titles).
d As documented by Cambridge Systematics, Inc. in 2008 Model Calibration and Validation Standards Final Report for the Florida DOT, results from models throughout the U.S.
e NCHRP Report 365 Travel Estimation Techniques for Urban Planning.

## Slide 10: Statewide Model Validation and Sensitivity Model Validation and Reasonableness Checking
Trip Distribution
  Average trip lengths for typical urban model purposes (HBW, HBO, NHB) are similar to those reported in regional models,
  while long-distance trip purposes show uniformly longer average trip lengths

## Slide 11: Statewide Model Validation and Sensitivity Model Validation and Reasonableness Checking
 | Statewide Model Results |  |  |  |  |  |  |  |  | Travel Survey Data |  |  |  |  |  | Guidance Documents |  |  | 
Trip Purpose | FL 2000 | LA | MA | OHd | RI | TX | UT | VA | VT | IN | LA | MA | VA | UT | NHTSa | FDOT |  | NCHRP | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Lowb | Highb | Lowc | Highc
Home-Based Work | 18.38 | 17.3 | 23.05 | 11 | 21.59 | 16 | 17.79 | 14.6 | 21.97 | 20.11 | – | 24.14 | 16.40 | 18.20 | 24.46 | 12.00 | 35.00 | 11.20 | 35.40
Home-Based Other/Nonwork | 16.22 | 12.2 | 14.57 |  | 15.64 | 9.06 | 12.98 | 10.8 | 18.56 | 14.56 | – | 14.56 | 15.70 | 13.90 | 16.12 | 8.00 | 20.00 | 10.40 | 17.30
Home-Based Shop | 16.77 | – | 15.06 | 8.2 | – | – | – | – | 20.78 | – | – | 14.64 | – | – | 24.22 | 9.00 | 19.00 | 8.60 | 18.70
Home-Based Social/Recreation | 15.55 | – | 16.19 | 8.2 | – | – | – | – | – | – | – | 16.70 | – | – | 18.35 | 11.00 | 19.00 | – | –
Home-Based School | – | – | 13.93 |  | – | – | – | – | 19.24 | – | – | 13.59 | – | – | – | 7.00 | 16.00 | 8.90 | 15.90
Nonhome-Based | 13.06 | 9.3 | – |  | 14.45 | 9.68 | 12.37 | 23.17 | 14.49 | 14.41 | – | – | 22.50 | 13.40 | 19.86 | 6.00 | 19.00 | 8.10 | 17.10
Nonhome-Based Work | – | – | 17.91 |  | – | – | – | – | – | – | – | 17.44 | – | – | – | – | – | – | –
Nonhome-Based Other | – | – | 15.62 |  | – | – | – | – | – | – | – | 15.20 | – | – | – | – | – | – | –
Other | – | – | – | 7.1 | – | 10.83 | – | – | – | – | – | – | – | – | – | – | – | – | –
Long-Distance Business | 134.67 | 166 | – |  | – | – | – | 127.13 | – | – | 165.00 | – | – | – | – | – | – | – | –
Long-Distance Personal Business | – | – | – |  | – | – | – | 124.58 | – | – | – | – | – | – | – | – | – | – | –
Long-Distance Tourist | – | 172 | – |  | – | – | – | 126.67 | – | – | 192.00 | – | – | – | – | – | – | – | –
Long-Distance Work | – | – | – |  | – | 200.82 | 89.54 | – | – | – | – | – | – | – | – | – | – | – | –
Long-Distance Nonwork/Other | – | 164 | – |  | – | 199.71 | 81.73 | – | – | – | 168.00 | – | – | – | – | – | – | – | –
Internal-External Business | – | – | – |  | – | – | 51.26 | – | – | – | – | – | – | – | – | – | – | – | –
Internal-External Other | – | – | – |  | – | – | 55.49 | – | – | – | – | – | – | – | – | – | – | – | –
Internal-External Short-Distance | 42.82 | – | – |  | – | 30 | – | – | – | – | – | – | – | – | – | – | – | – | –
Internal-External Long-Distance | – | – | – |  | – | 125.75 | – | – | – | – | – | – | – | – | – | – | – | – | –
Average Trip Lengths Found in Statewide Models
Trip Lengths in Minutes
a As calculated from 2001 NHTS data (full national sample) by Cambridge Systematics, Inc. and documented in 2006 Model Parameters Final Report for the Florida DOT.
b As documented by Cambridge Systematics, Inc. in 2008 Model Calibration and Validation Standards Final Report for the Florida DOT, results from models throughout the U.S. (see Bibliography for all document titles).
c NCHRP Report 365 Travel Estimation Techniques for Urban Planning.
d Ohio data is in miles, not minutes.

## Slide 12: Statewide Model Validation and Sensitivity Model Validation and Reasonableness Checking
Auto Occupancy
  Auto occupancy statistics are readily available for statewide models
  Tend to run higher in SWMs than urban and regional models
  since longer distance trips generally involve either family members or business colleagues traveling together

## Slide 13: Statewide Model Validation and Sensitivity Model Validation and Reasonableness Checking
Trip Purpose | Statewide Model Results |  |  |  |  |  |  |  | Survey Data | Guidance Documents |  |  | 
 | CA | FL 2000 | KY | LA | MS | RI | TX | UT | NHTSa | FDOT |  | NCHRP | 
 |  |  |  |  |  |  |  |  |  | Lowb | Highb | Lowc | Highc
Home-Based Work | 1.19 | 1.1 | – | 1.15 | 1.1 | 1.12 | – | – | 1.10 | 1.05 | 1.10 | 1.11 | 1.13
Home-Based Nonwork | – | – | – | – | – | – | – | – | – | – | – | – | –
Home-Based Other | 1.54 | 1.7 | – | 1.78 | 1.65 | 1.56 | – | – | 1.70 | 1.65 | 1.95 | 1.65 | 1.67
Home-Based Shop | – | 1.8 | – | – | – | – | – | – | 1.80 | 1.50 | 1.80 | 1.44 | 1.48
Home-Based Social/ Recreation | 1.49 | 1.94 | – | – | – | – | – | – | 1.94 | 1.70 | 1.90 | 1.66 | 1.72
Nonhome-Based | – | 1.71 | – | 1.79 | 1.56 | 1.56 | – | – | 1.71 | 1.60 | 1.90 | 1.64 | 1.68
Work | – | – | – | – | – | – | 1.33 | – | – | – | – | – | –
Nonwork | – | – | – | – | – | – | 2.06 | – | – | – | – | – | –
Long-Distance Business | 1.19 | – | 1.8 | 1.86 | 1.39 | – | – | 1.82 | – | – | – | – | –
Long-Distance Tourist | – | – | 3.31 | 3.44 | 2.55 | – | – | 2.69 | – | – | – | – | –
Long-Distance Work | – | – | 2.43 | – | – | – | – | – | – | – | – | – | –
Long-Distance Recreation | 1.73 | – | – | – | – | – | – | – | – | – | – | – | –
Long-Distance Nonwork/ Other | 1.31 | – | – | 2.64 | 2.05 | – | – | 2.69 | – | – | – | – | –
Internal-External Business | – | – | – | – | 1.5 | – | – | – | – | – | – | – | –
Internal-External Tourist | – | – | – | – | 2.55 | – | – | – | – | – | – | – | –
Internal-External Other | – | – | – | – | 2.26 | – | – | – | – | – | – | – | –
Average Auto Occupancy Found in Statewide Models
a As calculated from 2001 NHTS data (full national sample) by Cambridge Systematics, Inc. and documented in 2006 Model Parameters Final Report for the Florida DOT.
b As documented by Cambridge Systematics, Inc. in 2008 Model Calibration and Validation Standards Final Report for the Florida DOT, results from models throughout the U.S. (see Bibliography for all document titles).
c NCHRP Report 365 Travel Estimation Techniques for Urban Planning.

## Slide 14: Statewide Model Validation and Sensitivity Model Validation and Reasonableness Checking
Trip Assignment
  Traffic assignment RMSE for statewide models tends to track at higher levels than urban and regional models due to lower link volumes, larger zones, and relatively sparse networks
Range | Statewide Model Results |  |  |  |  |  |  |  |  |  |  |  | Guidance Documents |  |  | 
 | AL | AZ | FL 2000 | IN | MD | MI | OH | OR | TN | TX | UT | WI | FDOT |  | Oregon DOTb | Michiganc
 |  |  |  |  |  |  |  |  |  |  |  |  | Acceptablea | Preferablea |  | 
1 to 5,000 | 141.8 | 103.6 | 60.9 | 42.29-99.06 | – | 35.33 | 115-58 | 100.33 | 27.2-21.8 | 90-290 | 57-147 | 41.82-80.61 | 100 | 45 | 115.76 | 50- 200%
5,000 to10,000 | 80.7 | 56.9 | 43.4 | 35.52-42.97 | 114 | 22 | 55-42 | 32 | 15.9 | 70 | 53-76 | 32 | 45 | 35 | 43.14 | 25%
10,000 to 20,000 | 65.5-82.4 | 36.7 | 32.7 | 31.33-35.6 | 86 | – | 36-24 | – | 25.4-35.5 | 61.0d | 34.0-81.0 | 22.3 | 30.0- 35.0 | 25.0- 27.0 | 28.73 | 20%
20,000 to 30,000 | 57.1 | 27.5 | 25.9 | 29.34 | 45 | 20.3 | 25-28 | – | 20.2 | 40.0d | 45 | 19.33 | 27 | 15 | 25.84 | 20%
30,000 to 40,000 | 36.2e | – | 21.4 | 21.93 | 49 | – | 23 | 31 | 18.2 | 40.0d | 36 | 13.62 | 25 | 15 | 30.25 | 15%
40,000 to 50,000 | – | – | 17.4 | 15.74 | 12 | 16.4 | – | – | 8.8 | – | 36 | 13.91 | 25 | 15 | 30.25 | 15%
50,000 to 60,000 | – | – | 14.5 | – | 37 | 13.9 | 17 | – | 5.1f | – | – | – | 20 | 10 | 30.25 | 10%
> 60,000 | – | – | 10.9-14.9 | 13.22-14.6 | 23.5 | – | 11 | – | – | – | 41 | – | 19 | 10 | 19.2 | 10%
Total | 82.2 | 56 | 32.6 | 39.42 | – | – | 35 | – | – | 90 | 49 | 39.21 | 45 | 35 |  | 
a As documented by Cambridge Systematics, Inc. in 2008 Model Calibration and Validation Standards Final Report for the Florida DOT, results from models throughout the U.S. (see Bibliography for all document titles).
b As documented in 1995 Travel Demand Model Development and Application Guidelines for Oregon DOT.
c Percent Deviation from Counts – Michigan DOT Urban Model Calibration Targets, 1993. 10,000 to 25,000 and 25,000+ ranges used in Texas model reference.
e 25,000+ range used in Alabama model reference.
f 50,000+ range used in Tennessee model reference.
RMSE Statistics from Statewide Models

## Slide 15: Statewide Model Validation and Sensitivity Model Validation and Reasonableness Checking
Chart: Midpoint Volume Range
| 2500 | 7500 | 15000 | 25000 | 35000 | 45000 | 55000 | 65000
AL | 141.8 | 80.7 | 73.95 | 57.1 | 36.2
AZ | 103.6 | 56.9 | 36.7 | 27.5
FL | 60.9 | 43.4 | 32.7 | 25.9 | 21.4 | 17.4 | 14.5 | 12.9
IN | 70.675 | 39.245 | 33.465 | 29.34 | 21.93 | 15.74 | 13.91
MD | 114 | 86 | 45 | 49 | 12 | 37 | 23.5
MI | 35.3333 | 22 | 20.3 | 16.4 | 13.9
OH | 81.6 | 47.3333 | 31 | 30 | 22 | 15
OR | 100.3333 | 32 | 31
TN | 24.5 | 15.9 | 30.45 | 20.2 | 18.2 | 8.8 | 5.1
TX | 190 | 70 | 61 | 40 | 40
UT | 102 | 64.5 | 57.5 | 45 | 36 | 36 | 41
WI | 61.215 | 32 | 22.3 | 19.33 | 13.62 | 13.91

## Slide 16: Statewide Model Validation and Sensitivity Model Validation and Reasonableness Checking
Facility Type | Statewide Model Results |  |  |  |  |  |  |  | Guidance Documents |  |  |  |  | 
 | AL | FL 2000 | MA | MI | OH | TX | VT | WI | Ratios from Urban/ Regional Modelsa |  | FDOT |  | Michigan DOT (+/-)b | FHWA (+/-)c
 |  |  |  |  |  |  |  |  | Low | High | Acceptable (+/-)a | Preferable (+/-)a |  | 
Interstate | – | – | – | 1.00 | – | 0.84 | 0.98 | 0.94 | – | – | 7.00% | 6.00% | 6.00% | 7.00%
Freeway | 1.01 | 0.98 | 1.01 | – | 0.96 | – | – | 1.08 | 0.86 | 1.15 |  |  |  | 
Expressway | – | – | – | – | – | – | – | 1.05 |  |  |  |  |  | 
U.S. Highway | – | – | – | – | – | 1.03 | – | – | – | – | 15.00% | 10.00% | – | 10.00%
State Highway | – | – | – | – | – | 0.55 | – | – | – | – |  |  | – | 
Arterials | – | – | 0.97 | – | – | – | – | – | – | – |  |  | – | 
Principal Arterial | 1.05 | – | – | – | – | – | 1.02 | 0.99 | 0.89 | 1.06 |  |  | 7.00% | 
Major Arterial | – | 1.01 | – | 0.99 | 0.9 | – | – | – | – | – |  |  | – | 
Minor Arterial | 0.94 | 1.03 | – | 1.03 | 1.09 | – | 0.95 | 1.06 | 0.77 | 1.07 |  |  | 10.00% | 15.00%
Collector | 0.87 | 1.01 | 0.97 | – | 1.17 | – | 1.11 | – | 0.37 | 1.05 | 25.00% | 20.00% | 20.00% | 25.00%
Major Collector | – | – | – | 0.88 | – | – | 0.93 | – | – | – |  |  |  | 
Minor Collector | – | – | – | 0.95 | – | – | 1.02 | – | – | – |  |  |  | 
Percent Assignment Error for Statewide Models
a As documented by Cambridge Systematics, Inc. in 2008 Model Calibration and Validation Standards Final Report for the Florida DOT, results from models throughout the U.S. (see Bibliography for all document titles).
b Michigan DOT Urban Model Calibration Targets, 1993.
c 1997 FHWA Model Validation and Reasonableness Checking Manual (same accuracy standards referenced in several other documents as well). (In guidance documents, seven percent assign­ment error = volume-over-count ratio of 0.93 to 1.07.)

## Slide 17: Statewide Model Validation and Sensitivity Model Validation and Reasonableness Checking
Model Forecasting and Sensitivity Testing
  Statewide models require more comparative assessment than urban and regional models
    SWMs validated and updated less frequently than urban models
    Minimal involvement of MPOs and their knowledge base
  Three recommended comparative assessments
    Traffic count extrapolations
    Comparisons with other models
    Assess model sensitivity/elasticity
Elasticity =
VMT
LaneMiles

## Slide 18: Statewide Model Validation and Sensitivity Modal Issues
Modes Selected for Analysis
Mode Choice Approaches
Mode Choice Validation
Modes Considered in Statewide Models
Mode Split Reasonableness Comparisons
Modes | CA | DE | FL | GA | IN | IA | LA | MA | MS | NJ | NM | OH | OR | PA | RI | TX | VA | WI
Auto | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ●
Air | ● |  | ● |  |  |  |  |  |  |  |  | ● |  |  |  | ● | ● | ●
Bus (Generic) |  | ● |  |  |  |  |  |  |  |  |  |  | ● |  |  |  |  | 
Intercity Bus |  |  |  |  |  |  |  |  |  |  |  | ● |  |  |  |  |  | ●
Rail (Generic) | ● | ● | ● |  |  |  |  |  |  |  | ● | ● |  | ● |  | ● | ● | ●
High-Speed Rail | ● |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Intercity Rail |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ●
Amtrak |  |  |  |  |  |  |  |  |  |  |  | ● |  |  |  |  |  | 
Truck |  |  | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● |  |  |  | ● | ● | ●
Light-Truck |  |  | ● |  |  |  |  |  |  | ● |  |  | ● |  |  |  |  | 
Medium-Truck |  |  | ● |  |  |  |  |  |  | ● |  |  |  |  |  |  |  | 
Heavy-Truck |  |  | ● |  |  |  |  |  |  | ● |  |  | ● |  |  |  |  | 
102-Inch Truck |  |  |  |  |  |  |  |  |  | ● |  |  |  |  |  |  |  | 
Container Truck |  |  |  |  |  |  |  |  |  |  |  |  | ● |  |  |  |  | 
Commodity-Carrying |  |  |  | ● |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Noncommodity-Carrying |  |  |  | ● |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Commercial Vehicle |  |  |  |  |  |  |  | ● |  |  |  |  |  |  |  |  |  | 
Water |  |  |  |  |  |  |  |  |  |  |  | ● |  |  |  |  | ● | ●
Intermodal |  |  |  | ● |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Modes Simulated by State

## Slide 19: Statewide Model Validation and Sensitivity Statewide Freight Models
Validation approaches by freight model type
  Truck Models
  Direct Commodity Table Model
  Four-Step Freight Model
  Economic Model

## Slide 20: Statewide Model Validation and Sensitivity Statewide Freight Models
State Name | No Freight Model | Truck Model | Direct Commodity Table Model | Four-Step Freight Model | Economic Model
Alabama |  | ● |  |  | 
Alaska | ● |  |  |  | 
Arizona |  | ● |  |  | 
Arkansas | ● |  |  |  | 
California | ●b |  |  |  | 
Colorado | ●a |  |  |  | 
Connecticut |  | ● |  |  | 
Delaware |  | ● |  |  | 
Florida |  |  |  | ● | 
Georgia |  |  | ● |  | 
Hawaii | ● |  |  |  | 
Idaho | ●a |  |  |  | 
Illinois | ●a |  |  |  | 
Indiana |  |  |  | ● | 
Iowa |  | ● |  |  | 
Kansas | ●a |  |  |  | 
Kentucky |  |  | ● |  | 
Louisiana |  |  | ● |  | 
Maine |  | ● |  |  | 
Maryland |  | ● |  |  | 
Massachusetts |  | ● |  |  | 
Michigan |  |  |  | ● | 
Minnesota | ● |  |  |  | 
Mississippi |  |  | ● |  | 
Missouri |  | ● |  |  | 
State Name | No Freight Model | Truck Model | Direct Commodity Table Model | Four-Step Freight Model | Economic Model
Montana |  |  | ● |  | 
Nebraska |  | ● |  |  | 
Nevada | ● |  |  |  | 
New Hampshire |  | ● |  |  | 
New Jersey |  | ● |  |  | 
New Mexico |  |  | ● |  | 
New York | ● |  |  |  | 
North Carolina | ● |  |  |  | 
North Dakota | ● |  |  |  | 
Ohio |  |  |  | ● | 
Oklahoma | ● |  |  |  | 
Oregon |  |  |  |  | ●c
Pennsylvania |  |  |  | ●c | 
Rhode Island |  | ● |  |  | 
South Carolina | ●a |  |  |  | 
South Dakota | ● |  |  |  | 
Tennessee |  |  | ● |  | 
Texas |  |  |  | ● | 
Utah |  | ● |  |  | 
Vermont |  | ● |  |  | 
Virginia |  |  | ● |  | 
Washington | ● |  |  |  | 
West Virginia | ● |  |  |  | 
Wisconsin |  |  |  | ● | 
Wyoming | ● |  |  |  | 
a No information obtained.
b Travel Demand Model does not report truck volumes or performance.
c Includes the estimation of trips through intermediate distribution and warehouse centers.
Statewide Freight Models

## Slide 21: Statewide Model Validation and Sensitivity Statewide Freight Models
Data sources for freight model validation
  Commodity Flows – comparison against model flows
  Networks – correct entry points for external freight flows
  Truck Counts – by vehicle class; can’t separate freight trucks
  Categories of Outputs – classification of counts
  Inclusion of Nonfreight Trucks – not produced by freight model
  Distribution Centers/Logistics Centers – potential for mode shifts

## Slide 22: Statewide Model Validation and Sensitivity Statewide Freight Models
STCC | Commodity Type | Movement Type |  | 
 |  | Intrastate | Interstate | Through
01 | Farm Products | 16.1 | 16.1 | 16.1
09 | Fresh Fish or Marine Products | 12.6 | 12.6 | 12.6
10 | Metallic Ores | 11.5 | 11.5 | 11.5
11 | Coals | 16.1 | 16.1 | 16.1
14 | Nonmetallic Ores | 16.1 | 16.1 | 16.1
19 | Ordinance or Accessories | 3.1 | 3.1 | 3.1
20 | Food Products | 17.9 | 17.9 | 17.9
21 | Tobacco Products | 9.7 | 16.4 | 16.8
22 | Textile Mill Products | 15.2 | 16.1 | 16.5
23 | Apparel or Relented Products | 12.4 | 12.4 | 12.5
24 | Lumber or Wood Products | 21.1 | 21.0 | 21.1
25 | Furniture or Fixtures | 11.3 | 11.3 | 11.4
26 | Pulp, Paper, Allied Products | 18.6 | 18.5 | 18.6
27 | Printed Matter | 13.8 | 13.6 | 13.9
28 | Chemicals or Allied Products | 16.9 | 16.9 | 16.9
29 | Petroleum or Coal Products | 21.6 | 21.6 | 21.6
30 | Rubber or Miscellaneous Plastics | 9.1 | 9.2 | 9.3
31 | Leather or Leather Products | 10.8 | 11.0 | 11.3
32 | Clay, Concrete, Glass, or Stone | 14.4 | 14.3 | 14.4
33 | Primary Metal Products | 19.9 | 19.9 | 2.00
34 | Fabricated Metal Products | 14.3 | 14.3 | 14.3
35 | Machinery | 10.8 | 10.8 | 10.9
36 | Electrical Equipment | 12.7 | 12.8 | 12.9
37 | Transportation Equipment | 11.3 | 11.3 | 11.3
38 | Instruments, Photo Equipment, Optical Equipment | 9.4 | 9.4 | 9.7
39 | Miscellaneous Manufacturing Products | 14.2 | 14.4 | 14.8
40 | Waste or Scrap Metals | 16.0 | 16.0 | 16.0
50 | Secondary Traffic | 16.1 | 16.1 | 16.1
Virginia Freight Model Truck Load Factors
Tons per Truck

## Slide 23: Statewide Model Validation and Sensitivity Summary and Conclusions
Most statewide models solely validated through the reporting of traffic assignment statistics
Lack of reported validation statistics for trip generation, trip distribution, and mode choice might reflect a prior lack of comparative statistics from other statewide models
Lack of consistency in market sectors (trip purposes, etc.) also adds complexity to making comparisons across statewide models

## Slide 24: Statewide Model Validation and Sensitivity Summary and Conclusions
Variations in statewide model network and zone systems make it difficult to establish a typical range of ratios such as links or population per zone
Few states have conducted statewide household or intercept studies focused on model parameters and benchmarks for statewide model calibration and validation
Relatively little information is documented on sensitivity testing or the reasonableness of forecasts

## Slide 25: Statewide Model Validation and Sensitivity Summary and Conclusions
NCHRP Task 91 – List of Statewide Models Reviewed
Alabama (2005/2035)
Arizona (2005/2030/2050)
California (2000/2030)
Colorado (2000/2025)
Connecticut (2005/unknown)
Delaware (2003, 2005/2030)
Florida (2000/2030, 2005/2035)
Florida Turnpike Model (2004/2015)
Georgia (2001/2035)
Indiana (2000/2030)
Iowa (2000/2030)
Kentucky (1999/2030)
Louisiana (2000/2030)
Maryland (unknown)
Massachusetts (2000/unknown)
Michigan (unknown)
Mississippi (2000/2005-2030)
Missouri (unknown)
New Hampshire (2000/unknown)
New Jersey (unknown)
New Mexico (2005/2030)
Ohio (2000/2030)
Oregon (1990/2020)
Pennsylvania (2006/2030)
Rhode Island (2000/2030)
Tennessee (2003/2030)
Texas (1998/2025)
Utah (2005/2030)
Vermont (2000/2020/2030)
Virginia (2000/2025)
Wisconsin (2000/2030)
Model (Base Year/Future Year)

## Slide 26: Statewide Model Validation and Sensitivity Summary and Conclusions
ACKNOWLEDGMENTS
This study was requested by the American Association of State Highway and Transportation Officials (AASHTO), and conducted as part of the National Cooperative Highway Research Program (NCHRP) Project 08-36. The NCHRP is supported by annual voluntary contributions from the state departments of transportation. Project 08-36 is intended to fund quick response studies on behalf of the AASHTO Standing Committee on Planning. The report was prepared by a team led by Rob Schiffer of Cambridge Systematics, Inc. Significant contributors included Sarah McKinley, Dan Beagan, Tom Rossi, David Kurth, Dan Tempesta, and Ed Bromage of Cambridge Systematics. Wade White of the Whitehouse Group, Inc. led the section on Integrated Transportation and Land Use Modeling. The work was guided by a task group consisting of Charles E. Howard, Rick Donnelly, Brian J. Gregor, Phillip J. Mescher, Vidyadhara N. Mysore, Jeremy Raw, and Supin Yoder. The project was managed by Nanda Srinivasan, NCHRP Senior Program Officer.
DISCLAIMER
The opinions and conclusions expressed or implied are those of the research agency that performed the research and are not necessarily those of the Transportation Research Board or its sponsors. The information contained in this document was taken directly from the submission of the author(s). This document is not a report of the Transportation Research Board or of the National Research Council.
Note: The Transportation Research Board of the National Academies, the National Research Council, the Federal Highway Administration, the American Association of State Highway and Transportation Officials, and the individual states participating in the National Cooperative Highway Research Program do not endorse products or manufacturers. Trade or manufacturers’ names appear herein solely because they are considered essential to the object of this report.