## Slide 1: A Simple Methodology to Evaluate the Disproportionate Impacts of Fare and Service Changes on Protected Populations in a Fixed Guide-way System By Vijay Mahal HDR Engineering May 11, 2011 13th TRB Applications Conference Reno

## Slide 2: Presentation Purpose
Objectives:
Define the problem / Explain equity impacts
Review existing methods
Discuss HDR method
Present an example

## Slide 3: The Problem
Public transportation is
A public service
Most often uses Federal funds
Service and Fare changes impacts people
Are protected populations impacted disproportionately?
If so, mitigation is required

## Slide 4: Equity Impacts: Title VI requirements
What is “Title VI Requirements” ?
Who needs to comply ?
When is it required ?
Why is it required ?

## Slide 5: Fare and Service Changes
Fare:
Across the board increase
Increase on minimum fares only
Increase on some selected modes only
Increase in transfer fares
Service:
Route modifications
Service reductions
Service elimination

## Slide 6: How do you measure impacts?
Using travel models
Surveys
Simple sketch planning techniques
Note: FTA does not endorse any
particular method

## Slide 7: HDR’s Methodology
Developed in 2010 for a fixed guide-way system.
First applied to BART.
It is a Sketch planning approach.
Does not require large data.
Easy to understand (most FTA reviewers are not modelers)

## Slide 8: HDR’s Methodology
Six steps involved
Step 1: Identify where protected populations live (in GIS)
Step 2: Delineate station catchment area. Estimate average boarding fares at each station before and after fare increase
Step 3: Determine magnitude of protected populations in the station catchment area

## Slide 9: HDR’s Methodology
Step 4: Compute system wide average fare for each protected group (before & after)
Step 5: Compare % increase in fares for protected groups with non-protected groups
Step 6: Use professional judgment or statistical tests to determine if disparity exists

## Slide 10: Example
Ex: Lagrange County Transportation Authority (LCTA)
LCTA wants to increase rail fares by 10 %. CBD surcharge by 5 %.
System has distance based fare
Question: Will there be any disproportionate impacts associated with this fare increase ?

## Slide 11: Data needed
Fare tables
Station to station passenger flows (if available)
Census Data / ACS Data
Catchment area definition

## Slide 12: Step 1: Identify Protected Groups
Map the Distribution of minority, non-minority, low-income and non-low-income populations.
Definitions must be consistent with MPO’s standards

## Slide 13: Step 2: Delineate catchment Area / Estimate Ave. fares
Delineate catchment area
Use data from survey
Or 1/3 mile for rail
Or 1/4 mile for Bus
Estimate average boarding fares for each station
Simple average
Average weighted by trips

## Slide 14: Step 2: Estimate Average Boarding Fares

## Slide 15: Step 2: Estimate Average Boarding Fares

## Slide 16: Step 2: Estimate Average Boarding Fares

## Slide 17: Step 2: Estimate Average Boarding Fares

## Slide 18: Average boarding fares
Sycamore Ctr:
Ave. Boarding Fare: $ 3.35
(before fare increase)
What does it represent?

## Slide 19: Percent increase in boarding fares
Sycamore Ctr:
Ave. Boarding Fare: $ 3.73
(after fare increase)
Fare Increase: 11.40 % for all people in the catchment area

## Slide 20: Percent increase in boarding fares
Percent increase is a function of:
Trip flows
Increase in min. boarding fee
Increase in CBD surcharge

## Slide 21: Fare Increase for the System
Simple average
Average weighted by population
Average weighted by protected population

## Slide 22: Step 3: Estimate the magnitude of Protected Populations
US Census, ACS
Dealing with Overlapping areas

## Slide 23: Step 4: Compute System wide Average Fare

## Slide 24: Step 5: Compare Percentages
Ave. fare for Minorities: 12.96%
Ave. fare for Non-minorities: 12.67%
Ave. fare for Low-income pop: 12.31%
Ave. fare for Non-low-inc pop: 12.01%

## Slide 25: Step 6: Determination of Disparate Impact
Use professional judgment
Use statistical methods

## Slide 26: Closing Remarks
HDR method is
Simple and logical
Doesn’t require large data
Can be expanded to any system
Acceptable to FTA