## Slide 1
Development and Application of a Parcel Based Statewide Travel Demand Model for the Assessment of the Travel Impacts of Smart Growth Strategies and Sidewalk Investments

## Slide 2: Why Model Small Areas w/a Statewide Model?
ISTEA is Now 20 Years Old and We are Still Searching for the
Land Use-Transportation Connection.
Actually, Analysis of that Connection Has Been Sought for Much Longer:
“How Can You Know What to Try With Traffic Until You Know How the City Itself Works, and What Else it Needs to Do With Its Streets ?”
- Jane Jacobs, The Death and Life of Great American Cities, 1961,
Quote Reprinted in ITE Journal, April 2011.
But, We’re Coming Around:
“ . . . Communities are Starting to Realize that Transportation Must Address Accessibility Rather than Mobility and They are Looking for Solutions to Improve Their Transportation” Networks.
- Todd Littman, ”American Needs Complete Streets”,
Quote Printed in ITE Journal, April 2011.

## Slide 3: Why Model Small Areas w/a Statewide Model?
Widen
Congestion
Congestion
Traffic
Capacity
Years
The problem with current practices

## Slide 4: Why Model Small Areas w/a Statewide Model?
Common Development Trends

## Slide 5: Why Model Small Areas w/a Statewide Model?
Smart Growth Goals

## Slide 6: Why Model Small Areas w/a Statewide Model?
Project Need:
DelDOT routinely conducts transportation and land use studies for corridors and communities
DelDOT conducts scenario planning for it’s Statewide and MPO Long Range Transportation plans that include land use alternatives and various modal investments
A tool needed to be developed to evaluate the impacts of various growth strategies and transportation investments on transportation demand and air quality

## Slide 7: Why Model Small Areas w/a Statewide Model?
Current Options to evaluate the impacts of land use form on transportation needs:
GIS
3-D Visualization (Sketch Planning)
Travel Demand Models
Microsimulation Models

## Slide 8: Why Model Small Areas w/a Statewide Model?
GIS
Pros:
  Easy to work with
  Readily available
  Excellent Relational Data Analysis Tool
Cons:
  Can’t Evaluate Travel Demand Impacts of Transportation and Land Use Decisions
  Would not produce the detailed data needed for operational analyses

## Slide 9: Why Model Small Areas w/a Statewide Model?
3-D Visualization and Scenario Planning (Sketch Planning) Concept Tools
Pros:
  Visually Exciting
  Readily available
  Rapid Scenario Evaluations
Cons:
  Can’t Evaluate Travel Demand Impacts of Transportation and Land Use Decisions
  Wouldn’t reflect the impacts of small study areas within the context of the overall region
  Would not produce the detailed data needed for operational analyses

## Slide 10: Why Model Small Areas w/a Statewide Model?
Travel Demand Models
Pros:
  Readily available
  Rapid Scenario Evaluations
  Good For Evaluating travel demand impacts of land use and transportation decisions
  Can produce the detailed data needed for operational analyses
  Reflects the impacts of changes in small study areas within the context of the overall region
Cons:
  Not visually exciting for the public without post-processing
  Aggregate TAZ’s usually too large to be sensitive to smart growth scenario testing

## Slide 11: Why Model Small Areas w/a Statewide Model?
Microsimulation Models
Pros:
  Visually Exciting
  Readily available
  Rapid Scenario Evaluations
Cons:
  Can’t Directly Evaluate Travel Demand Impacts of Transportation and Land Use Decisions
  Wouldn’t reflect the impacts of small study areas within the context of the overall region
  Data intensive with long lead times makes scenario testing difficult

## Slide 12
DelDOT chose to use their Statewide Travel Demand Model because of its geographic coverage and ease of implementation.
Why Model Small Areas w/a Statewide Model?

## Slide 13: DelDOT Micro-Model
DelDOT’s Travel Demand Model Policy:
Develop Standard Applications.
New Features Must Integrate with Entire Model Chain.
Leverage Model Development Funds:
  Delaware Travel Monitoring System (DTMS):
Ongoing Trip, Mode, O-D Data Collection
250 Households/Month, CATI Polling Method
Over 32,000 Surveys in Database Since 1998

## Slide 14: DelDOT Peninsula Model Background
Background:
  Delaware plus Maryland’s “Eastern Shore”
  Population of 1.2 Million
  Area of 5,375 miles2

## Slide 15: DelDOT Peninsula Model Background
Feature Models
Air Quality Conformity
EZPass Toll/Mode Split Model
“Build/No Build” Model
Statewide Evacuation Model
Seasonal Tourist Model
Junction Model
TIS Model (Extra P’s & A’s)
Model Maintenance
(Network, TAZ, &
Count Update Utilities)
Micro-Model
Outputs
(Reports, GIS Files,
Loaded Networks, etc)
Core Model
(5-Step Travel Demand Model Equations)
Single Network Processor
GIS TAZ Land Use Layer

## Slide 16: DelDOT Peninsula Model
  13,491 Links in the Travel Network
2108 TAZ’s

## Slide 17: DelDOT Micro Model
  177,211 Links in the Travel Network
  19,640 TAZ’s

## Slide 18: DelDOT Micro Model Process

## Slide 19: DelDOT Micro Model Process

## Slide 20: DelDOT Micro Model Process

## Slide 21: DelDOT Micro Model Process
Choose TAZ for Micro Modeling
Demographic Data Processor
Peninsula Model TAZ Demographic Data
Census Block Demographic Data
Micro Model Demographic Data
Define Micro Links to include in Micro Model in GIS
Network Processor
Master Input Network with Peninsula Model Network links and statewide Local links
Micro Model Network
Trip Generation
Trip Distribution
Model Split
Traffic Assignment
Mode Split Factor from Peninsula Model

## Slide 22: DelDOT Statewide Sidewalk Network

## Slide 23
Motorized/Non-Motorized Split
Sidewalk walking distance
Bicycle traveling distance
Walk
Bike
Motorized
Mode Split
Mode Split Factor
Transit User
SOV: Non-toll/Cash/EZ-Pass
HOV: Non-toll/Cash/EZ-Pass
Micro Model Mode Split Process

## Slide 24: Case Studies
200 unit subdivisions in Southern New Castle County
  Suburban Middletown
    Case Studies 1 and 2
  Urban Middletown
    Case Studies 3 and 4

## Slide 25: Case Study
Detailed Study Area from South of the Canal to the Kent County Border

## Slide 26: Case Study Scenarios
Test the impacts of “Grid vs. Cul-de-Sac” development patterns on travel patterns, mode choice, and emissions

## Slide 27: Case Study Scenarios
Evaluate Scenarios using:
  Peninsula Model TAZ’s
  Micro-model TAZ’s
  Individual Parcels as TAZ’s for subdivision

## Slide 28: Existing Study Area Sidewalk Connections
Assume Sidewalks on all new roads and centroid connectors

## Slide 29: Peninsula Model TAZ Connections

## Slide 30: Micro Model TAZ Connections

## Slide 31: Parcel Model TAZ Connections

## Slide 32: Peninsula Model TAZ Connections

## Slide 33: Micro Model TAZ Connections

## Slide 34: Parcel Model TAZ Connections

## Slide 35: Model Results for Subdivision Trips
Chart: Average Travel Time (hours)
| Peninsula Model | Micro Model | Parcel Model
Case 1 | 0.42072 | 0.41363 | 0.41501
Case 2 | 0.40721 | 0.415 | 0.42173
Case 3 | 0.34699 | 0.2812 | 0.24808
Case 4 | 0.3535 | 0.33 | 0.28

## Slide 36: Model Results for Subdivision Trips
Chart: Average Trip Distance (miles)
| Peninsula Model | Micro Model | Parcel Model
Case 1 | 18.525 | 18.0912 | 18.1305
Case 2 | 17.9529 | 18.0141 | 18.5911
Case 3 | 15.8402 | 12.4773 | 10.9361
Case 4 | 15.889 | 15.577 | 13.2096
Chart: Average Travel Distance (Miles)
| Peninsula Model | Micro Model | Parcel Model
Case 1 | 18.525 | 18.0912 | 18.1305
Case 2 | 17.9529 | 18.0141 | 18.5911
Case 3 | 15.8402 | 12.4773 | 10.9361
Case 4 | 15.889 | 14.7 | 12.2

## Slide 37: Model Results for Study Area Trips
Chart: Daily Walking Trips within Study Area
| Peninsula Model | Micro Model | Parcel Model
Case 1 | 147 | 150.63 | 152.56
Case 2 | 147 | 150 | 151
Case 3 | 149.75 | 152 | 176
Case 4 | 149.25 | 150 | 162

## Slide 38: Conclusions
All three models were sensitive to the location of the subdivision
The Micro Model and Parcel Model were sensitive to the “Smart Growth” vs. “Traditional Growth” evaluation

## Slide 39: Conclusions
The Parcel Model was most sensitive to the location of the subdivisions on both motorized and non-motorized travel.
The models produced data needed for more detailed operational analyses.

## Slide 40: Questions?
Scott Thompson-Graves
724-779-7940
sthompson-graves@wrallp.com
Mike DuRoss
302-760-2110
michael.duross@state.de.us
Li Li
703-293-7423
lli@wrallp.com