## Slide 1: Davie Road/S.R. 84 Transit Facility Demand Estimation
Presented by
Jeff Weidner & Jeremy Mullings
Florida Department of Transportation
Yongqiang Wu & Kasey Cursey
Gannett Fleming, Inc.
Presented to
13th TRB National Transportation Planning Applications Conference
Reno, Nevada
May 9, 2011

## Slide 2: Overview
Project Background
Transit Activity Estimation
Parking Demand Estimation
Summary
2

## Slide 3: Participating Agencies
Florida Department of Transportation (FDOT), District 4, Office of Modal Development – LEAD
  FDOT District IV, Systems Planning Office
  Broward County Transit (BCT)
  Town of Davie
  South Florida Commuter Services
  South Florida Education Center (SFEC) Transportation Facilities
  Cruisin’ Community Transit Connection (CCTC)

## Slide 4: Project Location – Town of Davie, Broward, FL
Davie PnR
South Florida Education Center (SFEC)

## Slide 5: Existing Bus Services
Notes: Route 12 operates between West Regional Terminal and North Beach Park running along major thoroughfares such as Sheridan St, Davie Rd, and University Dr.

## Slide 6: Proposed Express Services

## Slide 7: Project Needs
Develop a Park-and-Ride Transit Facility to Support Regional Connectivity and Multimodal Options in Broward County
Provide Access to Local and Express Bus Services
Provide Connections between Bus Service and the SFEC Campus Shuttle Services
Provide a Location for Commuters Using Van-pool and Carpool Options

## Slide 8: Study Objectives
Develop a General Order-of-Magnitude for Transit Activity at the Proposed Davie Facility
Determine the Number of Parking Spaces Required to Meet the Demand

## Slide 9: Transit Activity Estimation
General Methodology
  Use model (SERPM) to estimate future ridership
  Use historical ridership for post-model adjustment when appropriate
  Coordinate with local agencies
  Use professional judgment

## Slide 10: Southeast Florida Regional Planning Model
Covers Three Counties (Palm Beach, Broward, and Miami-Dade) in South Florida
Multimodal
  Automobile
  Trucks
  Bus (regular, express, limited stop)
  Rail (light, heavy, commuter)
Time-of-Day (AM, OP, PM)
Validated to 2005 Conditions
Includes 2030 Adopted LRTP Model

## Slide 11: SERPM Flow Chart

## Slide 12: Future Population & Employment Growth
Chart: 
| POP | EMP
2005 | 272915 | 121050
2030 | 363540 | 154831
33%
12

## Slide 13: Estimated Transit Activity
Route | 2030 Daily Boardings at Davie PnR | Sources
Route 9 | 148 | Model/BCT Local Data
Route 12 | 125 | Model/BCT Local Data
Sunrise Express 2 | 85 | Model
Weston Express 2 | 85 | Model
Sawgrass – Miami Express | 57 | Model
Total Transit Activity | 500 | 

## Slide 14: Parking Demand Estimation
Park-and-Ride Demand
  Based on projected transit activity
Vanpool and Carpool Demand
  Based on FDOT Guidelines and Coordination with FDOT’s South Florida Commuter Services

## Slide 15: Total Parking Demand for Local Buses
Route | Adjusted Peak Period Boarding | PnR Share | Space Needed
Route 9 | 65 | 4% | 3
Route 12 | 99 | 4% | 4
Total Spaces |  |  | 7

## Slide 16: Total Parking Demand for Express Buses
Route | Projected Peak Period Boarding | PnR Share | Space Needed
Sunrise Express | 85 | 25% | 21
Weston Express | 85 | 25% | 21
Sawgrass-Miami Express | 57 | 25% | 14
Total Spaces |  |  | 56

## Slide 17: SFEC Campus Shuttle
Will Provide a Connection to Davie Park-and-Ride Lot During Peak Periods
Coordinated with Director of Facilities
  Students and faculty may use shuttle at Davie to avoid parking on Campus
Built a 1,000-Space Garage in 2008
  No near-term needs
Needs 12 in the Future
  Current ridership 250/day
  Apply 5% factor

## Slide 18: Carpool and Vanpool Parking Demand
Based the State Park-and-Ride Lot Program Planning Manual by FDOT, April 2001
Formula (Adaption of the ITE Model)
  Demand = a*Vp + b *Vs
  Where
  Vp = Total design period traffic on primary facilities
  Vs = Total design period trafic on secondary facilities
  a, b = Diversion Factors on the primary/secondary facilities
Design Period Traffic from the Model
a = 0.03, b=0.01(Manual Recommended)

## Slide 19: Total Parking Demand
Route | Space Needed
Local Bus (minimal for 2010) | 7
Express Bus | 56
SFEC Campus Shuttle | 12
Carpool/Vanpool | 65
Total Estimated Demand for Parking | 140

## Slide 20: Summary
Involved Using SERPM Model, Post Model Adjustment Procedures, FDOT Guidelines, and Professional Judgment
Total Transit Activity at Davie Projected to be 500 Daily Boardings
Will need 140 Parking Spaces
Final Design Scheduled for July 1, 2011.

## Slide 21: Questions?