## Slide 1: Hybrid Mesoscopic-Microscopic Traffic Simulation Framework
September 2008
What’s coming in Aimsun: New features and model developments
1
Alex Torday, Jordi Casas and Josep Perarnau
torday@aimsun.com

## Slide 2: Content
Background
  Traffic Simulation Requirements
  What model is the best, Meso or Micro?
  One step forward: Hybrid model
  Problems combining Mesoscopic and Microscopic models
Model Integration
  Why?
  How?
  DTA as a key process
  How DTA is included?
Hybrid Framework
Computational Results
Conclusions

## Slide 3: Background
Traffic Simulation models Requirements
  Large Complex Systems
  Dynamic analysis
  Real-time applications
Example:
  Integrated Corridor Management Systems (ICM Systems)
    Source: http://www.its.dot.gov
    USDOT Intelligent Transportation Systems (ITS) program has launched a generation of initiatives aimed at improving transportation safety, relieving congestion and enhancing productivity.

## Slide 4: Background: What model (Meso or Micro) is the best?
The question is not whether one approach is better or more appropriate than other
But which is the most appropriate use of each approach and how can then work together in a common framework
Or if there is a unique approach that can replace satisfactorily all others

## Slide 5: Background: One step forward, Hybrid Model
Model decision: All or Nothing (black or white)
  Mesoscopic model or Microscopic model?
    Is a detailed representation of the vehicles necessary?
    Is a detailed representation of detector measurements necessary?
    What type of signal control as to be emulated?
    What is the available data for calibration/validation?
    What is the size of the network?
    What is the required computation time?
    What kind of outputs are required?

## Slide 6: Background: One step forward, Hybrid Model
Model decision: The GREY exists
    Previous answers could lead to the need of using both models!
The Hybrid model is an alternative for solve all requirements of a project
Split the network in two type of areas:
  Mesoscopic areas
  Microscopic areas
Unique Traffic demand
Unique Traffic Control
Unique DTA
Notes: AFEGIR UNIQUE NETWORK REPRESENTATION

## Slide 7: Background: Problems combining Mesoscopic and Microscopic models
  Network representation consistency
  Consistency problems in Route Choice
  Communication and Exchange of information
  Vehicle representation
  Traffic dynamics at meso-micro boundaries
Model Integration
Hybrid Framework

## Slide 8: Model Integration, Why?
An integrated framework to support a transport analysis methodology that combines the three approaches, overcomes consistency and synchronization problems

## Slide 9: Model Integration: How?
EXTENSIBLE OBJECT MODEL
MODEL DATABASE
Micro
Meso
Macro
EXTENSIBLE OBJECT MODEL
MACRO ASSIGNMENT MODEL
MICROSCOPIC
TRAFFIC SIMULATOR
MESOSCOPIC TRAFFIC SIMULATOR

## Slide 10: Model Integration: DTA as a key process
Principles (Florian et al 2001)
  Components of DTA models:
    Method for determining path-dependent flow rates on the paths in the network
      Dynamic equilibrium algorithm
      Route Choice stochastic model
    Dynamic network loading method
      Simulation model
        Mesoscopic
        Microscopic
Time-dependent OD Matrices
Network with performance functions
gi(t)
sa(v(t))
(1) PATH CALCULATION AND SELECTION
a) Dynamic equilibrium algorithm
b) Route Choice stochastic model
Determine paths and time-dependent path flows
(2) DYNAMIC NETWORK LOADING
Load Network (network loading problem)Link flows, time, path times.
Convergence Criteria:
a) Analytical (Rgap)
b) All demand loaded?
STOP
No
Yes
Notes: According to Florian et al. (2001), a dynamic traffic assignment model consists of two main components:
A method for determining path-dependent flow rates on the paths in the network.
A dynamic network loading method, which determines how these path flows give rise to time-dependent arc volumes, arc travel times and path travel times.
The diagram in Figure 3.1 depicts the logical, conceptual approach to dynamic traffic assignment models. Path flow rates depend on the emulation of drivers’ path choice behaviour, determining in this way which of the alternative approach is implemented:
Dynamic en-route assignment. At each time period, the corresponding fraction of the demand is assigned to the currently available paths for each origin-destination pair according to the probabilities estimated by a route choice model. Drivers can be allowed to dynamically change route en route if a better path from their current position to their destination becomes available.
Dynamic equilibrium assignment. Path flows are determined by an approximate solution to the mathematical model for dynamic equilibrium conditions (Florian et al., 2001), (Barceló et al., 2002).

## Slide 11: Model Integration
Historical Link Costs
Dynamic Traffic Assignment Server
Network
Link Cost Functions
Shortest
Path
Server
Calculated
Paths
Path
Statistics
Route Choice Models
MSA Module
RGap Evaluation
Time – dependent OD Matrices
Path Flows
Network Loading
Microscopic
Model
Mesoscopic
Model
Updated Link Costs

## Slide 12: Hybrid Framework
Time – dependant OD Matrices
Hybrid Network Loading
Microscopic Model
Mesoscopic Model
Path Flows
Updated Link Costs
Historical Link Costs
Dynamic Traffic Assignment Server
Shortest Path Server
Network
Link Cost Functions
Calculated Paths
Path Statistics
Route Choice Models
MSA Module
RGap Evaluation
META Event Oriented Simulator
Vehicle Manager

## Slide 13: Hybrid Framework: New elements
META Event Oriented Simulator: syncronization between Mesoscopic and Microscopic models
Vehicle Manager:
  Vehicle generation
  Boundary conditions
Hybrid Network Loading
Microscopic Model
Mesoscopic Model
META Event Oriented Simulator
Vehicle Manager

## Slide 14: Computational Results
Madrid Network
  Mixed network: urban and urban freeway
  Topology:
    327 centroids
    1375 intersections
    3591 sections
    Total length: 570 Km
    Total length lane 1160 Km
  Traffic demand: Morning Peak hour (6:15am – 9:30 am)
    Time slice 15 minutes
    Total number of trips: 409502
  Public Transport: 172 Public Transport lines

## Slide 15: Computational Results
191 sections and 55 nodes considered as microscopic

## Slide 16: Computational Results
Scenario Analysis
  Using only Microscopic simulation (Micro)
  Using only Mesoscopic simulation (Meso)
  Using Hybrid (meso/micro) simulation (Hybrid)

## Slide 17: Computational Results
Validation of the real data set compared with simulation outputs
MOE | Meso | Hybrid
Vehicles gone out | 365.159 | 345.396
Vehicles inside | 31.764 | 34.669
Vehicles waiting out | 20.318 | 36.935
Regression slope | 0,92 | 1,04
Regression intercept | 234,19 | -14,9
Regression R2 | 0,90 | 0,86
Flow [veh/h] | 103.628 | 104.349
Density [veh/km] | 13,43 | 12,61
Speed [km/h] | 39,82 | 39,56
Travel time [sec/km] | 115,96 | 117,38
Delay time [sec/km] | 54,81 | 61,54

## Slide 18: Computational Results
Consistency between Meso and Hybrid
Chart: Flow

## Slide 19: Computational Results
Consistency between Meso and Hybrid (GEH)
Chart: 

## Slide 20: Computational Results
Consistency between Meso and Hybrid (GEH)

## Slide 21: Computational Results
Consistency between Meso and Hybrid (GEH)

## Slide 22: Computational Results
Computation Time
  Micro: 2595 seconds
  Meso: 259 seconds (10% of the Micro time)
  Hybrid: 331 seconds (13% of the Micro time)

## Slide 24: Conclusions
Equivalence of three models compared with the real data set
Consistency between Meso and Hybrid
Once the consistency is guaranteed, the performance becomes the critical point
  The difference of computation time between meso and micro is significant
  The difference of computation time between meso and hybrid is not significant. Obtaining a higher detail of the simulation outputs
Usability in large scale networks: 1 meso subnetwork + n micro subnetworks

## Slide 25
20 West 22nd Street
Suite 612
New York NY 10010 Tel. 917 267 8534 mail: info@aimsun.com
web: www.aimsun.com