## Slide 1: Estimating Mobile Source GHG In Los Angeles County:
Presented by:
David Jackson & Michael Snavely, Cambridge Systematics, Inc.
Robert Calix, Los Angeles County Metropolitan Transportation Authority
May 9, 2011
A Web-based Tool for Calculating the Greenhouse Gas Benefits of Transportation Improvement Projects

## Slide 2: LA Metro GHG Impact Toolset Agenda
Background/Context
Technical Approach
Web-Based Analysis
Applying Tools in the Gateway Cities COG
Results

## Slide 3: 1. Background SB 375 Mobile-Source GHG Reduction Legislation
Sets GHG reduction targets for MPOs
  Targets for 2020 and 2035 vs. 2005
  Metric : lbs CO2e per capita
MPOs must develop “Sustainable Communities Strategy” (SCS) that:
  Lays out regional strategy for meeting targets
  Is integrated w/long range planning process
  Has “reasonably expected” funding
Notes: SCS:
- note that bill language and ARB direction is largely land use focused. Integration with housing needs assessment requirements

## Slide 4: 1. Background SCAG Region SB 375 GHG Reduction Targets
Chart: 
| 2005 | 2020 | 2035
BAU | 21.2 | 20.1 | 20.4
Target | 21.2 | 19.5 | 18.4

Lbs carbon/capita
Per weekday
8%
13%

## Slide 5
1. Background
Los Angeles County: Strained Infrastructure
Los Angeles
County
Notes: Fee

## Slide 6: 1. Background Los Angeles County: Strained Infrastructure
Chart: 
| Lane-Miles | VMT | Delay
 | 0.03 | 0.39 | 2.13
Estimated Growth 2005 - 2035

## Slide 7: 1. Background Opportunity to Measure (and fund) GHG Reduction…
CS Moving Cooler sketch-planning methodologies
  Adapt to reflect specific nature of travel within LA County.
Metro’s Existing Congestion Mitigation Fee program site
  Project & growth database accessible to all cities
  Fee on new development to fund improvements to network
  If projects coincide, fee solves unfunded mandate problem

## Slide 8: 2. Technical Approach Process Overview
Adapt “best practices” project methodologies to region
    Local research for elasticities, speed-flow curves, etc. to accurately portray traveler response in LA County
    Project-specific inputs that city staff can fill-in
Develop and test a draft analytical spreadsheet tool
Develop and test tool in a web-based environment.

## Slide 9: 2. Technical Approach Applicable Projects w/ GHG Reduction Potential
  Intersection Improvements
  Corridor System Operations Improvements
  Roadway Capacity Improvements
  On/Off-Ramp Capacity
  RR Grade Separations
  Transit Enhancements
  Park-and-Ride Lots
  Bike/Pedestrian Projects
  Transit/Managed Lanes (HOT, Shared Busway)
Limited to improvements eligible for fee program
Either Reduce VMT – or – Reduce Delay

## Slide 10: 2. Technical Approach Process Overview
VMT Reduction Projects (bike/ped, transit, park/ride)
Corridor-Specific Details
(ADT, Ridership)
Project-Specific Details
(extent, frequency)
Other
Local Factors
(e.g, lot usage %)
Project Effectiveness
Change in Travel Time or Cost
Apply Local Elasticity
Vehicle Trip Reduction
VMT Reduction
LDV CO2e Emission Factors
Average Trip Lengths
CO2e Reduction
Area-Specific Details
(Density, Activity Centers)

## Slide 11: 2. Technical Approach Process Overview
Delay Reduction Projects – Corridor (Signal Sync, etc.)
“Project” Inputs
Corridor Details
+
Project-Specific
(e.g. extent,
# intersections)
LDV CO2e Emission Factor by Speed
Project CO2e Emissions
Corridor No-Project
Peak VHT & Congested Speed
“No Project” Inputs
Corridor Details
e.g. ADT + operations
Apply
Appropriate Speed/Flow Curve
Corridor Project Peak VHT & Congested Speed
LDV CO2e Emission Factor by Speed
CO2e Reduction
No-Project
CO2e Emissions

## Slide 12: 2. Technical Approach Process Overview
Delay Reduction Projects – Intersection Projects
Intersection Peak Period Approach
Volumes
Project-Specific Details
Post -Improvement Delay Calculation
Change in Total Peak Delay
LDV CO2e Emission Factors
CO2e Reduction
Intersection Existing Delay Calculations
Existing Condition

## Slide 13: 2. Technical Approach Summary of Outputs – GHG Emission Calculations
Project Type | Project Performance Outputs | CO2 Emissions Calculation
Bike/‌pedestrian Transit Park-and-ride Managed lanes | Reduction in VMT Improvement in transit speeds | Total reduction in VMT is multiplied by average VMT weighted speed light-duty vehicle emissions factor Additional transit revenue miles are multiplied by urban bus VMT weighted speed emission factor Emission factors (g/mi) for pre- and post-improvement urban bus speeds are multiplied by total transit miles
Road capacity On/Off-Ramp capacity Intersection improvement System ops. Grade separation | Change in peak speeds Change in intersection daily hours of delay Change in corridor average speed resulting from signal timing Total reduction in delay for at-grade rail crossings | Emission factors (g/mi) for pre- and post-improvement speeds multiplied by total VMT Idle emission factor is multiplied by pre- and post-improvement intersection hours of delay.

## Slide 14: 3. Web-Based Analysis LA Metro CMF Webtool
Fee Calculator
Socioeconomic
Forecast Data
Project Database
GHG Analysis

## Slide 15: 3. Web-Based Analysis LA Metro Project-Level GHG Sketch-Planning Tool

## Slide 16: 3. Web-Based Analysis LA Metro Project-Level GHG Sketch-Planning Tool

## Slide 17: 3. Web-Based Analysis LA Metro Project-Level GHG Sketch-Planning Tool
User-specified
Derived on
back-end

## Slide 18: 3. Web-Based Analysis LA Metro Project-Level GHG Sketch-Planning Tool

## Slide 19
Gateway Cities COG
4. Applying Tools in the Gateway Cities COG
Notes: Fee

## Slide 20: 4. Applying Tools in the Gateway Cities COG Background
27 Cities + Port of Long Beach
Already dense & built out
Low-income
Very congested roadway network
Transportation GHG reduction benefits
Initial SCS Analysis using Metro toolset shows considerable
per capita reduction from Transportation projects

## Slide 21: 6. Results
Project-level sketch planning tools serve policy need
Web-based interface allows easy data entry for all users
Transportation projects show potential for significant GHG reduction in communities at/near capacity
Integration with congestion mitigation fee offers SCS funding solution
Opportunities exist to improve and expand functionality

## Slide 22
CONTACT
David Jackson
Cambridge Systematics, Inc.
Bethesda, MD
301-347-0100
Michael Snavely
Cambridge Systematics, Inc.
Oakland, CA
510-873-8700
Robert Calix
LA County Metropolitan Transportation Authority
Los Angeles, CA
213-922-5644