## Slide 1: USE OF TRIP TABLE ESTIMATION TO IMPROVE PROJECT TRAFFIC FORECASTS
13th TRB Planning Applications Conference
Reno, Nevada

## Slide 2: Background
Estimate Future Project Traffic.
I-95 in Southeast Florida.
64 mile Corridor Feasibility Study with managed lanes.
Model results must be:
  Carefully reviewed.
  Adjusted.
Search for a Systematic Process.

## Slide 3: Study Area
Miami-Dade, Broward, Palm Beach Counties
Southeast Regional Planning Model
3 time periods
4,284 TAZs
Subarea with 2,123 TAZs
Subarea

## Slide 4: Goals
Produce traffic estimates for morning and afternoon peaks.
Multiple target years: 2010, 2035, 2050.
Make systematic adjustments.
Minimize “post-processing”.

## Slide 5: Method
Trip table estimation (Cube Analyst).
Corrects for systematic errors.
Productions and attractions not altered.
Future volumes based on:
Adjusted Base
+ Growth (unadjusted future-base)
Difference judged to be more reliable than factors.

## Slide 6: Requirements
4,284 TAZs seemed too big for Analyst.
Subarea of 2,123 TAZs worked.
Analyst worked better as an iterative process (20), on a sample of traffic counts.
Freeway counts chosen for every iteration.
Arterial counts chosen randomly (about 10% used, each time).

## Slide 7: Effectiveness
Chart: Analyst %RMSE
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
AM | 0.442 | 0.335 | 0.293 | 0.271 | 0.255 | 0.244 | 0.235 | 0.226 | 0.22 | 0.215 | 0.212 | 0.209 | 0.206 | 0.204 | 0.201 | 0.2 | 0.197 | 0.196 | 0.194 | 0.192
Off-PK | 0.422 | 0.292 | 0.241 | 0.216 | 0.195 | 0.179 | 0.173 | 0.167 | 0.163 | 0.158 | 0.156 | 0.153 | 0.153 | 0.154 | 0.152 | 0.146
PM | 0.395 | 0.309 | 0.267 | 0.245 | 0.23 | 0.219 | 0.217 | 0.204 | 0.201 | 0.192 | 0.192 | 0.189 | 0.184 | 0.181 | 0.182 | 0.18 | 0.183 | 0.183 | 0.179 | 0.177

## Slide 8: Changes in the Trip Table
Chart: Analyst Effect on Trip Distance
| AM PEAK | PM PEAK | OFF PEAK
Before | 7.11 | 6.96 | 7.65
After | 6.6 | 6.31 | 7.3

## Slide 9: Conclusions/Caveats
Weigh against ad hoc or NCHRP 255-style adjustments.
Changes the average trip length, so some concern about the overall impact on traffic patterns.
Dramatic reduction in link-by-link assignment error.
Careful review of results still required.
Post-processing adjustments still needed.

## Slide 10: Acknowledgements
Florida Department of Transportation, District 4
  Shi-Chiang Li, AICP
  Derek Miura