## Slide 1: Forecasting Traffic Impacts for Work Zone Transportation Management Plans
TRB Planning Applications Conference
June 4, 2019

## Slide 2: Problem Statement
Work zone traffic impacts are addressed through Traffic Management Plans (TMP), a process recently updated to include modeling
Need to validate current modeling capabilities and determine appropriate level of effort

## Slide 3: Context
Traditional four-step model recently replaced by activity-based model
DTA updated to spatially align with ABM – larger/more detailed coverage

## Slide 4: Approach
Back-casting for two major construction projects
  35W@94: Downtown to Crosstown in Minneapolis
  US 169 Nine Mile Creek Bridge Replacement
Use of StreetLight Data and MnDOT loop detectors for ground truth data

## Slide 5: Slide Symbols
StreetLight Data
Loop Detector Counts
Regional travel demand model (ABM)
Dynamic Traffic Assignment (DTA) model
LOOP
ABM
Street
Light
DTA

## Slide 6: 35W@94: Crosstown to Downtown

## Slide 7: 35W@94: Downtown to Crosstown
I-35W from I-94 to 43rd St
Summer 2017 to Fall 2021
Partnership
  MnDOT
  Metro Transit
  Hennepin County
  City of Minneapolis
Major transit corridor
  Over 500 daily bus trips
  14,000 daily rides
Notes: Aging Infrastructure
Roadway and Bridges originally constructed in 1965.
Replace 11 bridges with 17 new bridges and re-habilitate 4 other bridges.
New Pavement on I-35W from 43rd Street to 11th Avenue
325,000 Square yards of concrete pavement (65 football fields)
70,000 Tons of Asphalt (= to the weight of 35,000 cars)
10 Million pounds of reinforcement (Equal to the weight of 22 Statues of Liberty)
Rehabilitating inplace noise walls
Transit Advantage
Convert Priced Dynamic Shoulder Lane to Permanent MnPASS Lane NB
Establish MnPass Lane in the SB direction out of Downtown Minneapolis
Construct In-Line Transit Station at Lake Street.
Construct direct connection for transit vehicles from TH 65 to 12th Street.
Transit improvements on Lake Street.
Improve Mobility on I-35W and I-94
New access ramps and auxiliary lanes reduce weaving on the corridor
Re-alignment of NB to WB flyover improves mobility on both I-35W and I-94.
Accessibility Improvements
New ramp from NB I-35W to 28th Street. (Improved access to Children’s Hospital, Allina, and Wells Fargo.
New ramp from SB I-35W to Lake Street.
Upgrade intersections to be ADA compliant
Provide infrastructure for bicycle corridors.

## Slide 8: I-35W: Construction Scenarios
Alt. | Phase | Description | Number of General Purpose Lanes | Number of Transit/HOV/ MnPass Lanes | TH 65 Ramp Open or Closed | EB I-94 to SB 35W Ramp Open or Closed | NB I-35W to WB I-94 Ramp Open or Closed | Duration
1 | 1 | 6 Lanes | 4 (2 NB / 2 SB) | 2 (1 NB / 1 SB) | Open | Open | Open | 2 Years
 | 2 | 6 Lanes | 4 (2 NB / 2 SB) | 2 (1 NB / 1 SB) | Open | Open | Closed | 2 Years
2a | 1 | 5 Lanes, Phase 1 | 4 (2 NB / 2 SB) | 1 (1 NB / 0 SB) | Closed | Closed | Open | 1 Year
 | 2 | 5 Lanes, Phase 2 | 4 (2 NB / 2 SB) | 1 (1 NB / 0 SB) | Open | Open | Open | 1.5 Years
2b | 1 | 4 Lanes | 4 (2 NB / 2 SB) | 0 | Closed | Closed | Closed | 1 Year
 | 2 | 6 Lanes | 4 (2 NB / 2 SB) | 2 (1 NB / 1 SB) | Open | Open | Closed | 1.5 Years
3 |  | Full Closure | 0 | 0 | Closed | Closed | Closed | 2.5 Years
Timeline
  Pre-construction period: April 2018
  Construction time period: October

## Slide 9: 35W ABM: Volume Delta map
ABM
Blue – Volume Increase
Orange – Volume Decrease
Closed: TH 65 to Downtown and I-94 West
I-35W Capacity Restrictions

## Slide 10: Where does the traffic go?
ABM
Baseline I-35W traffic
Trips assigned with construction restrictions

## Slide 11: Volume Delta : Freeways
Loop Detector
ABM
ABM
Many locations have similar traffic diversion pattern (I-35W, I-94, TH 100)
Magnitude of delta in work zone location similar to observed conditions

## Slide 12: Volume Delta : Arterials
Lower volume diversion on arterials versus DTA
27,500 Volume delta on arterials
Volume Delta
ABM
About 50% of diversion within 2.5 miles of I-35W

## Slide 13: DTA: Local Streets
High volume diversion on Stevens Ave
Volume Delta at:
  Stevens Ave: +26,000
  Nicollet Ave: +12,000
DTA

## Slide 14: Volume Delta : Freeways
31 Locations
Overestimation of volume delta at the work zone location
Underestimation of volume delta on freeway system
Possible chances of overestimation on lower functional class
Loop Detector
DTA
DTA
LOOP

## Slide 15: Volume Delta : Arterials
52,500 positive volume delta on arterials close to the work zone
DTA
Volume Delta
Nearly 70% of diversion within 2.5 miles of I-35W

## Slide 16: Arterials Volume Delta : ABM vs DTA
DTA
ABM
Traffic diversion similar on Lyndale Ave, Cedar Ave, Hiawatha
Low volume delta observed on Nicollet Ave
Concern that DTA model does not adequately constrain capacity on local roadways
ABM
DTA

## Slide 17: Streetlight Analysis : Arterial
Street
Light
No up-to-date volume data on arterials available
Streetlight O-D percentages were used to analyze traffic diversion on major parallel routes
Reported values estimated by applying proportion of volume diversion to StreetLight percentages

## Slide 18: Summary: 35W Construction Scenario
Observation
  DTA overestimates diversions to roadways closer to the work zone
Possible reasons
  From previous analysis we know DTA directs more trips to local network
Recommendations
  Additional customized “traffic flow models” could be developed for DTA
  Addition of signal controls
DTA

## Slide 19: US 169 Bridge Closure

## Slide 20: US 169 Bridge Closure
Bridge closed

## Slide 21: Hwy 169 Construction Timeline
494 & 100 Constr.
Start
End
Dovre Dr. Closure
Nov 2016
Jan 2017
Sep 2017
Mar 2017
Initial traffic control configuration
Modified traffic control configuration
Data collection for during construction
Data collection for pre-construction

## Slide 22: US 169: Construction Scenarios
Scenario 2 most closely resembles the actual construction condition
Scenario | Description | Days of Construction
1a & 1b | Year 1: close one lane in each direction The freeway would remain open over the Nine Mile Creek bridge. Year 2: close one lane in each direction There would also be additional construction along I-35W between I-94 and 43rd Street and along I-94 between Nicollet Avenue to Shingle Creek Boulevard. | 335 + 215
2 | Close one lane of traffic in each direction Full closure over the Ninemile Creek bridge. | 335
3a & 3b | Directional closure of US 169 Year 1: Northbound full closure Year 2:Southbound full closure | 550

## Slide 23: US 169 Construction Results
ABM
DTA

## Slide 24: StreetLight Data
Assumptions for evaluation of Hwy 169 construction project
  Pre-construction time period: Mid November – Mid December 2016 (excluding the Thanksgiving weekend)
  Construction time period: April 2017
  Data only showing personal vehicles indexed volume*
  The volume is for average weekday and the time period is entire day
  * Indexed volume does not indicate actual number of trips or vehicles on the road but can be used to understand travel patterns and percentages
Street
Light

## Slide 25: Pre-construction NB Volume Using the Bridge
NB: 50,000
Middle Filter
Origin/Destination Passthrough Zone
Street
Light

## Slide 26: Pre-construction NB Volume Using the Bridge
Middle Filter
Origin/Destination Passthrough Zone
50% of NB traffic comes from 169 S of 62
Street
Light
50% of NB traffic comes from 62 & 212 & Bren Rd

## Slide 27: Pre-construction NB Volume Using the Bridge
Middle Filter
Origin/Destination Passthrough Zone
27% of NB traffic comes from 169 S of 494
Street
Light
23% of NB traffic comes from 494 & Valley View

## Slide 28: Pre-construction SB Volume Using the Bridge
Middle Filter
Origin/Destination Passthrough Zone
SB: 43,000
Street
Light

## Slide 29: Pre-construction SB Volume Using the Bridge
Middle Filter
Origin/Destination Passthrough Zone
Street
Light
40% of SB traffic comes from 169 N of 394
60% of SB traffic comes from 394, Hwy 7, Excelsior Blvd, 7th St, etc.

## Slide 30: Traffic Diversions During Construction
32% of traffic originally using the bridge to/from TH 169 south of I-494 diverted to TH 100.
35% of traffic originally using the bridge to/from TH 169 south of I-494 diverted to I-494.
Middle Filter
Origin/Destination Passthrough Zone
Accounted Diversion Routes
Other Diversion Routes

## Slide 31: Summary of US 169 Evaluation
Observation
  DTA emphasizes diversions to roadways closer to the work zone area
Possible reasons and Recommendations
  Signal controls are missing
  More calibration is needed for DTA
    Traffic flow models on freeways
    Addition of signal controls
Use of other methods in DTA
  Defining different user classes
  Defining official detour routes
DTA
Add some ABM findings

## Slide 32: Findings & Recommendations
DTA model tends to divert traffic later in the trip as it gets closer to the work zone, resulting in higher diversion to immediately adjacent routes
ABM (static assignment) may require more severe speed/capacity reductions on work zone links to replicate diversion magnitude
Signal control in DTA could help to constrain traffic shifts to local arterials

## Slide 33: Thank you! Questions?
Minnesota Department of Transportation SRF Consulting Group, Inc.
Jim Henricksen, AICP Paul Morris, PE
Director of Travel Behavior Principal – Transportation Analytics
jim.Henricksen@state.mn.us pmorris@srfconsulting.com
651-234-7782 763-452-4773