## Slide 1
Jeff Shelton
Texas A&M Transportation Institute
TRB Planning Applications Conference – Portland, OR
June 4, 2019
Dynamic Traffic Assignment Modeling to Assess ICM Strategies

## Slide 2: Goal
Assist TxDOT in analyzing potential benefits of ICM strategies for planned and unplanned events
Planned Closure
Overnight
Work Zone
Unplanned Closure
Incident

## Slide 3: Planned Closure
Full freeway closure
ICM response plan starts 5am
  DMS provide diversion routes
  Extend green time of 20 secs
  At 5am, DMS diverts 20%
  Drops to 10% at 6am
  Remove tolls from 5-7am
Austin, TX
What happens if TxDOT cannot open freeway by 5:00 am?

## Slide 4: Planned Closure – Travel Time Comparison

## Slide 5: Planned Closure - Heat Maps
Improvement in speed beyond morning peak
5:00
am
7:00
am
5:00
am
7:00
am
Base
ICM
Cesar Chavez
SH 45
Work Zone
San Marcos

## Slide 6: Unplanned Closure
Base case
  All 4 lanes closed on I-35
  Used actual incident data (fatality)
  Use DMS to divert traffic to alternate routes
Strategies
  ICM 1: DMS diversion to frontage road north of incident
  ICM 2: Adjust signal timing plans on frontage
  ICM 3: Additional DMS messaging to promote more diversion routes
DMS
I-35 Austin, TX

## Slide 7: Unplanned Closure
As additional ICM strategies are modeled, delays on I-35 are reduced

## Slide 8: Unplanned Closure
I-35 @ US 183 – Frontage Road
I-35 @ US 183 – Main Lanes

## Slide 9: Road User Cost
Section | Base | SH Only | SH + Arterials
San Marcos | $ 883,185 | $ 882,680 | $ 881,965
Kyle | $ 854,793 | $ 855,815 | $ 855,129
SH 45 | $ 824,281 | $ 825,386 | $ 824,798
Slaughter | $ 810,109 | $ 811,382 | $ 810,891
William Cannon | $ 810,860 | $ 812,289 | $ 811,752
SH 71 | $ 829,151 | $ 830,604 | $ 830,114

## Slide 10: Conclusion
ICM strategies improve mobility by shifting traffic away from highly congested areas
DTA model provides valuable insights on the impacts of ICM
Road user costs quantify congestion into monetary values
Challenges
  Predicting driver behavior
  Traffic control

## Slide 11: Thank You
John Nevares – TxDOT
Adam Kaliszewski – TxDOT
Natalia Ruiz Juri – UT Austin
Heidi Ross – UT Austin
Matt Miller – TTI
Debra Vermillion – HNTB
Rob Belarimo - HNTB