## Slide 1: A Comparison of Updated Four-Step Model to New Tour-Based Model

## Slide 2: Outline
What did we do?
Why did we do it?
Why not “go for broke” (full ABM)
What structure was used?
Performance of the 2 models (daily traffic)
Time and dollar cost
Next steps

## Slide 3: 2016 Modeling Suite Updates
Travel DEMAND forecasts (PTV Visum / visem)
Four-Step Travel Model (Updated to 2015 Base Year) PTV
Tour-Based Travel Model (2015 Base Year)
Synthetic population Generation
PopGen2
Socioeconomic forecasts
Cloud-Based UrbanSim
Notes: In 2016 as the agency planned a 2015 update to the base year, staff wanted to stand up a tour-based 2015 and compare it to a four-step version of the same year. We had the software to do just that.

## Slide 4: Tour-Based Model
Why a Tour-Based Model?
PPACG’s Four-Step Model lacks detail and fidelity to support planning roles and responsibilities. The current trips-based model:
Does not account for trip interdependencies – models only discrete one-way trips
Lacks detail needed to evaluate travel behavior of individuals – individuals within households are modeled as groups with homogeneous travel behavior
Is relatively insensitive to time-of-day – only eight time-of-day slices are modeled
Understates the role of accessibility – doesn’t capture travel decisions made based on accessibility
Notes: For the usual reasons.

## Slide 5: Tour-Based Model
Why Not a Full Activity-Based Model?
Migration to a full ABM was not a “good fit” for PPACG in the near term primarily due to resource constraints. Factors weighing against near-term implementation of a full ABM included:
Initial Development Cost – typical model costs $1M to $1.4M
Technical Issues – run times, greater data requirements, inconsistency of outputs, model accessibility for external users
Staffing and Training – modeling staff of one, potential for staff turn-over, staff knowledge base
Institutional Issues – potential sensitivity to changing the status quo
Notes: Time and money costs for ABM were prohibitive

## Slide 6: Tour-Based Model
If Not an ABM, What Then?
A tour-based model offered PPACG a “right-sized”, incremental step toward ABM functionality. Cost effective development of the new model was accomplished by:
Leveraging resources – funding and agency staff resources
Using a blended team – to staff and expedite model development, while building agency staff capability/knowledge base
Preserving model compatibility/continuity – networks and zonal data were updated concurrently for the two models
Developing comprehensive documentation – technical methodology report, training materials, and user guide
Notes: PTV software provided a “bridge” product

## Slide 7: Model Development Approach
Following A Different Path
Rather than upfront development or “transfer and refine” implementation, PPACG chose to use an adapted incremental implementation approach:
First step in path to a full ABM –
Built on current trips-based model structure and software platform to facilitate transition to new model.
Developed in parallel – the trips-based model was maintained as the “official model” to support transition and external users.
Both models used the 2010 Front Range CO household travel survey.
Notes: Keeping the baby and the bath water.

## Slide 8: Tour-Based Model Structure
Tour-Based Model:
Retains current software – implements a tour-based add-on module (VISEM); only synthetic population generation (PopGen2) is an external data/process. A combination of python scripts and built-in procedures are used, all within VISUM.
Focuses on essential upgrade – addition of tour generation model.
Retains some trips-based model components – distribution parameters, mode choice coefficients, transit skimming and assignment, truck model and trip assignment were adapted and retained.
Uses matrix operations to convert retained components to tour-based format.

## Slide 9
Tour-Based Model – Overview of Methodology
Disaggregate simulation-based tour generation is combined with aggregate tour-based destination and mode choice
Synthetic Population (PopGen2)
Disaggregate person level tour frequency choice
Tour type / stop frequency choice at zone level by person type
Aggregate destination/mode choice by person/tour type
Work based sub-tour using work destination as control total
Number of work-based sub-tours constrained to work destinations
Tour-based model- synthetic population- legacy trips-based model

## Slide 10: Tour-Based Model Components
Person Types – 8 types: Non-worker, senior, 3 students levels 3 worker income levels.
Activity Codes – 5 codes: home, other, school, work and stop (end). Activities are classified as home or non-home.
Tour types – 29 skeletal tour type combinations.
Time periods – 24 one-hour periods
Verification of trip tour rates done against Columbus OH and Phoenix AZ

## Slide 11: Four-Step Model Validation
2015 Validation: R2=0.93
%RMSE=31

## Slide 12: Tour-Based Model – Model Validation
2015 Validation: R2=0.9; %RMSE=25

## Slide 13: Tour-Based Model – Facts & Dimensions
How the TOUR-BASED Model Measures UP
Hardware – Standard laptop computer (workstation specifications desirable)
Software – PTV VISUM with tour-based add-on module
Run time – shorter than trips-based model, < 3 hours
VISUM version (scenario) size on disk – < 1GB
Development timeframe – beta version three months
Development cost – $210K

## Slide 14: Next Steps
PPACG has set the tour-based model as their official model!
Continue collaborative model development & application
Improve truck models

## Slide 15: Questions?