## Slide 1
Toll Optimization Algorithm for Evaluating Road Pricing Scenarios: Application to SacSim
June 4, 2019
Albab Noor, Joel Freedman, Mark Bradley (RSG)
Kyle Shipley, Yanmei Ou, Bruce Griesenbeck (SACOG)

## Slide 2: Road Pricing
Manage Congestion
Generate Revenue

## Slide 3: Network Coding
TOLLID = 1
GPID = 1
GENERAL PURPOSE LANES
HIGH OCCUPANCY TOLL (HOT) LANE
Travel time (Toll lane)
Travel time (GP lane)
Time Savings = Travel time (Toll lane) - Travel time (GP lane)

## Slide 4: Algorithm
Start
Toll
V/C > MAX V/C
Highway Assignment
New Toll = Value of Time * Time Savings
New Toll = Current Toll * Increment Factor
Toll Change < Conv. Criteria
Toll Change < Conv. Criteria
End
NO
YES
YES
YES
NO
NO

## Slide 5: Toll Optimization Loops in AM Peak Period 3 (9 AM – 10 AM)
 | Segment | HOT Time | GP Time | Time Savings | VOT Toll | Max V/C |  | DA | S2 | S3 | CV
Loop 1 | 1 | 3.21 | 3.33 | 0.12 | 0.04 | 0.79 |  | 0.11 | 0 | 0 | 0.16
 | 2 | 3.33 | 3.56 | 0.24 | 0.07 | 0.69 |  | 0.11 | 0 | 0 | 0.16
 | 3 | 4.78 | 6.07 | 1.29 | 0.38 | 0.79 |  | 0.61 | 0 | 0 | 0.92
 | 4 | 4.09 | 4.24 | 0.15 | 0.04 | 0.76 |  | 0.11 | 0 | 0 | 0.16
Loop 2 | 1 | 3.2 | 3.35 | 0.15 | 0.04 | 0.79 |  | 0.11 | 0 | 0 | 0.16
 | 2 | 3.33 | 3.56 | 0.24 | 0.07 | 0.7 |  | 0.11 | 0 | 0 | 0.16
 | 3 | 4.9 | 5.85 | 0.95 | 0.28 | 0.85 |  | 0.92 | 0 | 0 | 1.37
 | 4 | 4.07 | 4.25 | 0.18 | 0.05 | 0.74 |  | 0.11 | 0 | 0 | 0.16

## Slide 6: Volume after Loop 5 in AM Peak Period 3 (9 AM – 10 AM)
 | Segments | DA | CV2 | CV3 | S2 | S3
Low VOT | 1 | 0 | 0 | 0 | 219 | 75
 | 2 | 0 | 0 | 0 | 145 | 49
 | 3 | 0 | 0 | 0 | 257 | 89
 | 4 | 0 | 0 | 0 | 236 | 79
Med VOT | 1 | 33 | 5 | 1 | 346 | 149
 | 2 | 0 | 0 | 0 | 207 | 89
 | 3 | 24 | 4 | 1 | 348 | 152
 | 4 | 0 | 0 | 0 | 272 | 122
High VOT | 1 | 231 | 90 | 3 | 220 | 129
 | 2 | 281 | 277 | 17 | 106 | 65
 | 3 | 211 | 91 | 2 | 207 | 126
 | 4 | 210 | 232 | 1 | 141 | 90

## Slide 7: Application: Scenarios 2035

## Slide 8: Range of Results for Pricing Tests

## Slide 9: Conclusion
Enhancements made to the model allow the user to evaluate different road pricing scenarios
The user has control over which sections of which roadway to toll, set the initial, minimum, and maximum tolls for each segment
The user can estimate revenues and time savings that can be generated from different pricing scenarios
Disaggregate results from the ABM can be used for cost-benefit/equity analyses.

## Slide 10
ALBAB NOOR
ANALYST
albab.noor@rsginc.com
KYLE SHIPLEY
ANALYST (SACOG)
kshipley@sacog.org