## Slide 1
Scenario Modeling of CAVs with Trip-Based Models
Vince Bernardin, PhD
June 3, 2019

## Slide 2
All models are wrong, but some are useful.
– George Box
famous statistician

## Slide 3: How can trip-based models be useful in planning for CAVs?
Scenario Planning
  structured way for organizations to think about the future using a limited number of scenarios (e.g., best case, worst case, most likely, etc.)
Exploratory Modeling Analysis (EMA)
  simultaneously vary input assumptions across a wide range of future scenarios along key dimensions of uncertainty
  to explore potential outcomes, find critical input assumptions, and identify future policy directions likely to be robust in the face of “deep uncertainty”

## Slide 4: Jacksonville EMA Study
Combined ABM-DTA model
Factors explored
  Level of AV ownership among households
  Level of paid rideshare use and corresponding changes in auto ownership
  Amount of dedicated lanes & smart signals
  Level of vehicle automation
Best case: no CAVs
Even without ZOVs, demand increases more than capacity

## Slide 5
A Trip-Based Framework for CAVs

## Slide 6: The New Michigan Statewide Model
One of the longest traditions of statewide modeling in the country since early 1970s
Last major update was mid 1990s
New model complete near the end of 2018
  Data-driven approach using AirSage & ATRI
  Advanced trip-based passenger modeling
    Linkage of HB & NHB, LD and Visitor trips
  Commodity-flow based freight modeling
  Summer model

## Slide 7: CAVs in Michigan
Home of the Auto Industry
  All auto-makers actively investing in CAV technology
Public-Private Partnerships
  Research rapidly moving into reality
    U of M has been using autonomous shuttles for almost a year

## Slide 8: CAVs in Trip-Based Models
Lots of off-model / manual analysis
Michigan statewide model
New factors / market segments + ZOV step

## Slide 9: CAVs in Trip-Based MPO Models
Lots of off-model / manual analysis
Adapted Michigan framework
Charleston, Charlottesville, & Ann Arbor MPOs
EXTERNAL AND TRUCK TRIPS
ASSIGNMENT
Autonomous Vehicle Only Lanes / Facilities
Passenger Car Equivalencies for Autonomous Cars and Trucks in Mixed Traffic
RESIDENT INTERNAL PASSENGER TRIPS
AUTO OWNERSHIP
Overall Ownership Level
Split of Vehicles between CAV vs. Conventional
DESTINATION CHOICE
Adjust Trip Lengths by CAV ownership
ZOV GENERATION
HH CAV to Family
HH CAV to Home
HH CAV to Free Parking
HH CAV to Circulate
MaaS CAV to Next Pickup
MaaS CAV to Depot
INDUCED TRIPS
EE & EI/IE Scaling Factors
SUT Scaling Factor
MUT Scaling Factor
INDUCED TRIPS
Adjust Trip Rates by Seniors, Children, Autos
MODE CHOICE
Add MaaS modes
Add CAV / Conv Submodes
TIME OF DAY
Ext Diurnal Distributions
Trk Diurnal Distributions

## Slide 10: Model Segmentation
NON-WORK ACTIVITIES SEGMENTED BY DURATION
  Less than 30 min (won’t send vehicle home)
  Greater than 30 min (might send vehicle home)
VEHICLE OWNERSHIP
  No vehicles
  Vehicles < Adults
    Without CAV
    With CAV
  Vehicles ≥ Adults
    Without CAV
    With CAV

## Slide 11
EXTERNAL AND TRUCK TRIPS
ASSIGNMENT
Autonomous Vehicle Only Lanes / Facilities
Passenger Car Equivalencies for Autonomous Cars and Trucks in Mixed Traffic
RESIDENT INTERNAL PASSENGER TRIPS
AUTO OWNERSHIP
Overall Ownership Level
Split of Vehicles between CAV vs. Conventional
DESTINATION CHOICE
Adjust Trip Lengths by CAV ownership
ZOV GENERATION
HH CAV to Family
HH CAV to Home
HH CAV to Free Parking
HH CAV to Circulate
MaaS CAV to Next Pickup
MaaS CAV to Depot
INDUCED TRIPS
EE & EI/IE Scaling Factors
SUT Scaling Factor
MUT Scaling Factor
INDUCED TRIPS
Adjust Trip Rates by Seniors, Children, Autos
MODE CHOICE
Add MaaS modes
Add CAV / Conv. Submodes
TIME OF DAY
Ext Diurnal Distributions
Trk Diurnal Distributions

## Slide 12: Auto Ownership
Subdivide HH autos into conventional and CAV by income
Decrease overall ownership

## Slide 13
EXTERNAL AND TRUCK TRIPS
ASSIGNMENT
Autonomous Vehicle Only Lanes / Facilities
Passenger Car Equivalencies for Autonomous Cars and Trucks in Mixed Traffic
RESIDENT INTERNAL PASSENGER TRIPS
AUTO OWNERSHIP
Overall Ownership Level
Split of Vehicles between CAV vs. Conventional
DESTINATION CHOICE
Adjust Trip Lengths by CAV ownership
ZOV GENERATION
HH CAV to Family
HH CAV to Home
HH CAV to Free Parking
HH CAV to Circulate
MaaS CAV to Next Pickup
MaaS CAV to Depot
INDUCED TRIPS
EE & EI/IE Scaling Factors
SUT Scaling Factor
MUT Scaling Factor
INDUCED TRIPS
Adjust Trip Rates by Seniors, Children, Autos
MODE CHOICE
Add MaaS modes
Add CAV / Conv. Submodes
TIME OF DAY
Ext Diurnal Distributions
Trk Diurnal Distributions

## Slide 14: Trip Generation
Scale up trips to represent induced demand
Largest increases to households with:
  Disabled
  Seniors
  Children
More long distance / external trips from reduced lodging cost?
[Also, careful of trip rates by vehicle ownership]
Source: Jalopnik.com

## Slide 15
EXTERNAL AND TRUCK TRIPS
ASSIGNMENT
Autonomous Vehicle Only Lanes / Facilities
Passenger Car Equivalencies for Autonomous Cars and Trucks in Mixed Traffic
RESIDENT INTERNAL PASSENGER TRIPS
AUTO OWNERSHIP
Overall Ownership Level
Split of Vehicles between CAV vs. Conventional
DESTINATION CHOICE
Adjust Trip Lengths by CAV ownership
ZOV GENERATION
HH CAV to Family
HH CAV to Home
HH CAV to Free Parking
HH CAV to Circulate
MaaS CAV to Next Pickup
MaaS CAV to Depot
INDUCED TRIPS
EE & EI/IE Scaling Factors
SUT Scaling Factor
MUT Scaling Factor
INDUCED TRIPS
Adjust Trip Rates by Seniors, Children, Autos
MODE CHOICE
Add MaaS modes
Add CAV / Conv. Submodes
TIME OF DAY
Ext Diurnal Distributions
Trk Diurnal Distributions

## Slide 16: Trip Distribution
Passengers may be willing to travel farther since time in CAVs can be used positively for working, relaxing, sleeping, etc.
User can factor down traveler sensitivity to travel time / impedance

## Slide 17
EXTERNAL AND TRUCK TRIPS
ASSIGNMENT
Autonomous Vehicle Only Lanes / Facilities
Passenger Car Equivalencies for Autonomous Cars and Trucks in Mixed Traffic
RESIDENT INTERNAL PASSENGER TRIPS
AUTO OWNERSHIP
Overall Ownership Level
Split of Vehicles between CAV vs. Conventional
DESTINATION CHOICE
Adjust Trip Lengths by CAV ownership
ZOV GENERATION
HH CAV to Family
HH CAV to Home
HH CAV to Free Parking
HH CAV to Circulate
MaaS CAV to Next Pickup
MaaS CAV to Depot
INDUCED TRIPS
EE & EI/IE Scaling Factors
SUT Scaling Factor
MUT Scaling Factor
INDUCED TRIPS
Adjust Trip Rates by Seniors, Children, Autos
MODE CHOICE
Add MaaS modes
Add CAV / Conv. Submodes
TIME OF DAY
Ext Diurnal Distributions
Trk Diurnal Distributions

## Slide 18: Mode Choice
Add Taxi / TNC mode
Decrease cost
Vary occupancy
Source: Futurism.com
Notes: This slide is more for MPO models

## Slide 19: Mode Choice
Add MaaS mode
Add CAV / Conventional Submodes
Person Trips
Private Auto
MaaS
Transit
Non-Motor
SOV
HOV2
HOV3
CAV
Cnv
CAV
Cnv
CAV
Cnv
SOV
HOV2
HOV3
CAV
CAV
Cnv
CAV
Cnv
Walk
MaaS
Drive
CAV
Cnv
CAV
Cnv
Walk
Bike
Notes: This slide is more for MPO models

## Slide 20
EXTERNAL AND TRUCK TRIPS
ASSIGNMENT
Autonomous Vehicle Only Lanes / Facilities
Passenger Car Equivalencies for Autonomous Cars and Trucks in Mixed Traffic
RESIDENT INTERNAL PASSENGER TRIPS
AUTO OWNERSHIP
Overall Ownership Level
Split of Vehicles between CAV vs. Conventional
DESTINATION CHOICE
Adjust Trip Lengths by CAV ownership
ZOV GENERATION
HH CAV to Family
HH CAV to Home
HH CAV to Free Parking
HH CAV to Circulate
MaaS CAV to Next Pickup
MaaS CAV to Depot
INDUCED TRIPS
EE & EI/IE Scaling Factors
SUT Scaling Factor
MUT Scaling Factor
INDUCED TRIPS
Adjust Trip Rates by Seniors, Children, Autos
MODE CHOICE
Add MaaS modes
Add CAV / Conv. Submodes
TIME OF DAY
Ext Diurnal Distributions
Trk Diurnal Distributions

## Slide 21: Long-Distance & Trucks
Long distance travelers may use sleeping hours to travel
Source: theautofuture.com
There may be more long distance (external) trips as the cost of travel is reduced
Trucks / long distance travelers may shift to nighttime hours to avoid congestion

## Slide 22
EXTERNAL AND TRUCK TRIPS
ASSIGNMENT
Autonomous Vehicle Only Lanes / Facilities
Passenger Car Equivalencies for Autonomous Cars and Trucks in Mixed Traffic
RESIDENT INTERNAL PASSENGER TRIPS
AUTO OWNERSHIP
Overall Ownership Level
Split of Vehicles between CAV vs. Conventional
DESTINATION CHOICE
Adjust Trip Lengths by CAV ownership
ZOV GENERATION
HH CAV to Family
HH CAV to Home
HH CAV to Free Parking
HH CAV to Circulate
MaaS CAV to Next Pickup
MaaS CAV to Depot
INDUCED TRIPS
EE & EI/IE Scaling Factors
SUT Scaling Factor
MUT Scaling Factor
INDUCED TRIPS
Adjust Trip Rates by Seniors, Children, Autos
MODE CHOICE
Add MaaS modes
Add CAV / Conv. Submodes
TIME OF DAY
Ext Diurnal Distributions
Trk Diurnal Distributions

## Slide 23: Deadheading / ZOVs
Types of ZOV trips
  Private CAVs
    for car sharing among household members (1)
    to avoid paid parking
      by parking at home (2)
      by parking elsewhere (3)
      by circulating instead of parking (4)
  Shared CAVs
    for passenger pick-up/drop-off (5)
    to/from depots (6) (for re-charging / demand response)
Source: driverlesstransportation.com

## Slide 24: Private CAV ZOV Modeling Methods
for car sharing among household members
  invert asserted percentage of Os & Ds, gravity model
to avoid paid parking by parking at home
  invert asserted percentage of HB trip ODs for pay TAZs
to avoid paid parking by parking elsewhere
  create trips between pay TAZ & nearest non-pay TAZs as a function of long Ds at pay TAZ
to avoid paid parking by circulating instead of parking
  after assignment, factor up volumes on non-freeway links within buffer of pay TAZ based on short stops

## Slide 25: Shared CAV ZOV Modeling Methods
for passenger pick-up/drop-off
  invert all passenger Os & Ds; gravity model
to/from depots (for re-charging / demand response)
  assert depot TAZs with capacities; generate trips by min(difference in demand between periods, charging requirement assumption); gravity between shared CAV Os & Ds and depot TAZ

## Slide 26
EXTERNAL AND TRUCK TRIPS
ASSIGNMENT
Autonomous Vehicle Only Lanes / Facilities
Passenger Car Equivalencies for Autonomous Cars and Trucks in Mixed Traffic
RESIDENT INTERNAL PASSENGER TRIPS
AUTO OWNERSHIP
Overall Ownership Level
Split of Vehicles between CAV vs. Conventional
DESTINATION CHOICE
Adjust Trip Lengths by CAV ownership
ZOV GENERATION
HH CAV to Family
HH CAV to Home
HH CAV to Free Parking
HH CAV to Circulate
MaaS CAV to Next Pickup
MaaS CAV to Depot
INDUCED TRIPS
EE & EI/IE Scaling Factors
SUT Scaling Factor
MUT Scaling Factor
INDUCED TRIPS
Adjust Trip Rates by Seniors, Children, Autos
MODE CHOICE
Add MaaS modes
Add CAV / Conv. Submodes
TIME OF DAY
Ext Diurnal Distributions
Trk Diurnal Distributions

## Slide 27: Assignment
Separate autonomous and conventional vehicle classes
User option to have dedicated CAV-only facilities/lanes and assert high capacities and higher speeds
User option to assert different capacity consumption in mixed traffic (through PCE factor)

## Slide 28
Scenario Planning Example

## Slide 29: BURLINGTON, VT Scenario Planning
Intended to start a conversation about future transportation and traffic implications of the impending CAV future for LRTP
Not used in selecting projects
Two scenarios
  80% CAV, 50% shared, base occupancy
  100% CAV, 65% shared, higher occupancy

## Slide 30: BURLINGTON, VT Scenario Assumptions
5% more HBO for induced person trips
No temporal or destination choice changes
All ZOV types except intra-household sharing
Generous increased capacity assumptions
  Doubling of freeway capacity for 80% scenario
  Tripling of freeway and 50% increase of arterial capacity for 100% scenario

## Slide 31: BURLINGTON, VT Scenario Assumptions
Pay Parking TAZ
Depot TAZ

## Slide 32: BURLINGTON, VT Scenario Results

## Slide 33
Conclusions

## Slide 34: Parting Thoughts
Trip-based models can be enhanced to capture almost (but not) all dimensions of uncertainty about CAVs
  Add adjustments to all steps
  Add taxi/TNC mode
  Add special ZOV components
They can NOT tell us what will happen
They CAN help us understand
  the range of possible futures
  the relative importance of different factors
  the robustness of policies / investments

## Slide 35
VINCE BERNARDIN, PHD
DIRECTOR
vince.bernardin@rsginc.com 812.200.2351