## Slide 1
An Agile, Data-Driven Ensemble Modeling Framework for the ILSTDM
Vince Bernardin, PhD, Steve Tuttle, Sheng Chen
June 3, 2019

## Slide 2: Illinois is investing in a Statewide Model
AVERAGE 10-YR COST OF A STATEWIDE MODEL FOR A “LARGE” STATE
  Enhanced Trip-Based Model: $2,240,000
  Activity-Based Model: $5,690,000
ILLINOIS INVESTMENT IN A STATEWIDE MODEL
  Initial 3-Year Investment: $1,632,840
Average figures and graph from NCHRP 08-36 Task 137 Draft Final Report
IL

## Slide 3: Status
Network and Zone Development Tasks Now Complete
On-going
  Development of Future Year Scenarios
  Development of Freight and Passenger Demand Models

## Slide 4: Building on Existing Models
ILSTDM TAZ Inside Illinois
Area | Total TAZs
CMAP Area | 1,752
MPO Area | 1,252
Rural Area | 1,362
Total (Inside Illinois) | 4,366

## Slide 5: PHASE 1
TIME: Aug 2019
PRODUCT: ILSTDM v1 will have fixed base and future year demand (OD tables) that can be assigned to the statewide highway network for different highway network investment scenarios

## Slide 6: Phase 1 Future Demand
Pivot off of Base OD Data
MPOs – MPO Model OD Growth
  From future E+C trip tables
Rural – Quick Response

## Slide 7: PHASE 2
TIME: Nov 2020
PRODUCT: ILSTDM v2 will have dynamic advanced trip-based passenger demand and commodity flow-based freight models as well as the original v1 demand

## Slide 8: 40 States Have Now Developed a Statewide Model!

## Slide 9
Model Framework

## Slide 10: A Phased, Modular, Data-Driven Ensemble Approach

## Slide 11
Key insight from machine learning:
Multiple models are better than one

## Slide 12: Ensemble Modeling & Forecasting
Combine multiple forecasts into a “consensus” forecast via binding function
Works best with different (uncorrelated) models
Can also “boost” with models in series
Has led to greater predictive validity (e.g., in meteorology, bioinformatics)
Ensemble Forecast of Hurricane Isaac - noaa.gov
Notes: DON’T have to throw out our models
AUGMENT existing models with new/more models

## Slide 13
All models are wrong, but some are useful.
– George Box
famous statistician

## Slide 14: Deep Thoughts…
Different models are wrong in different ways…
Being wrong in multiple ways allows you to better understand how you are wrong…
Multiple models are more useful…
Notes:   When you are wrong in only one way, you have no sense of how you are wrong.

## Slide 15: An Old Lesson
“There is no single approach to travel forecasting or set of procedures that is ‘correct’ for all applications.”
– TRB Special Report 288
Notes:   When this was written, I think everyone interpreted this to mean that some agencies would have trip-based models and some would have activity-based models.
  Perhaps, the deeper truth is that one model is not enough for any agency.

## Slide 16: Top 25 MSAs – Using Multiple Models Already
Notes: Apologize if any of this is not current / accurate – limited fact-checking
Roughly half of agencies with ABMs have two models (TBM & ABM)

## Slide 17: Updating Base without Recalibration
Base ODs can be updated without recalibrating demand models

## Slide 18: Addressing New Changing Behaviors/Patterns without System Recalibration
Shopping to Delivery Boosting Model
Forecast A’
Forecast B’
Adding new modules for new functionality instead of rebuilding

## Slide 19
Passive Data Development

## Slide 20: Leveraging Big Data
General Population Movement Data
  5.5M Monthly Active Users
    42% of population
  1M Daily Active Users
    7.6% of population
Truck GPS Data
  820k Unique Trucks (US)
  700B annual sightings

## Slide 21: ATRI Dataset
>1 billion sightings, ~700,000 trucks
Time period | Trucks (raw) | Trucks (kept) | Pings (raw)
February 2018 | 183,176 | 151,671 | 295,534,447
May 2018 | 178,258 | 148,135 | 286,057,818
July 2018 | 178,171 | 149,211 | 305,602,323
October 2018 | 171,577 | 142,767 | 270,425,363
Total | 711,182 | 591,784 | 1,157,619,951

## Slide 22: ATRI Processing Results - Unexpanded
~6 million trips, ~360 million VMT overall
Time period | Unexpanded trip count | Distance (mi)
February 2018 | 1,419,789 | 87,443,217
May 2018 | 1,552,876 | 87,486,371
July 2018 | 1,452,520 | 93,530,117
October 2018 | 1,529,128 | 91,784,476
Total | 5,954,313 | 360,244,181

## Slide 23: ATRI Processing Results

## Slide 24: Intermediate Stop Filtering
Filtering stops for fuel, food, etc., necessary for understanding actual long-distance OD demand for both passenger and freight flows
Geofencing around gas stations / truck stops, etc.

## Slide 25: Intermediate Stop Filtering Results
16.4% of trips have at least one intermediate stop
Time period | Unexpanded trip count | Trips with 1+ intermediate stop
February 2018 | 1,419,789 | 243,426 (17.1%)
May 2018 | 1,552,876 | 237,262 (15.3%)
July 2018 | 1,452,520 | 254,722 (17.5%)
October 2018 | 1,529,128 | 241,284 (15.8%)
Total | 5,954,313 | 976,694 (16.4%)

## Slide 26: Stop Density Reasonableness Checks

## Slide 27: Circle Interchange Bottleneck – 1 day

## Slide 28: Circle Interchange – OD Patterns Served

## Slide 29: Graph Theory for Residence, Work, Depot Imputation – Basis for Fusion
Topological centrality as primary indicator, overnighting secondary – higher confidence, multi-point fusion

## Slide 30
Conclusion

## Slide 31: Advantages of a Data-Driven Ensemble Modeling
Improved predictive accuracy
  Based on theory and application to other domains
  Built-in cross-validation
Leverages passive data
Easier to maintain / update
  New ODs, SE data & Projects = New Base Year
  No need for system recalibration
    Even functionality can be added without calibration
  Model can be updated every year
Less waste
  Reuse of early simpler model versions

## Slide 32
VINCE BERNARDIN, PHD
DIRECTOR, RSG
vince.bernardin@rsginc.com 812.200.2351
SHENG CHEN
ILLINOIS DOT
sheng.chen@Illinois.gov 312.793.1491