## Slide 1: Regional Dynamic Traffic Assignment with Feedback
Norm Marshall, President
Smart Mobility Inc.
nmarshall@smartmobility.com

## Slide 2: Overview
Why replace Static Traffic Assignment (STA) with Dynamic Traffic Assignment (DTA)?
Why regional DTA?
Why regional DTA with feedback?
Is regional DTA with feedback practical today?
  DTA Software
  Data
  Computer hardware
  Implementation aids

## Slide 3: Why replace STA with DTA?
Speed-flow data from I-405 in Orange County California
STA forecasts for I-405
STA fails to constrain traffic to capacity
STA over-assigns
  Freeways
  Ramps
  Upstream and downstream segments
Extreme case but over-capacity horizon year assignments are very common

## Slide 4: Why Regional DTA?
Why not STA subarea trip tables?
Not capacity constrained
Volumes unrealistic as inputs either to DTA or microsimulation
Why not synthetic subarea trip tables
Adds cost and complications
No good way of transforming into future subarea trip tables

## Slide 5: Why Regional DTA with Feedback?
Why feedback
Trip distribution/destination choice - travelers decide where to go based on expected travel times –
Assignment - Models calculate travel times from the choices travelers made
Achieving consistency between these model steps requires feedback iterations
Feedback has been recommended practice for over 20 years
Why feedback with DTA times
STA travel times inaccurate
  Over-assigned links
  Unrealistically long times on some segments
  Unrealistically short times on some segments (especially upstream of bottlenecks)
  Will not constrain subarea trip tables to capacity

## Slide 6: Is Regional DTA with Feedback Practical Today?
DTA software
DTALite is well suited to regional applications
An open-source mesoscopic DTA simulation package …
has been developed to provide … a theoretically rigorous and computationally efficient traffic network modeling tool …
uses a queue-based approach (Zhou and Taylor 2014)
Xuesong Zhou of Arizona State University enthusiastically supports these applications and is working on DTALite enhancements

## Slide 7: Is Regional DTA with Feedback Practical Today?
Data Requirements
DTALite requires only the same inputs as STA
  Lanes
  Free-flow speed
  Roadway class

## Slide 8: Is Regional DTA with Feedback Practical Today?
Computer Hardware
Up to 1 million population:
  $5,000 Windows computer with 8 cores
  Portland Maine case study described in paper
More than 1 million population:
  “You’re going to need a bigger computer” – but on the same order of magnitude as the processing power that is being applied to Activity-Based Models in larger MPOs
  Hybrid DTA/STA subarea model
or

## Slide 9: Is Regional DTA with Feedback Practical Today?
Hybrid DTA/STA Subarea Model
Loudoun County VA (purple) within greater Washington DC model
DTA model includes
  All trips with origin or destination in purple area
  All trips in other colored areas except trips internal to that color
STA model of region
Both models run in feedback iterations
Travel time matrix composite of DTA times in subarea and STA time outside
Practical on 8-core $5,000 computer

## Slide 10: Is Regional DTA with Feedback Practical Today?
Implementation aids
I am developing and distributing open source Java programs to aid integration with commercial travel demand modeling software
Travel Demand Model
Java: convert network and trip tables
DTALite
Java: convert volumes and travel times