## Slide 1: Practical Population Synthesis Enhancements to Support Advanced and Activity-Based Travel Demand Models
Ramachandran Balakrishna
Srinivasan Sundaram
Caliper Corporation
2019 TRB Planning Applications Conference
Portland, OR
3rd June, 2019

## Slide 2: Outline
Population synthesis overview
Limitations in current methods
Proposed methodology
Solutions to practical (data) challenges
Illustrative results
Qualitative summary of results

## Slide 3: Population Synthesis Overview
Objective
  Enumerate a region’s households (HH) and constituent persons
    Forms base for advanced travel demand models
      Hybrid (trips/tours with some disaggregate aspects)
      Activity-Based Models (ABM)
  Inputs:
    Sample of HH and persons (e.g. ACS PUMS) with attributes
    Control totals of desired HH and person variables
      HH Size (1,2,3,4+), Income (Low,Med,Hi), Gender (M,F), …
      Usually at finer geography than the sample
  Outputs:
    HH and person tables that aggregate accurately to control totals

## Slide 4: Population Synthesis Overview
Examples of geographic layers

## Slide 5: Population Synthesis Overview
Typical synthesis steps
  Read (or estimate) weights for each HH in the sample
  Select a geographic resolution (e.g. blocks or zones)
  For each geographic element
    Assemble the control totals across variables of interest
    Estimate the number of each sample HH type to include
      By matching the HH control totals
      (e.g.) Iterative Proportional Fitting (IPF)
    Randomly draw from the sample to make up the required #HH
      Use weights to derive the sampling probabilities

## Slide 6: Population Synthesis Overview
Typical synthesis steps (contd.)
Nested IPF handles controls from different geographies
  (e.g.) blocks, block groups, zones, …
IPF: Scale rows and columns iteratively to match marginals

## Slide 7: Limitations in Current Methods
Methods have largely matched only HH control totals
  (e.g.) Size, auto ownership, income
  Person totals are left to chance, often fit poorly
    But are critical to person-level calculations like in ABMs
      (e.g.) Age, gender, work status, …
Fixes have been proposed and tried
  Optimization-based methods stay close to initial HH weights
    Biased starting weights persist into the synthesized outputs
  Modified heuristic methods have created new problems
    Sensitivity to sample data scarcity
    Long running times (several hours)

## Slide 8: Limitations in Current Methods
Iterative Proportional Updating (IPU) heuristic
  Joint distribution of all HH and person variables
    Exponential increase in number of columns
      (e.g.) 4 variables with 3 levels each = 81 columns
    Each sample HH contributes to a (small) number of columns
  Pros:
    Includes each sample HH’s contribution to person variables
    Simple: iteratively matches column totals like in IPF
  Cons:
    Fractionates sample records among large number of columns
      Resulting zero-cell, zero-marginal problems need heuristic fixes
    Impractical running times
      4 hours for 2088 block groups (quad-core proc.)[Ye et. al. (2009)]

## Slide 9: Proposed Methodology
Simplify the IPU survey incidence table
  Individually match each variable level, not their exhaustive combinations
    Zero-cell, zero-marginal instances much less likely
  Iterate between column totals like in traditional IPU

## Slide 10: Proposed Methodology
Integrated framework
Implemented as a general feature in TransCAD

## Slide 11: Proposed Methodology
Benefits of the new approach
  Jointly match both person and HH variables
  Improve robustness of estimation
  Allow HH weights to change for each geographic unit (e.g. block group)
  Highly efficient computations
  Approach can also be used to re-weigh HH surveys
    Treat entire region as one geographic unit
    Improve accuracy of trip-based models

## Slide 12: Solutions to Data Challenges
Inconsistencies between HH and person marginals
  Result in an infeasible mathematical problem
  Can match HH or person variables, but not both
Key issue: Large average HH sizes in the highest bins
Multi-HH need to be split for travel modeling purposes
  Corrections need to come from outside these datasets

## Slide 13: Solutions to Data Challenges
Database USA records
  Available for purchase
  Based on a variety of commercial sources including credit card transactions
  Contains detailed demographic information
    HH counting methods differ between Census, Database USA
      Multi-family HH correctly split into functional HH units
      Census: 820K, Database USA: 1.15 million
  Average 5+ HH size = 5.57
    Almost the same for two different states (Nevada, California)

## Slide 14: Solutions to Data Challenges
Correction method for marginals
  Retain the number of 5+ HH from Census
  Infer the 5+ HH population using Database USA average
  Compute “excess” population from the 5+ bin
  Reallocate the excess to smaller HH sizes
    In proportion to Census HH size distribution
  Use these new marginals in the synthesis

## Slide 15: Illustrative Results: Las Vegas, NV
Without IPU
With IPU

## Slide 16: Illustrative Results: Central Coast, CA
Without IPU
With IPU

## Slide 17: Qualitative Summary of Results
Modified IPU
  Corrects for systematic bias in person variables
    Expected to highly impact the outcomes of disaggregate models
      Daily household activity patterns
      Household interactions
  Features practical run times (10 minutes for Las Vegas)
  Provides solid platform for advanced travel demand models
Current work: Localizing the impacts of targeted changes to marginals