## Slide 1: Traffic and Revenue Forecasts for I-95 Express Lanes in South Florida
June 4, 2019
Phani Jammalamadaka, PE, PMP
Ozge Cavusoglu, PhD, PTP
Negaar Minaei

## Slide 2: Overview
Background
Travel Demand and Toll Diversion Modeling
Results

## Slide 3: 95-Express Lane Phases and Opening Dates
Phase 1
  stretches about 7 miles from the GGI to SR 112/SR 836.
  NB ELs have been in operation since December 2008 and the SB ELs since Jan 2010.
FDOT extended 95-Express into Broward County, known as Phase 2
  in operation since October, 2016.
Phase 3
  will open in sub-phases. All Phase 3 segments are planned to be open by July 2024.

## Slide 4: Current Project Configuration of 95-Express
HOV Lanes
I-395/
SR 836
Exit 2D/3A
I-195/
SR 112
Exit 4
62nd St.
Exit 6A
SR 934
(79th St.)
Exit 7
Rev. Dr.
A. Jackson Jr.
Blvd.
(95th St.)
Exit 8A
SR 924
(119th)
Exit 9
SR 860
(Miami Gardens Dr.)
Exit 14
Ives Dairy Rd.
(203rd St.)
Exit 16
SR 858
(Hallandale
Beach Blvd.)
Exit 18
SR 820
(Hollywood Blvd.)
Exit 20
69th
Exit 6B
SR 922
(125th)
Exit 10A
Golden Glades
Interchange
Exit 12A
SR 824
(Pembroke Rd.)
Exit 19
Miami-Dade Co.
Broward Co.
SR 822
(Sheridan St.)
Exit 21
SR 848
(Stirling Rd.)
Exit 22
SR 818
(Griffin Rd.)
Exit 23
I-595/
SR 862
Exit 24
SR 736
(Davie Blvd.)
Exit 26
SR 842
(Broward Blvd.)
Exit 27
SR 838
(Sunrise Blvd.)
Exit 29
SR 816
(Oakland
Park Blvd.)
Exit 31
SR 870
(Commercial Blvd.)
Exit 32
Cypress
Creek Rd.
Exit 33
SR 814
(Atlantic Blvd.)
Exit 36
Copans Rd.
Exit 38
SR 834
(Sample Rd.)
Exit 39
Park
& Ride
Match Line A
Match Line A
Segment 1
Segment 2
Segment 3
2
2
1
1
2
2
1
1
2
2
1
1
1
1
N
4
4
6
6
5
5
4
4
4
4
4
4
4
4
4
4
5
5
4
5
4
3
3
4
5
5
5
5
5
5
5
5
5
5
5
5
4
4
5
5
5
5
5
5
4
4
4
4
4
4
4
4
4
5
LEGEND
Segment 1
Segment 2
Segment 3
0
Number of Managed Lanes/HOV Lanes
Two Direction Toll Gantry
One Direction Toll Gantry
0
Number of General Purpose Lanes Auxiliary lanes
One Direction Data Gantry
Phase 2
Phase 1
Phase 3
Phase 2
I-75/
SR 869/
SW 10th
Exit 41
HOV Lanes
HOV Lanes
Match Line A

## Slide 5: 95-Express Segment 1 (Phase 1) Peak Period Toll Rate Trends
Source: FDOT SunGuide 95 Express Monthly Operations Reports
Chart: Average Peak Period Tolls
NB PM Peak Rates Frequently Hit Max Toll of $10.50
AM Peak - Southbound
PM Peak - Northbound

## Slide 6: Trend in Average Peak Period Speeds General Purpose (GP) Lanes 95-Express Phase 1 - 6-Month Moving Average
Chart: Speed (mph)
GP Lanes SB
GP Lanes NB
NB GP Lanes Before Express Lanes
Source: FDOT SunGuide 95 Express Monthly Operations Reports
2018
2016
2014
2013
2015
2017

## Slide 7: Trend in Average Peak Period Speeds Express Lanes 95-Express Phase 1 - 6-Month Moving Average
Chart: Speed (mph)
2016
2014
2013
2015
2017
2018
AM Peak - Southbound
PM Peak - Northbound
Target Minimum Express Lanes Speed
Threshold Speed for Minimum Toll Charge
Source: FDOT SunGuide 95 Express Monthly Operations Reports

## Slide 8: Travel Demand and Toll Diversion Modeling

## Slide 9: Express Lanes Time of Day (ELToD) Model Version 4
ELToD Model is a forecasting tool developed by the Florida’s Turnpike Enterprise (FTE) in collaboration with AECOM, RSG, and HNTB
Incorporates a Dynamic Traffic Assignment (DTA) Model
Predicts the share of express lanes traffic by utilizing a binary logit choice model, which includes value of time and value of reliability
Estimates the associated dynamic toll rates for the express lanes based on the defined toll pricing policy curves

## Slide 10: Adjusted Study Toll Pricing Curve Assumptions

## Slide 11: ELToD Model Features1
Toll Choice Model
  Decision making during trip via decision making nodes.
Dynamic Toll Rates for Express Lanes
  Static tolls used for toll facilities on the network.
15-minute Trip Tables
1 ELToD Model v2.1 User Guide and Documentation. Florida Department of Transportation (FDOT), March 2016.

## Slide 12: Perceived Time in ELToD Model
Perceived Time1: ELToD model takes into account perceived time of travelers.
  Max: defines the maximum travel time weight for the model.
  k: determines how rapidly the travel time weights increase as the V/C ratio approaches the midpoint value for each network link.
  v/c: V/C ratio for the Travel Time Weight is being calculated
  Mid: defines the V/C ratio at which the travel time weights reach their midpoint value.
1 ELToD Model v2.1 User Guide and Documentation. Florida Department of Transportation (FDOT), March 2016.
+1

## Slide 13: South Florida T&R Modeling Overview
ELToD v4 modeling platform
  Regional model – all study corridors in one network along with other Express Lanes (ELs) in South Florida
  Calibrated to reflect recent trends (2017, 2018, and 2019)
    Traffic, tolls, speeds, roadway capacities
    Extensive iterative regional and corridor level calibration
30-year T&R forecast
  Baseline Forecast
  Risk Adjusted Forecast using Monte-Carlo analysis
Planning Level T&R Study - not intended for use in support of bond financing

## Slide 14: Full-build Configuration of 95-Express
I-395/
SR 836
Exit 2D/3A
I-195/
SR 112
Exit 4
62nd St.
Exit 6A
SR 934
(79th St.)
Exit 7
Rev. Dr.
A. Jackson Jr.
Blvd.
(95th St.)
Exit 8A
SR 924
(119th)
Exit 9
SR 860
(Miami Gardens Dr.)
Exit 14
Ives Dairy Rd.
(203rd St.)
Exit 16
SR 858
(Hallandale
Beach Blvd.)
Exit 18
SR 820
(Hollywood Blvd.)
Exit 20
69th
Exit 6B
SR 922
(125th)
Exit 10A
Golden Glades
Interchange
Exit 12A
SR 824
(Pembroke Rd.)
Exit 19
Miami-Dade Co.
Broward Co.
SR 822
(Sheridan St.)
Exit 21
SR 848
(Stirling Rd.)
Exit 22
SR 818
(Griffin Rd.)
Exit 23
I-595/
SR 862
Exit 24
SR 736
(Davie Blvd.)
Exit 26
SR 842
(Broward Blvd.)
Exit 27
SR 838
(Sunrise Blvd.)
Exit 29
SR 816
(Oakland
Park Blvd.)
Exit 31
SR 870
(Commercial Blvd.)
Exit 32
Cypress
Creek Rd.
Exit 33
SR 814
(Atlantic Blvd.)
Exit 36
Copans Rd.
Exit 38
SR 834
(Sample Rd.)
Exit 39
I-75/
SR 869/
SW 10th
Exit 41
SR 810
(Hillsboro Blvd.)
Exit 42
Palmetto
Park Rd.
Exit 44
SR 794
(Yamato Rd.)
Exit 48
Congress Ave.
Exit 50
Linton Blvd.
Exit 51
SR 806
(Atlantic Ave.)
Exit 52
Park
& Ride
Match Line A
Match Line A
Match Line B
Match Line B
HOV Lanes
Segment 1
Segment 2
Segment 3
Segment 6
Segment 7
Segment 8
2
2
1
1
2
2
1
1
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
1
1
N
4
4
6
6
5
5
4
4
4
4
4
4
4
4
4
4
5
5
4
5
4
3
3
4
5
5
5
5
5
5
5
5
5
5
5
5
4
4
5
5
5
5
5
5
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
5
5
5
5
5
5
5
5
Phase 3B-1
Segment 11
SR 808
(Glades Rd.)
Exit 45
4
5
LEGEND
Segment 1
Segment 2
Segment 3
Segment 4
Segment 5
Segment 6
Segment 7
Segment 8
Segment 9
Segment 10
Segment 11
Segment 12
0
Number of Managed Lanes/HOV Lanes
Two Direction Toll Gantry
One Direction Toll Gantry
0
Number of General Purpose Lanes Auxiliary lanes
One Direction Data Gantry
Broward Co.
Palm Beach Co.
Segment 12
2
2
Segment 4
Segment 5
Phase 2
Phase 1
Turnpike ELs
Phase 3
Phase 2
Segment 9
Segment 10
Phase 3B-2
Phase 3C
Phase 3A
Phase 3A-1
Phase 3A-2
2
2
Turnpike ELs
2
2
SR 826 EW ELs
SR 826 EW ELs

## Slide 15: 2018 Study Methodology
Base year (2017) ELToD model calibration
  Reviewed hourly traffic counts on ramp and mainline locations from FDOT’s website; screenline counts were added
  Developed updated detailed count profile for 95-Express/595-Express (including detailed count patterns at GGI), and profile along I-75/SR 826
    Several iterations of Origin/Destination Matrix Estimation (ODME) and model calibration performed
      ODME included 8 network wide screenlines

## Slide 16: 2018 Study Methodology (Cont'd)
  24 different ELToD calibration runs
    Toll Constants at each Decision Making Node were updated for every 15-min for all model years.
    Toll Pricing Curves updated
    Speeds/capacities on arterials updated
    Capacities on general purpose lanes and express lanes updated
    PCE factor updated for trucks
    Dynamic Traffic Assignment (DTA) module update
  Reviewed 95-Express, 595-Express and 75-Express trends in terms of traffic, toll, revenue, and operations through April/May 2018

## Slide 17: 2018 Study Methodology (Cont'd)
Future Year models
  2018, 2019, 2021, 2023, 2024, 2028, 2030, 2035, and 2045
    2028 Model Year run with and without GGI improvements, including TPKE/SR 826 EW ELs
    2030 Model Year run with and without Sawgrass Express 10th St extension
  Base year trip table adjustments carried to future years
  Network updates to reflect latest phasing on 95-Express and 75-Express, and other ELs on the network (Turnpike, HEFT, Sawgrass)
  Post-processing adjustments were applied after performing reasonableness checks

## Slide 18: Results

## Slide 19: Calibration Results
Differences between corridor demand after ODME and after ELToD runs, which significantly impacted EL volumes. Screenline counts were added to ODME to solve this issue
Chart: I-75/SR 826 Corridor Latest ELToD Run
| 99613 | 100429 | 109050 | 106222 | 99557 | 99101 | 100146 | 104123 | 108319 | 97194 | 94449 | 94305 | 100010 | 102300 | 96844 | 98394 | 50684 | 57697 | 73854 | 70319 | 72470 | 69268 | 70736 | 62158 | 62867 | 59331 | 59142 | 71335 | 72014 | 74225 | 70834 | 73577 | 54280 | 47552
TOT VOL | 104357 | 101876 | 109497 | 108888 | 100764 | 99983 | 101615 | 104027 | 115249 | 103112 | 99828 | 100607 | 104814 | 101762 | 94869 | 96844 | 48926 | 57151 | 73319 | 71221 | 71659 | 69816 | 70724 | 62404 | 63329 | 63151 | 61298 | 72169 | 70164 | 70421 | 73345 | 74122 | 53429 | 44275
Chart: I-95 Corridor Latest ELToD Run
| 105210 | 124785 | 129078 | 132067 | 132452 | 132115 | 133598 | 126627 | 128325 | 129987 | 126478 | 126478 | 36640 | 42137 | 89358 | 103191 | 107299 | 113056 | 114366 | 120301 | 121331 | 122489 | 123526 | 109133 | 119817 | 81393 | 72191 | 84795 | 75411 | 67374 | 113929 | 131236 | 122668 | 117508 | 105365 | 101604 | 101652 | 87801 | 96436.548984706416 | 86481.789707300413 | 84551 | 87920 | 87835 | 86464
TOT VOL | 107796 | 121315 | 122334 | 125707 | 127865 | 130469 | 130142 | 117796 | 124574 | 124021 | 121300 | 121132 | 30723 | 37750 | 90369 | 98771 | 106234 | 110265 | 109247 | 114058 | 116816 | 118658 | 118704 | 104489 | 117767 | 81883 | 71296 | 84472 | 75476 | 67863 | 106199 | 126464 | 119950 | 112837 | 101775 | 99944 | 98858 | 92066 | 94722 | 91567 | 89219 | 92046 | 90656 | 83430
Chart: I-595 Corridor Latest ELToD Run
| 32085 | 16301 | 72076 | 83432 | 74550 | 67490 | 81150 | 87460 | 65849 | 75458 | 106884 | 71412 | 92832 | 89368 | 80421 | 85686 | 77963 | 63780 | 75660 | 57244 | 70673 | 54537 | 60490
TOT VOL | 33420 | 18004 | 71807 | 81760 | 71998 | 62975 | 73264 | 82908 | 62385 | 71609 | 101087 | 75630 | 91085 | 88200 | 79438 | 84728 | 76618 | 62372 | 71587 | 53999 | 66373 | 53335 | 60331

## Slide 20: Other Express Lanes in South Florida
Modeled by 2028
  Golden Glades Interchange (GGI) Improvements
  HEFT Express Lanes
  Sawgrass Express Lanes
  SR 826 Express Lanes East West Extension
  Turnpike Express Lanes – GGI to Griffin Rd and Atlantic Blvd. to Sawgrass Expressway
  Modeled by 2030
    Sawgrass Express Lanes SW 10th St. Extension
    Turnpike Express Lanes - Sawgrass Expressway to Hypoluxo Rd.

## Slide 21: Comparative Results for Model Year 2028
95-Express Phase 1 NB
  Due to improvement of GGI bottleneck, increase in traffic but decrease in revenue (as tolls required to maintain free-flow speeds decrease)
  595-Express and 75-Express
    Drop in traffic and revenue due to opening of SR-826 E/W EL and HEFT EL
  Palmetto/SR-826 Express
    Increase in traffic and revenue due to opening of SR-826 E/W EL
LEGEND
Traffic Decrease
Revenue Decrease
Traffic Increase
Revenue Increase
2028 Express Lanes Improvements

## Slide 22: Thank you!