## Slide 1: Using Big Data in Transit Market Research - Findings from Los Angeles
June 4, 2019
Transportation Planning Applications Conference
Presented at:

## Slide 2: Background & Study Motivation
LA Metro is the third largest transit agency in the US with over 1.2 million boardings/day
  140 operational bus lines
  6 rail lines
  27 regional affiliate bus services
Bus service has not changed in the past 25+ years – activity locations and travel markets have changed considerably

## Slide 3: Understanding the Transit Market
Who are our riders? Define customer segments
Where and why do these riders travel? Profile travel markets by geography, purpose, time-of-day, distance
What are the transit market shares? Comprehensive performance indicator by inferring overall travel using granular location-based services data
How competitive is transit w.r.t auto in terms of travel time? Tipping point where transit market shares drop
Mine rich, voluminous smart farecard data and perform advanced analytics to answer key questions:

## Slide 4: Measuring Transit Competitiveness
Cell phone data to explain TOTAL
travel market
TAP card data to explain TRANSIT travel market
Trips
Metro Open Trip Planner
Google
Traffic API
Transit Path & Travel Times
Highway Travel Times
Transit Competitiveness

## Slide 5: Transit Customer Segments
Frequent
Infrequent
Occasional
>150 Transactions
50 – 150 Transactions
10 – 50 Transactions
<10 Transactions
TOTAL
Usage Frequency
152,532
248,851
# of Farecards
5%
9%
552,374
1,905,501
2,859,258
12,585,194
5,614,072
83,908,041
20%
66%
100%
100%
7%
15%
43,680,893
22,027,882
Count of Boardings
52%
26%

## Slide 6: Competitiveness of Relative Travel Times
Chart: 
| No transit Path | 0 - 1 | 1 - 1.25 | 1.25 - 1.50 | 1.50 - 1.75 | 1.75 - 2.00 | 2.00 - 2.25 | 2.25 - 2.50 | 2.50 - 2.75 | 2.75 - 3 | 3.00 - 3.25 | 3.25 - 3.50 | 3.50 - 3.75 | 3.75 - 4.00 | 4.00 - 4.25 | 4.25 - 4.50 | 4.50 - 4.75 | 4.75 - 5.00 | 5 +
% Mkt Share (incl. walk only) | 0.13214 | 0.12814 | 0.096171 | 0.071565 | 0.053798 | 0.039271 | 0.02845 | 0.020788 | 0.01581 | 0.012553 | 0.010301 | 0.0084427 | 0.0073396 | 0.0064816 | 0.0059128 | 0.0054792 | 0.0053056 | 0.0057238
1-1.25
1.5-1.75
2-2.25
2.5-2.75
3-3.25
3.5-3.75
4-4.25
4.5-4.75
5-5.25
0 – 1
2%
6%
4%
8%
10%
12%
14%
Transit to Drive Time Ratio
Transit Market Share
When driving
is over twice as fast, transit is less competitive

## Slide 7: Transit service designed around longer commute trips
Short trips represent our largest potential market
Trip Distance
Transit Share
16%
46%
22%
7%
6%
5%
4%
3%
2%
1%
0-1 mi
1-5 mi
5-10 mi
10+ mi
% of total trips
16%

## Slide 8: Key Takeaways
Other Trips
60% of all trips
2% transit market share
24% of all trips
4% transit market share
All Day
Commute Trips
8% of all trips
5% transit market share
8% of all trips
9% transit market share
Short Distance
Long Distance
Frequency
Peak Hour
Speed
Metro is successful here and should continue to focus on this travel market.
Metro is not competing well in our biggest potential market and needs to rethink service to better capture short trips.

## Slide 9: Transit Market Profiles (Strategic Planning)

## Slide 10
Transit Market Insights Dashboard
1
2
3
5
4
1
Spatial and Trip Characteristics Filter
2
Travel Market Overview
3
Spatial Visualization of OD
4
Transit Market Profiles
5
Market Performance segmented along various dimensions

## Slide 11: Impacts
At the forefront of innovation: What transit agencies can get from big data
Understanding total travel vs transit market share and travel time competitiveness are indicators of transit success
Data driven toolkit to quantify market performance can be updated and maintained for future adjustments beyond initial study
  Before and after-analysis
  Service planning
  Alternative Analysis

## Slide 12
Sylmar/San Fernando
Sunland/La Crescenta
60%
60% of trips occur within the area
27% of trips are to the Valley
1% of trips are to Downtown LA
3% of trips are to Sunland/La Crescenta
27%
1%
3%
Redesign in Action
Trips: 380,000 trips
Market Share: 1.4% market share
Mileage: 76% of trips under 2.5 miles
Travel time competitiveness: 3.25-3.50
Sylmar/San Fernando Key Facts
Percentages do not equal 100%. Additional trips dispersed throughout the County.

## Slide 13
Sylmar/San Fernando
Sunland/La Crescenta
60% of trips occur within the area
2% of trips are to Sylmar/San Fernando
11% of trips are to the Valley
1% of trips are to Downtown LA
8% of trips are to Glendale
6% of trips are to Pasadena
11%
1%
2%
8%
6%
Trips: 325,000 trips
Market Share: 0.7% market share
Mileage: 44% of trips under 2.5 miles
Travel time competitiveness: 3.00-3.25
Sunland/La Crescenta Key Facts
60%
Percentages do not equal 100%. Additional trips dispersed throughout the County.
Redesign in Action

## Slide 14
Line90/91
Line 92
Line 94/794
Line 222
Line 224
Line 901 (Orange Line)
Red Line
North Hollywood Station
Only 2-3% of trips travel between Sylmar and Sunland
No connection to North Hollywood Station
Only 1% of trips go all the way to Downtown
Only one route connects to North Hollywood, every 12-21 min
Existing Transit
Redesign in Action

## Slide 15
New circulators to address short-distance travel
Fewer routes go Downtown, feed Red Line, frees up resources
Increase frequency to every 10 minutes all day
Direct connection to North Hollywood
Line90/91
Line 92
Line 222
Line 224
Sylmar Shuttle 1
Sylmar Shuttle 2
Sylmar Shuttle 3
Line 901 (Orange Line)
Red Line
North Hollywood Station
Modified Service
Redesign in Action