## Slide 1: Dual-mode survey of park and ride users
Kevin Stefan, HBA Specto Inc.

## Slide 2: Context
Edmonton, AB, Canada:
  1.3M (region) / 930K (City)
  LRT system has 18 stations + 12 under construction; 113K weekday boardings
Survey:
  Fall 2017 (main survey Oct 31 – Nov 10)
  Revealed and stated preference aspects
  In person recruitment
  Online followup

## Slide 3: Recruitment survey
In person recruitment during morning:
  LRT stations, Transit Centres, Buses
  Downtown, Postsecondary Education, Hospital
8 days, ~27 recruiters per day
Single page form – questions about trip being made
  Origin, destination, purpose, mode (detail about park and ride)

## Slide 4: Online Survey
Online survey host using LimeSurvey (FOSS)
General flow:
  Information about trip made
  Stated preference choice games
    540 preloaded choice sets
  Demographics

## Slide 5: Stated preference games:
Lot type (4)
    Structure, surface paved, surface gravel, on street
Walk distance (12) – 25m to 1400m, with time
Price (15) – term and cost, vary by trip purpose
    Free, hourly ($1 to $5), daily ($2 to $15), monthly ($35 to 250)
Availability (9) – time of day
Other features (6) – up to 3 for any alternative

## Slide 6: Survey Response Rates
7600 recruited; 2040 completed survey
  27% completion rate
  23% at transit, 33% at destinations
91% who started online survey completed
Additional 340 without ID

## Slide 7: SP Response quality
Learning curve; most people paying attention
  Tested quick responses in estimation; excluded 3.7%
60% same day, 20% next day response
After 3 SP questions, option to do 3 more
  87% chose to do all six

## Slide 8: Model estimation
Utility expressed in terms of daily cost
  Monthly cost valued at 12.0 days per month (work and school)
  Hourly cost valued at 3.1 hours per day (other purposes)
  High income HH had about 2/3 the cost sensitivity
Not significant:
  Attendants, help phones, fences
  Parking in structure (vs. paved lot)

## Slide 10: Learnings
Pilot useful; real-time response even more so
  Changed recruitment on day-to-day basis
  Dropped third week of recruitment
  Still got twice as many surveys as initial goal
High response and completion rates
Volunteer responses were reasonable
Implemented utility aspects in capacity constrained park and ride model

## Slide 11: Acknowledgements
City of Edmonton
  Arun Bhowmick
  Cherry Liu
HBA Specto
  Doug Hunt
Photo by Banter Snaps on Unsplash