## Slide 1: Use of a Response Surface Model to Quantify Forecasting Error Intervals for Disparate Impacts Analysis
June 4, 2019
John Gliebe, Boston MPO

## Slide 2: Background
Long-range transportation plan (LRTP) disparate impact disproportionate burden (DIDB) policy
  Applies to set of projects in LRTP as a group
  Could the build scenario adversely affect minority and/or low-income populations?
  2018: 3 working group mtgs, 1 public workshop
    Set of metrics to measure impacts
    Account for uncertainty in forecasts

## Slide 3: Potential Metrics
Accessibility (highway and transit)
  Jobs
  Retail amenities
  Healthcare facilities
  Higher education
Mobility (highway and transit)
  Average travel time
Environmental (highway)
  Congested VMT
  Carbon monoxide

## Slide 4: Why Study Uncertainty?
Does the difference between no-build and build scenarios exceed the statistical error in the regional forecasting model?
“It's tough to make predictions,
especially about the future.” ― Yogi Berra

## Slide 5
Uncertainty in Forecasting
Cone of Uncertainty

## Slide 6
Sources of Uncertainty in Regional Travel Forecasting
Forecasting human behavior!
Projecting to the future! (2040)
Model is a complex assembly of data inputs, assumed behaviors, statistical relationships, and algorithms
Notes: 1. Demographics (HH, Jobs)
2. Costs/Payment
3. Response sensitivity (mode bias, VOT, OVT, peak spreading)
4. Transit service frequency
5. System capacity assumptions (lanes, pkg, tran, VDFs)
6. Trip generation rates

## Slide 7: Effect of Uncertainty on Metrics Relatively “High” Variance
-/+ 25%
-/+ 7%
“High” Variance

## Slide 8
Study Steps
Derived forecasting error
intervals from predictions
5
Estimated meta models
from results of experiments
3
Made 1000s of predictions
using meta models
4
Ran experiments varying
key inputs, collected metrics
2
Identified 18 key drivers of
regional model uncertainty
1

## Slide 9: Example of Estimated Meta Model
Average Highway Travel Time in Minutes for Low-Income and Non-Low-Income Groupings
Linear regression

## Slide 10: Example of Simulated Predictions
Minutes per trip
Number of simulated outcomes
Forecasting error interval
-13.3%
+13.3%
-13.1%
-13.1%
Average Highway Travel Time in Minutes for Low-Income and Non-Low-Income Groupings

## Slide 11
Build scenario output
No-build scenario output
5 min.
Hypothetical: Travel Time for Minority Population
15 percent (forecasting error) X 20 minutes = 3 minutes
Is 5 minutes > 3 minutes? Yes. Projected impact.
0
20
15
10
5
25

## Slide 12: Discussion
  Produced forecasting error intervals to be “plugged” into the policy analysis framework
Not all metrics are useful for determining statistically significant impacts—large uncertainty
Not all inputs are useful for modeling uncertainty—some revealed to have little impact on results

## Slide 13
Questions

## Slide 14: Reserve Slides

## Slide 15: Technical Details
Normalized inputs as -/+ % delta from starting values
Latin hypercube sampling
Model input setup and output scripts linked to sampling plan variables
Triangular distributions for simulation

## Slide 16: 18 key inputs (drivers of uncertainty)
Auto operating costs
Transit fares
Toll costs
Value of time
Household sizes
Job locations
Transit mode bias
Walk/bike mode bias
Trip length sensitivity
Transit wait/walk sensitivity
Transit service frequency
Park-and-ride lot supply
Roadway capacities
Congestion-delay sensitivity
Peak spreading factors
Work trip generation
Non-work trip generation
Truck trip generation