## Slide 1: Autonomous Vehicle Impact – Demand Side Story
17th TRB National Transportation Planning Applications Conference
Tuesday, June 4, 2019
Mei Ingram
Travel Behavior Modeling Group/ITRE/NCSU
mzingram@ncsu.edu
Notes: Last but NOT the least 
v.4, Friday, 2019-05-31
16:9 ratio – wide format
Consolidated a few slides vs. v.3
v.3, Friday, 2019-05-17
Submitted to Plan Appl. Web.
v.2, Tuesday, 2019-05-07
Last but not the least:
Key:
To think, ask ourselves questions, technical approach can follow
What if scenarios

## Slide 2: Outline
Think first, forecast technique follows - What If Scenarios
- What are actually happening and would happen from the demand side
Scenario 1: Aging Society Nationwide and NC Triangle Region
Scenario 2: Regional Industry (Job) Mix Shift Due to Automation/AI
Scenario 3: Impact of Autonomous Vehicle
Notes: MZI 2019-04-30
Abstract – submitted 2018-09-05
Background to Problem [80 words]
We have seen significant amount of effort spent on forecasting the impact of CAV to the future transportation system from supply side (with big uncertainties for various reasons), however, much less attention and effort spent on the demand side.
The author believes that we cannot afford to ignore something also fundamental, i.e., the demand side for which the changes are already underway and some with significant foreseeable impact. One major part is the changes in traveler demography and travel patterns.
Description to Application [215 words]
The study uses 2016 Triangle Household Travel Survey and TRM v.6-2045MTP socio-economic information as scenario analysis basis. On the transportation system (supply side), X% of highway capacities and Y% of empty CAV trips are assumed as a result of an unknown % CAV penetration (i.e., not the focus).
The author estimates the impact of traveler and travel behaviors changes to the NC Triangle 2045 regional travels focusing on the following demographic aspects:
Aging society (11% 65/+ in 2016 in the NC Triangle region to 21% in 2040 nationwide predicted by census bureau)
Observed 2016 daily activities for population of age 65-84 and age 85/+ vs. younger adult [age 18-64] workers and non-workers, without impact of CAV
Observed 2016 travel behavior of population age 65-84 and age 85/+ vs. younger adult workers and non-workers, without impact of CAV
Elderly travels, especially by those age 85/+, with impact of CAV
Observed 2016 children [age < 18] daily activities, vs. other non-workers
Observed 2016 children travel behavior vs. other non-workers, without impact of CAV ct
Children travels, with impact of CAV
Children travels, with impact of distance learning
University students travels, with impact of distance learning
Number of regional trips, trips-in-motion by time of day, daily VMT, congestion level during peak time are displayed.
Statement on Why Application is Noteworthy [85 words]
To better inform policy makers and planners for wise decisions and preventing unnecessary investment in the wrong direction (i.e., no need to widen a roadway as future regional trips may be reduced, or future roadway capacity with impact of CAV is sufficient already), it is essential to understand how future travelers and their travel changes will be from demand side, in addition to forecast of supply side alone.
The presentation demonstrates year 2045 scenarios of regional travel changes with impacts of various potential legitimate factors.

## Slide 3: Aging Nation - % Age 65/+: 13.7% [2012] increase to 21.0% [2040]
Notes: MZI 2019-05-07
Census Bureau prediction:
https://www.census.gov/prod/2014pubs/p25-1140.pdf
“An Aging Nation: The Older Population in the United States, Population Estimates and Projections’, Current Population Reports, by Jannifer M. Ortman, Victoria A. Velkoff, and Howard Hogan, Issued May 2014
Table 2 Projections and Distribution of the Total Population by Age for the United States: 2012 to 2050 (numbers in Thousands)
2012, 2040 and 2050

## Slide 4: Scenario 1 – 2045 Aging vs. 2016 Age Distribution [NC Triangle]
Age Group | 2016 % Distribution | 2045MTP Population No Aging | 2045 Aging % Distribution | 2045 Population Aging | Difference Aging vs. 2016 Distribution | % Difference Aging vs. 2016 Distribution
0 – 17 | 24.5% | 726K | 21.6% | 641K | - 85K | - 12%
18 – 64 | 63.4% | 1,879K | 57.4% | 1,702K | - 177K | - 9%
65 – 84 | 11.5% | 340K | 16.8% | 499K | + 159K | + 47%
85/+ | 0.7% | 19K | 4.1% | 122K | + 103K | + 532%
All Ages | 100% | 2,964K | 100% | 2,964K | No Change | No Change
Notes: 1. 2016 % Distribution: 2016HTS [Expanded to 2010_2016ACS HHs]; % Elderly [65/+] in 2016 was 12.2% < 13.7% [Nationwide 2012] 2. 2045 Aging % distribution: U.S. Census Bureau, "Projections and Distribution of the Total Population by Age for the United States 2012 to 2050" [average of 2040 and 2050] 3. 2045 Aging population = 2045MTP total population * 2045 Aging % distribution |  |  |  |  |  | 
Notes: MZI/H, Fri, 2019-05-31
Source: Task_26413_CAV_v1_2018-08-29_11h30_MeiITRE_2019-05-17_12h00_MeiHome.xlsx
Tab “CAV_Test”
MZI 2019-05-07
Census Bureau prediction:
https://www.census.gov/prod/2014pubs/p25-1140.pdf
“An Aging Nation: The Older Population in the United States, Population Estimates and Projections’, Current Population Reports, by Jannifer M. Ortman, Victoria A. Velkoff, and Howard Hogan, Issued May 2014
Table 2 Projections and Distribution of the Total Population by Age for the United States: 2012 to 2050 (numbers in Thousands)
2012, 2040 and 2050

## Slide 5: Scenario 2 – 2045 Industry Shift - Automation/AI Impact [NC Triangle]
Establishment Type | 2045 MTP % of Total Jobs No Auto./AI | 2045MTP Jobs No Auto./AI | Job Market Change Assumption Automation/ AI Impact | 2045 % of Total Jobs Automation/ AI Impact | 2045 Jobs Automation/AI Impact | 2045 Job Changes Automation/AI Impact - vs. No Impact
Industry | 14% | 218K | - 50% | 11% | 109K | - 109K
Office | 36% | 553K | - 50% | 29% | 276K | - 276K
Service – Low Attraction Rate per Employee | 26% | 401K | - 10% | 38% | 361K | - 40K
Service – High Attraction Rate per Employee | 6% | 94K | - 20% | 8% | 75K | -19K
Retail | 17% | 266K | - 50% | 14% | 133K | - 133K
Total Jobs | 100% | 1,531K | - 32% | 100% | 954K | - 577K
Source – 2045 MTP Jobs [TRM v.6-2045 Employment by Establishment Type] SVN 307 |  |  |  |  |  | 
Notes: MZI/H, Fri, 2019-05-31
Source: Task_26413_CAV_v1_2018-08-29_11h30_MeiITRE_2019-05-17_12h00_MeiHome.xlsx
Tab “CAV_Test”

## Slide 6: Scenario 3 [Impact of Autonomous Vehicle] - Assumptions
Elderly [65/+] each makes as many trips (HBShop, HBO, and NHNW) as younger [Age 18-64] non-working adult
Teenager each makes twice of HBShop, and as many HBO and NHNW as non-working adults
Labor force reduced by 32%
Auto VMT increase by 10% for all trip purposes except HBK12

## Slide 7: Scenario 3 – AV Impact: Person Trip Rate Assumption
Age Group & Industry | HBW | HBShop | HBK12 | HBO | NHNW | WBNH | All Purpose
0 – 17 | 0.01 | 0.60 <= 0.29 | 0.87 | 1.40 <= 1.04 | 0.76 <= 0.55 | 0.00 | 2.76
18 – 64 | 0.77 | 0.57 | 0.23 | 0.98 | 0.51 | 0.64 | 3.70
Worker | 1.01 | 0.51 | 0.18 | 0.84 | 0.42 | 0.85 | 3.81
Industry | 1.14 | 0.42 | 0.13 | 0.70 | 0.33 | 0.79 | 3.51
Office | 1.00 | 0.51 | 0.20 | 0.89 | 0.42 | 0.93 | 3.93
Service – Low Rate | 0.96 | 0.54 | 0.17 | 0.88 | 0.47 | 0.87 | 3.88
Service – High Rate | 1.09 | 0.47 | 0.27 | 0.72 | 0.48 | 0.84 | 3.88
Retail | 1.04 | 0.52 | 0.16 | 0.77 | 0.34 | 0.51 | 3.34
Non-Worker | 0.00 | 0.77 | 0.33 | 1.40 | 0.76 | 0.00 | 3.30
65 – 84 | 0.18 | 0.77 <= 0.73 | 0.04 | 1.40 <= 1.15 | 0.76 <= 0.61 | 0.14 | 3.29 <= 2.85
85/+ | 0.04 | 0.77 <= 0.57 | 0.01 | 1.40 <= 1.05 | 0.76 <= 0.48 | 0.04 | 3.01 <= 2.17
Notes: 2016HTS [linked trip data]; 95% of workers are within age 18-64; % workers in 2016 and in 2045MTP [Adult -worker vs. Adult-non-worker (2016HTS) = 65.7% vs. 34.3%] 2016HTS person trip rate (all ages combined): All purposes combined: 3.36 [HBW 0.51, HBShop 0.52, HBK12 0.36, HBO 1.02, NHNW 0.42] |  |  |  |  |  |  | 
Notes: MZI 2019-04-30
MZI/H, Fri, 2019-05-31
Source: Task_26413_CAV_v1_2018-08-29_11h30_MeiITRE_2019-05-17_12h00_MeiHome.xlsx
Tab “CAV_Test”

## Slide 8: Scenario 3 – AV Impact: VMT per Auto Trip Assumption [Increase by 10% except HBK12 (shown), from 2016HTS Observed]
Age Group & Industry | HBW | HBShop | HBK12 | HBO | NHNW | WBNH | All Purpose
0 – 17 | 21.9 | 6.8 | 5.9 | 7.1 | 6.1 | 5.8 | 6.7
18 – 64 | 13.0 | 5.9 | 5.7 | 7.8 | 6.1 | 8.3 | 8.7
Worker | 13.0 | 5.9 | 5.6 | 7.6 | 6.1 | 8.3 | 9.1
Industry | 13.4 | 5.6 | 5.6 | 7.6 | 6.1 | 9.1 | 9.8
Office | 13.2 | 5.5 | 5.7 | 7.5 | 5.6 | 7.9 | 8.9
Service – Low Rate | 13.5 | 6.2 | 5.3 | 7.5 | 6.3 | 8.8 | 9.3
Service – High Rate | 12.0 | 5.2 | 4.4 | 8.5 | 8.9 | 7.3 | 8.9
Retail | 10.3 | 6.9 | 7.6 | 8.0 | 4.8 | 7.2 | 8.2
Non-Worker | 8.0 | 5.9 | 5.8 | 8.3 | 6.2 | 5.0 | 6.9
65 – 84 | 11.4 | 5.5 | 7.7 | 7.7 | 5.7 | 11.8 | 7.0
85/+ | 27.4 | 5.9 | 7.7 | 7.0 | 5.7 | 9.6 | 6.5
All Ages | 12.9 | 6.0 | 5.8 | 7.5 | 6.0 | 8.2 | 8.3
Source: 2016HTS [linked trip data] |  |  |  |  |  |  | 
Notes: MZI/H, Fri, 2019-05-31
Source: Task_26413_CAV_v1_2018-08-29_11h30_MeiITRE_2019-05-17_12h00_MeiHome.xlsx
Tab “CAV_Test”

## Slide 9: Scenario 3 – CAV Impact: Person Trips & Auto VMT vs. 2045MTP
Age Group If Worker & Industry | 2045 MTP NO Aging NO Labor Mix Shift - NO Auto./AI | S1 2045 Aging No Labor Mix Shift - No Auto./AI | Change S1 vs. 2045 MTP | S2 2045 Aging Labor Mix Shift - No Auto./AI | Change S2 vs. 2045 MTP | S3 2045 Aging Labor Mix Shift - Auto./AI Impact | Change S3 vs. 2045 MTP
Person Trips | 9,937 K | 9,795 K | 142 K [ - 1%] | 9,549K | 388 K [ - 4%] | 10,438K | + 501 K [+ 5%]
Auto VMT [Miles] | 49.4 M | 49.6 M | + 231 K [+ 0.5%] | 47.4 M | 2.0 M [- 4.0 % ] | 50.0 M | + 0.6 M [+ 1.2%]
Note: Not including empty auto vehicle VMT. |  |  |  |  |  |  | 
Notes: MZI/H, Fri, 2019-05-31
Source: Task_26413_CAV_v1_2018-08-29_11h30_MeiITRE_2019-05-17_12h00_MeiHome.xlsx
Tab “CAV_Test”

## Slide 10: A Few Potential Further Tests
Regional employment change by industry: some existing ones would be removed while new ones created
HBW trip rate reduction by Industry (even by employee type), full-time/part-time, due to telecommuting, flexible schedule, work in the AV
HBU trip rate reduction due to distant learning
HBO and NHNW trip rate increase due to more non-work time and CAV
- Key: just because CAV can bring convenience and lower cost, does not mean you will travel entire day on the roadway network! E.g., if average person trip rate is 3-4, you probably would less likely to make more than ten with CAV

## Slide 11: Acknowledgement
Triangle Regional Model stakeholder for funding the surveys
- North Carolina Department of Transportation
- Durham - Chapel Hill - Carrboro MPO
- Capital Area MPO
- GoTriangle
Travel Behavior Modeling Group team members for processing data
2016HTS conducted by RSG

## Slide 12
Questions and Suggestions?
Thanks for your time!
Please send to: mzingram@ncsu.edu