## Slide 1
Development of An Enhanced and Efficient Traffic Forecasting Tool (TFT)
June 4, 2019
Johnny Han, Corradino
Akbar Bakhshi, Corradino
Greg Katter, Indiana Department of Transportation
Korey Chu, Indiana Department of Transportation
Roy Nunnally, Indiana Department of Transportation
2019 TRB Transportation Planning Application Conference

## Slide 2
What is TFT ?
A customized application to facilitate State DOT’s long-range traffic forecasting activities at project level.

## Slide 3
2016 – 2017
TransCAD version
How TFT Evolves …
2018 – present
R version (on-line)
INDOT TFT v3
INDOT TFT v4

## Slide 4
An open-source & emerging programming language for travel demand modeling
Efficient data management of multiple links at a time
Powerful graphing capability for better output visualization
“Live” graphs
.HTML output files – extremely convenient for info dissemination
No or minimal software cost
Accessible by anyone (authorized users) and from anytime & anywhere (internet needed)
Why ?

## Slide 5
TFT Fundamentals
Traffic Estimation/Forecast Methods
  Linear
  Regression
  Exponential (Growth Factor)
  Adjusted Exponential (Statewide Traffic Growth Profile for IN, KY, TN)
  NCHRP 255 calibration
Data Sources
  Historical traffic counts (past 15 years)
  Statewide model volumes (Base Year & Future Year)
Analysis for multiple links at a time

## Slide 6
TFT Fundamentals (cont.)
Indiana Statewide Model
4-step model (TransCAD 6)
Coverage – entire IN + partial IL, KY, MI, OH
4879 zones & 46780 links
Modes
  auto, freight, LD transit
  tolling
Model years 2010 – 2035 with 5-year increment
Currently being updated

## Slide 7
Traffic Data
INDOT’s Traffic Count Database System (TCDS)
Recent AADT counts (2001 – 2015)
Cover all state-owned roadways in TFT v4
TFT Fundamentals (cont.)

## Slide 8
TFT Fundamentals (cont.)
Indiana Traffic Growth Profile
Q-Q Plot for Data Cleaning

## Slide 9
Pre-process
TransCAD Version
R Version
Join traffic counts with model network (fixed Base & Future scenarios)
Allow selection of desired scenarios

## Slide 10
Pre-process (cont.)
TransCAD Version
R Version
Green-highlight links with historical traffic data
R version incorporates OpenStreetMap background for familiarity and enables zoom-in function by selecting county.

## Slide 11
Choose Link
Choose/Clear Link
R Version
TransCAD Version

## Slide 12
Choose Link (cont.)
TransCAD Version
R Version

## Slide 13
Traffic Counts Reporting
Traffic Counts Reporting
R Version
TransCAD Version

## Slide 14
Traffic Counts Reporting (cont.)
Link #1
Link #2
R Version
TransCAD Version
“Real-time” report by link
Save as HTML file

## Slide 15
Traffic Estimation
Traffic Estimation Report & Graph
R Version
TransCAD Version

## Slide 16
Estimation Report
R Version
TransCAD Version
Link #1
Link #2
“Real-time” report by link
Save Estimation Graph
Save as HTML file
Linear Model
Reg. Model
Exp. Model
Linear Model
Reg. Model
Exp. Model

## Slide 17
Estimation Graph
R Version
TransCAD Version

## Slide 18
Traffic Forecast
Target year for forecast reporting
R Version
TransCAD Version
Target year for forecast reporting
Traffic Forecast Report & Graph

## Slide 19
Forecast Report
Link #1
Link #2
R Version
TransCAD Version
“Real-time” report by link
Linear
Reg.
Exp.
Adj. Exp.

## Slide 20
Forecast Graph
R Version
TransCAD Version
Based on traffic counts & ISTDM
Various forecasting methods
Forecasts refined by NCHRP 255 & Indiana Traffic Growth Profile
Capacities of LOS A – E

## Slide 21
In Progress …
New Corridor Analysis function (to report fundamental statistics of selected corridor)
Complete coverage of all state-owned roadways
Enhanced visualization in R version

## Slide 22
Johnny Han, PhD, PE
Technical Vice President
jhan@corradino.com
317.744.9858
Contact:
www.corradino.com