## Slide 1: Transit Performance and Reliability Evaluation for Arterial Corridors
Natalia Zuniga Garcia, M.Sc.
Randy B. Machemehl, Ph.D.
Natalia Ruiz-Juri, Ph.D.
Heidi W. Ross, M.Sc.
Nadia Florez-Morcote, M.Sc.
June 5th, 2019

## Slide 2: Outline
Background
Introduction
Case Study
Metrics
Future Work
2/14

## Slide 3: Background
Development, design, and construct improvements along key Austin corridors that enhance mobility, safety, and connectivity for all users.
Recommendations supported by identifiable metrics to prioritize:
  reduction in congestion
  improved level of service for all modes of travel
  connectivity, and improved effectiveness of transit operations
3/14

## Slide 4: Background
  Identify current and future data sources
  Complete back office system architecture capable of ingesting data from multiple sources
  Develop a tool that uses data from multiple sources to calculate key performance metrics
Our Role
Generate performance metrics for bond corridor evaluation by practitioners
4/14

## Slide 5: Introduction
Develop an evaluation tool to provide transit performance and reliability information for arterial corridors in Austin, Texas.
Objective
Problem
Digesting and understanding the large amount of complex data available
For arterial corridors: the presence of different traffic control systems, multiple transit routes, and multimodal interaction
Recent advances in ITS transit data-collection allow evaluation of multiple operational variables.
5/14

## Slide 6: Case Study
1
2
3
4
5
6
7
8
9
4
1
5
6
7
3
2
8
9
6/14

## Slide 7: Metrics: Tool Development
GTFS
AVL
APC
Vehicle Capacity
Data Sources
Transit Speed
Ridership
Occupancy
Dwell Time
Delay
Volume-to-Capacity Ratio
Reliability
Service Coverage
Frequency
Measurable Impacts
Automated Analysis
7/14

## Slide 8: Metrics: Transit Speed on Corridors
Speed estimated using AVL data
  GPS points (location & time stamp) for all buses
Average speed through the corridor
  Difference in time stamps over distance
  Distance is corridor length covered by bus trajectory
Challenges:
  GPS points are provided every 1-2 minutes
    The results may not be representative of the entire corridor
  Different routes cover different corridor segments
  Dwell times are included in travel time
Bus Route
Corridor
GPS points Bus 1
GPS points Bus 2
GPS points Bus 3
Distance for Bus 3
8/14

## Slide 9: Metrics: Transit Speed on Corridors
1. Choose Analysis Type
2. Select Dates and Corridor
4. Summarize Transit Speed Estimate by Hour and Direction
3. Visualize Transit Routes Serving Corridor for Analysis
9/14

## Slide 10: Metrics: Occupancy
1. Choose Analysis Type
2. Select Dates and Corridor
4. Summarize Transit Occupancy by Hour
3. Visualize Transit Routes Serving Corridor for Analysis
Number of Passengers
10/14

## Slide 11: Metrics: Boardings and Alightings
1. Choose Analysis Type
2. Select Dates
4. Summarize Passenger Counts
(not normalized by number of stops)
3. Visualize Transit Stops and Routes
11/14

## Slide 12: Metrics: Dwell Time
2. Select Dates
3. Visualize Dwell Time and Transit Information
1. Choose Analysis Type
12/14

## Slide 13: Future Work
Estimate bus trajectory
  Integrate AVL and APC
  Update speed estimation
Estimate bus on-time performance
  Integrate GTFS and APC
13/14

## Slide 14: THANKS
Questions or Comments?
nzuniga@utexas.edu
14/14