## Slide 1: Innovative methods towards building and evaluating congestion charging scenarios: The case of Metro Vancouver
Ilan Elgar
Fearghal King, Reid Keller, Daniel Firth
Presented at the 17th TRB Plan App Conference,
June 4th, 2019, Portland, OR.

## Slide 2: Metro Vancouver regional context
Geographic:
  ~2,900 km2 (~1,100 mi2)
  ~2.5 million pop. (2016)
  Contained by mountains, ocean, and the US border
Governance:
  23 local authorities
  23 mayors
  Regional Transportation Authority (TransLink)
    Board of Directors
    Mayors’ Council
~ 60km (37 miles)
USA
USA
OCEAN
LOTS OF MOUNTAINS!
LOTS OF
WATER CROSSINGS!

## Slide 3: Historical context
2009:
Golden Ears Bridge opens (tolled)
2012:
Port Mann Bridge opens (tolled)
Sept. 2017:
Bridge tolls removed
~2012 – 2016:
Vancouver ranked ‘most congested city’ in Canada
June 2017:
Mobility Pricing Independent Commission formed
Fairness and affordability concerns intensify; some dissent towards TransLink
1993:
Metro Vancouver first endorsed the idea of road pricing
1998:
TransLink formed
2013:
Road pricing confirmed in several policy documents (RTS, RGS, Transport 2040) and by the Mayor’s Council

## Slide 4: Commission objectives
The Commission’s work was guided by three core objectives:

## Slide 5: Evaluation framework & analytical approach
Coarse-level evaluation
Illustrative examples
IDENTIFY AND REFINE THE LIST OF POTENTIAL POLICY OPTIONS
SCENARIO DEVELOPMENT & EVALUATION PROCESS
Price-setting in the absence of clear objectives
Iterative development of scenarios to guide and educate MPIC
Development of complex metrics and KPIs
Evaluation exercises and trade-off discussions

## Slide 6: Approach towards addressing fairness
Benefiter Pay
Principle
  That people should pay in proportion to the time savings they experience
User Cost
Principle
  That people should pay in proportion to the amount of congestion they contribute to
Better aligned with usage
Better aligned with congestion contribution
SIMPLE
COMPLEX
 | Flat fee (Temporally) | 
 | Vary by time of day (TOD) | 
 | Vary by direction of travel (Dir.) | 
 | Vary by location | 
User Pay
Principle
  That people should pay in proportion to how much they use the transportation system

## Slide 7: Price-setting in the absence of clear focus
How bad is congestion?
How is congestion defined and measured?
Where should it be reduced?
When should it be reduced?
By how much should it be reduced?
1
2
8
7
6
5
4
3

## Slide 8: How are the rates set in theory?
Congestion charge should be equal to the costs that motorists impose upon society - Marginal Social Cost (MSC)
Ensures avoiding overcharge
Provides a benchmark to compare between scenarios
Provides useful insight into different values: paying by use vs. by congestion contribution

## Slide 9: Optimal Price-setting
Travel time with original VDF and MSC VDF
A system optimum assignment was developed to approximate the MSC.
The VDFs estimate travel time on a road network link given its free-flow speed, capacity, and vehicle demand.
In application, the MSC is the first derivative of the VDF with respect to vehicle demand.
The MSC cost in minutes is converted into dollars using weighted average values of time (VOT).
MSC cost in minutes

## Slide 10: Scenario development and iterations (point charges)
CBD:
  CBD ($5)
  CBD (MSC)
Bridges:
  Bridges ($1; $5)
  Bridges (TOD)
  Bridges (TOD + Dir.)
  Bridges (% MSC)
  Bridges + NR (% MSC)
Comparisons:
  Baseline scenario
  ‘Pure’ MSC scenario

## Slide 11: Scenario development and iterations (dist.-based charges)
DBC:
  DBC – flat ($0.10/km; $0.12/km; $0.15/km)
  DBC (TOD)
  DBC (TOD) – 2 zones
  DBC (TOD) – 2 zones transit (% MSC)
  DBC 8 zones (% MSC)
Comparisons:
  Baseline scenario
  ‘Pure’ MSC scenario
$/km
$$/km
Zone 1
Zone 2
Zone 4
Zone 3
Zone 5
Zone 7
Zone 6
Zone 8
Zone 8
Zone 8
Zone 8
Zone 8
Zone 8
Zone 8
Highest charge rates
Lowest charge rates
Zone 8

## Slide 12: Illustrative concepts
Range of charge rates per crossing:
Min scenario:
AM peak: $0.85 - $4.30
Off peak: $0.36 - $1.06
PM Peak: $1.03 - $5.52
Min+ scenario:
AM peak: $1.27 - $6.45
Off peak: $0.62 - $1.59
PM Peak: $1.54 - $8.27
A regional congestion point charge with charge points at or close to some or all of the regionally important crossings, complemented by further charges at locations within the Burrard Peninsula.

## Slide 13: Illustrative concepts
A distance-based charge with two or more zones with varying charge rates throughout Metro Vancouver.
Range of charge rates per km:
Min scenario:
AM peak: $0.02 - $0.25/km
Off peak: $0.02 - $0.07/km
PM Peak: $0.03 - $0.27/km
Min+ scenario:
AM peak: $0.03 - $0.38/km
Off peak: $0.03 - $0.11/km
PM Peak: $0.04 - $0.40/km
Zone 1
Zone 2
Zone 4
Zone 3
Zone 5
Zone 7
Zone 6
Zone 8
Zone 8
Zone 8
Zone 8
Zone 8
Zone 8
Zone 8
Highest charge rates
Lowest charge rates
Zone 8

## Slide 14: Evaluation results
Congestion: These scenarios have the potential to reduce congestion by 20-25%, while improving travel time reliability by 17-23%
Fairness: It is estimated that it would cost the average paying household between $3 - $8 per day
Revenue: These scenarios have the potential to raise between $1 - $1.6 billion in net revenues per year

## Slide 15: Next steps
Further research and evaluation to understand issues and impacts around…
  Equity/Affordability/Accessibility
  Business and Regional Planning impacts
  Coordinated pricing
  New mobility
  Performance targets
  Policy principles
  Administration
  Technology costs and timelines
  Pilot studies
Final Report: https://www.translink.ca/Plans-and-Projects/Mobility-Pricing.aspx
It’s Time website: https://www.itstimemv.ca/

## Slide 16: Thank you!
Fearghal King, PhD Senior Transportation Planner, Mobility Pricing Transportation Planning & Policy TransLink Tel: +1 778-375-7621 Email: fearghal.king@translink.ca
Web: www.translink.ca
Final Report: https://www.translink.ca/Plans-and-Projects/Mobility-Pricing.aspx
It’s Time website: https://www.itstimemv.ca/