## Slide 1
Hell’s Kitchen
Neighborhood Transportation Study
Commissioner Janette Sadik-Khan New York City Department of Transportation
TRB Presentation May 6, 2013
Goal: Improve mobility, safety and quality of life for all street users
  Pedestrians
  Cyclists
  Transit Users
  Deliveries
  Motorists

## Slide 2
Study Area
2
MANHATTAN
Hudson R
NEW
JERSEY
East R
QUEENS
BKLYN
LINCOLN
TUN

## Slide 3
3
Study Area
0.8 square miles
142 signalized intersections
Trip generators within study area:
  Port Authority Bus terminal
  Javits Convention Center
  Manhattan Cruise Terminal
  USS Intrepid Museum
  Theater Row
  Restaurant Row
  Hudson River Greenway Bike Path
  Caemmerer Rail Yards
  Quill Bus Depot
  US Postal Service Complex
  Distribution Centers for 3 major parcel delivery companies
37,000 residents
96,000 workers

## Slide 4
4
Study Area
Adjacent to the study area to the east:
  Theater District
  Times Square
  Garment District
  Penn Station
  Madison Square Garden
To the north:
  Lincoln Center
  Upper West Side neighborhood
To the south:
  Chelsea neighborhood

## Slide 5
5
Study Area

## Slide 6
6
Effects of Lincoln Tunnel
Biggest cause of congestion in the neighborhood
6 lanes of traffic in 3 tubes
Reversible middle tube
  AM peak: 4 lanes inbound, 2 lanes outbound
  PM peak: 2 lanes inbound, 4 lanes outbound
  AOT: 3 lanes inbound, 3 lanes outbound
120,000 vpd ADT
Traffic worst during PM peak
  Outbound capacity is 5200 vph
  Excess demand at least another 2000 vph

## Slide 7
7
Neighborhood Concerns

## Slide 8
8
Neighborhood Vision

## Slide 9
9
Reality of Traffic Congestion
Goal: Improve mobility, safety and quality of life for all street users
  Pedestrians
  Cyclists
  Transit Users
  Deliveries
  Motorists

## Slide 10
Data Collection
10
Traffic and pedestrian data
  Used data from 7 different EIS’s
  Supplemental Turning Movement Counts
  Supplemental ATRs
  MioVision Counts in some locations
Speed Data
  From EIS’s
  Supplemented with Taxi GPS

## Slide 11
Modeled Using SimTraffic
11
Network must extend to bottleneck of Lincoln Tunnel
To account for downstream congestion, must use demand volume, not processed volume
Limitations of model
  Max allowable crosswalk volume 1700 ped/hr
  Aggressive driving
    Merging
    Finding Gaps
    Getting into proper lane at the last second
    Turning onto a congested link

## Slide 12
Baseline Condition Average Travel Speeds
12

## Slide 13
4 Improvements
13
Signal Timing adjustments to protect pedestrians
Bike Lanes on 8th & 9th Avenues
36th & 9th Canoe Project
Turn ban at 37th & 9th
Show Incremental Effect and Cumulative Effect

## Slide 14
Improvement 1:Signal Timing to Protect Pedestrians
  NO IMPROVEMENT
  SPLIT PHASE
  LPI
  Conflict between pedestrians and turning vehicles
  Pedestrians get a 7 sec head start before conflict with turning vehicles
  Less crossing time but conflict free
  Less time for turning vehicles
  Need to remove parking
  High rate of non-compliance (peds and vehicles)

## Slide 15
Effect of 2012 Signal Timing Improvements
15

## Slide 16
Improvement 2: Bike Lanes on 8th & 9th Avenues
16
Parking protected bike lane on left side, with floating parking lanes
Left turn bays every other block
Retains same number of travel lanes, but narrower from 12’ to 10’ or 11’
Concrete pedestrian islands effectively reduces crossing distance
Removal of 76 parking spaces each on 8th & 9th Avenues
  Outreach effort to merchants assures sufficient loading zones provided

## Slide 17
Effect of Bike Lanes on Traffic
17

## Slide 18
Discontinuous Sidewalk on 9th Ave
18
9 Av
W 36 St
To Lincoln Tunnel

## Slide 19
Discontinuous Sidewalk on 9th Ave
19

## Slide 20
Discontinuous Sidewalk on 9th Ave
20

## Slide 21
Imp 3:“Canoe” Design with New Signalized Crosswalk
21
PROPOSED
EXISTING

## Slide 22
Effect of “Canoe”
22

## Slide 23
Improvement 4: Turn Ban from W 37th St to Ramp
23
Diverted Flow

## Slide 24
Sign for Turn Ban at WB Approach 37th & 9th
24
Diverted Flow

## Slide 25
Effect of Turn Ban at 37th & 9th
25

## Slide 26
Questions?
Thank
You
Gregory Haas ghaas@dot.nyc.gov (212) 839-7759