## Slide 1: Value of Time for Freight Transportation
TRB Applications Conference – Freight Committee
May 5th, 2013
Sashank Musti
Anurag Komanduri
Kimon Proussaloglou
Single Point Estimate or a Range

## Slide 2: Motivation and Goals
Two independent studies to assess freight movements on Hudson River crossings and Los Angeles area freeways
Freight moves majorly on trucks
Forecasted growth in freight movements – 40 percent by 2030 for New York; 100% by 2030 for Port of Los Angeles
Multimodal freight transportation investment critical
  Reduce congestion
  Support increased freight demand
Market assessment for nonhighway modes
Time-of-day shifts to reduce congestion

## Slide 3: Approach
“If we build it, they will come – won’t they?”
  “Go with the gut” - not an option
  “Do it once…and do it right“ – consensus building
Market assessment for all options
  Demand management options – truck rerouting and time-of-day switching
  New Multimodal options – water and rail crossings
  Related infrastructure investment – distribution centers
Assess impacts – quantify benefits
  Understand willingness to pay
  Test adoption under alternative scenarios
  Triple bottom line – people, planet and profit

## Slide 4: Methodology
Long-Term Planning Model
Demand Management
Routing Models
Time-of-Day Models
Baseline Sensitivities for Truck LOS
Inform Tolling and Other TDM Strategies
(Revenue Analysis)
Infr. Assessment
Models
Multimodal Options
Mode Choice Models
Quantify Preferences for New Modes
Support Capital Investment Decisions
(Cost Benefit Analysis)
Assess Distribution Center Relocation
Targeted Marketing to Improve Acceptance (Adoption Horizon)
Quantitative Market Research SP Experiments
Qualitative Market Research Focus Groups

## Slide 5: Focus Groups
Very successful – in-depth discussions
Focus group findings
  Slow is ok – but, we need reliable service
  Last mile service works against rail + no control over routing
  Distribution center locations prevent me from moving
  Lot of time (and money) wasted in local moves
  Safety, damage considerations are essential
  Willing to pay for improved service
  Cost, travel time & on-time performance critical
Establishments willing to try other options

## Slide 6: Stated Preference (SP) Surveys
“Trade-off” questions
  Truck route 1 vs. Truck route 2
  Truck peak vs. Truck off-peak
  Truck crossing vs. Rail crossing vs. Water crossing
Increasing order of difficulty in SP experiments
  Demand management options
  Multimodal options
  Infrastructure impact options
Tailored experiments
  Adjusted for short vs. long movements
  Adjusted for decision maker – carriers, shippers, service trucks, receiver carriers and shipper-carriers
  Customized levels of service – grounded in reality

## Slide 7: SP Experiment Route Choice – Demand Management
Suppose these were your transportation options to ship your goods from
Randleman, North Carolina to Long Island City, New York
Your choices are… | Option A | Option B
 | You ship/receive your good in the New York Region on existing or new highways, tunnels, and bridges The key characteristic of this option are as follows | You ship/receive your good in the New York Region on existing or new highways, tunnels, and bridges The key characteristic of this option are as follows
Mode of Transportation | Truck | Truck
Crosses Hudson on… | Existing bridges or new freight-only tunnel | Existing bridges or new freight-only tunnel
Transit Time (hours) | 24 | 35
Transportation Cost (all inclusive) | $332 | $167
Reliability (on-time delivery) | 95% | 93%
Which of the two options above would you choose? (Please circle one)
Option B
Option A

## Slide 8: SP Experiment Time-of-Day Choice – Demand Management
Suppose these were your transportation options to ship your goods for your regular shipment, new Truck-Only Express Lanes that provide faster, more reliable travel times may be constructed
Your choices are… | Option A | Option B | Option C
Time of Day | During Peak Period | Before Peak Period | After Peak Period
Distance | 60 miles | 60 miles | 60 miles
Transit Time | 2 hours 48 minutes | 2 hours 12 minutes | 2 hours 15 minutes
Reliability (on-time delivery) | 90% | 91% | 96%
Total Toll | $0 | $20 | $14
Option B
Option A
Option C
Which of the three options above would you choose? (Please circle one)

## Slide 9: SP Experiment Mode Choice - Multimodal Option
Suppose these were your transportation options to ship your goods from
Seattle, Washington to Bay Shore, New York
Your choices are… | Option A | Option B | Option C
 | You ship/receive your good in the New York Region on existing or new highways, tunnels, and bridges The key characteristic of this option are as follows | You ship/receive your good in the New York Region on existing or new highways, tunnels, and bridges The key characteristic of this option are as follows | You ship/receive your good in the New York Region on existing or new highways, tunnels, and bridges The key characteristic of this option are as follows
Mode of Transportation | Truck | Rail Intermodal | Truck
Crosses Hudson on… | New freight-only tunnel on rail cars | New freight-only tunnel | Existing bridges or new freight-only tunnel
Transit Time (hours) | 160 | 128 | 90
Transportation Cost (all inclusive) | $2,660 | $1,114 | $2,200
Reliability (on-time delivery) | 90% | 80% | 97%
Option B
Option A
Option C
Which of the three options above would you choose? (Please circle one)

## Slide 10: SP Information DC Relocation - Infrastructure Assessment
Does the establishment use a DC in the study region?
  Why? Why not?
Who manages the DC operations?
  Self managed – own/rent/lease
  Customer managed – shipment specific
How long has the DC been used?
What operations are carried out?
Would you consider relocating the DC?

## Slide 11: SP Experiment Model Results - Multimodal Option
Time Spline (Applied if TT > 24 hours) | Truck | 0.127 | 5.4
 | Truck Ferry | 0.131 | 4.7
 | Truck on Rail | 0.109 | 4.3
Cost Spline (Applied If Cost > $900) | Truck | 0.0013 | 4.5
 | Truck Ferry | 0.0015 | 4.5
 | Truck on Rail | 0.0014 | 4.3
 | Coefficient Description | Value | T-Stat
Time (hours) | Truck | -0.1380 | -6.1
 | Truck Ferry | -0.1430 | -5.5
 | Truck on Rail | -0.1190 | -4.9
 | Rail | -0.0122 | -2.2
 | Rail Float | -0.0122 | -2.2
 | Coefficient Description | Value | T-Stat
Constant | Truck Ferry | -1.53 | -10.2
 | Truck on Rail | -1.69 | -9.5
 | Rail | -4.69 | -4.4
 | Rail Float | -4.23 | -5.1
 | Truck Only | Base | 
On-Time Reliability | Low (<85% on time) | -1.03 | -6.0
 | Medium (85-90% on time) | -0.34 | -3.1
 | High (>90% on time) | Base | 
Shipment Cost by Commodity | Agricultural Goods | -0.0028 | -3.1
 | Metal and Mining Goods | -0.0035 | -3.9
 | Construction Goods | -0.0033 | -5.7
 | Chemical Goods | -0.0045 | -6.6
 | Wood and Paper Goods | -0.0036 | -5.2
 | Electronics Goods | -0.0034 | -5.7
 | Transportation and Utility Goods | -0.0026 | -3.7
 | Wholesale and Retail Goods | -0.0036 | -7.5
Model Fit | Value
Pseudo R2 (0) | 0.345
Pseudo R2 (c) | 0.149
Number of Observations | 1,093

## Slide 12: What is Value of Time (VOT)?
VOT is the $’s willing to pay to save time or the $’s to accept for lost time
Impedance Function
(Composite cost: distance, travel time, toll, operating costs,..)
Skims
VOT
Model Application & Traffic Assignment
(Congestion, Delay, Emissions)

## Slide 13: SP Experiment Multimodal Model Evaluation-Values of Time ($/hr)
Commodity Type | Truck |  | Truck Ferry |  | Truck on Rail | 
 | Short Trips |  |  |  |  | 
 | High Cost | Low Cost | High Cost | Low Cost | High Cost | Low Cost
Agriculture | $92.00 | $49.30 | $85.00 | $42.50 | $110.00 | $51.10
Metal and Mining | $62.70 | $39.40 | $56.70 | $34.00 | $71.50 | $40.90
Construction | $69.00 | $41.80 | $62.60 | $36.10 | $79.40 | $43.30
Chemical | $43.10 | $30.70 | $38.40 | $26.40 | $47.70 | $31.80
Wood and Paper | $60.00 | $38.30 | $54.10 | $33.10 | $68.10 | $39.70
Electronics | $65.70 | $40.60 | $59.50 | $35.00 | $75.30 | $42.10
Transportation and Utility | $106.20 | $53.10 | $99.20 | $45.80 | $130.00 | $55.00
Wholesale and Retail | $60.00 | $38.30 | $54.10 | $33.10 | $68.10 | $39.70
Commodity Type | Truck |  | Truck Ferry |  | Truck on Rail | 
 | Short Trips |  |  |  |  | 
 | High Cost | Low Cost | High Cost | Low Cost | High Cost | Low Cost
Agriculture |  |  |  |  |  | 
Metal and Mining |  |  |  |  |  | 
Construction |  |  |  |  |  | 
Chemical |  |  |  |  |  | 
Wood and Paper |  |  |  |  |  | 
Electronics |  |  |  |  |  | 
Transportation and Utility |  |  |  |  |  | 
Wholesale and Retail |  |  |  |  |  | 
SINGLE VALUE OF TIME

## Slide 14: Demand Management Findings
“We will pay for better options”
  High shipment costs + short trips = High willingness-to-pay
  Low shipment costs + long trips = Large time savings required
  Single value of time - oversimplification
Impact of “congestion” pricing
  Tolls > $60 – Most trucks will reroute
  Tolls~ $30 – Short-haul trucks will pay
  Tolls < $10 – No rerouting, but revenue generation
Night-time delivery option – great interest
  Local governance laws
  Maintaining off-hour crew and facility

## Slide 15: Multimodal Assessment Findings
Relocation of distribution centers & mode switching
  Carriers interested in relocation – business efficiency
  Tenants in their third or fourth year most likely to relocate
  Large establishments unlikely to relocate
Multimodal options
  Low preference to switch from truck
  Likely rail adopters are industries with low VoT (bulk)
  Trucks on rail/ferry – greater chance of adoption
Insight into freight decision-making
  Travel time, cost, on-time performance – all critical
  Vary by distance, industry/commodity, transportation cost
  First step for agent-based modeling

## Slide 16: Application of Model Results
Draft EIS and Final EIS study underway
Results integrated with planning model
  Test impact on delay, emissions, peak congestion
Several alternatives tested
  Quantify “switching” from truck
  Quantify “switching” time period
  Cost-benefit analysis for each alternative
  Identify most suitable options

## Slide 17
Any Questions?

## Slide 18: Choice Models
Three unique sets of “choice” models
  Disaggregate models
  Segmented by industry
Truck decision-making
  Route preference – time, toll, on-time reliability
  Day vs. night preference
Multimodal decision-making
  Truck vs. water vs. rail crossings
Distribution center decision-making
  Use – Yes/No
  Relocate – Yes/No

## Slide 19: Route Choice Model
 | Coefficient Description | Value | T-Stat
On-Time Reliability | Low Reliability (<85% on time) | -0.758 | -4.4
 | Medium Reliability (85-90% on time) | -0.275 | -1.4
 | High Reliability (>90% on time) | Base | 
 | Coefficient Description | Value | T-Stat
On-Time Reliability | Low Reliability (<85% on time) | -0.758 | -4.4
 | Medium Reliability (85-90% on time) | -0.275 | -1.4
 | High Reliability (>90% on time) | Base | 
Shipment Cost by Commodity | Agricultural Goods | -0.0108 | -4.4
 | Metal and Mining Goods | -0.0095 | -5.0
 | Construction Goods | -0.0086 | -7.0
 | Chemical Goods | -0.0092 | -6.0
 | Wood and Paper Goods | -0.0109 | -5.6
 | Electronics Goods | -0.0099 | -5.2
 | Transportation and Utility Goods | -0.0060 | -4.1
 | Wholesale and Retail Goods | -0.0068 | -7.0
 | Coefficient Description | Value | T-Stat
On-Time Reliability | Low (<85% on time) | -0.758 | -4.4
 | Medium (85-90% on time) | -0.275 | -1.4
 | High (>90% on time) | Base | 
Shipment Cost by Commodity | Agricultural Goods | -0.0108 | -4.4
 | Metal and Mining Goods | -0.0095 | -5.0
 | Construction Goods | -0.0086 | -7.0
 | Chemical Goods | -0.0092 | -6.0
 | Wood and Paper Goods | -0.0109 | -5.6
 | Electronics Goods | -0.0099 | -5.2
 | Transportation and Utility Goods | -0.0060 | -4.1
 | Wholesale and Retail Goods | -0.0068 | -7.0
Cost Spline | Applied if Cost > $900 | 0.0053 | 5.7
 | Coefficient Description | Value | T-Stat
Travel Time | Time (hrs) | -0.320 | -5.6
 | Coefficient Description | Value | T-Stat
Time (hrs) | Time | -0.320 | -5.6
Time Spline (Applied if TT>12 hrs) | Agricultural Goods | 0.237 | 3.6
 | Metal and Mining Goods | 0.173 | 3.1
 | Construction Goods | 0.166 | 3.2
 | Chemical Goods | 0.146 | 2.4
 | Wood and Paper Goods | 0.156 | 2.8
 | Electronics Goods | 0.135 | 1.7
 | Transportation and Utility Goods | 0.205 | 3.8
 | Wholesale and Retail Goods | 0.174 | 3.6
Time Spline (Applied if TT>25 hrs) | Time | 0.109 | 2.6
Model Fit | Value
Pseudo R2 (0) | 0.415
Pseudo R2 (c) | 0.324
Number of Observations | 716

## Slide 20: Route Choice Model – Values of Time ($/hr)
Single point estimate = over simplification
VoT short trips (<12 hours) = 4* VoT long trips (>24 hours)
VoT for exp. shipments 2-3 times VoT for less exp. shipments
Commodity Type | Low Cost Shipments |  |  | High Cost Shipments |  | 
 | Time<=12 hrs | Time 12-25 hrs | Time>=25 hrs | Time<=12 hrs | Time 12-25 hrs | Time>=25 hrs
Agricultural | $29.63 | $7.69 | - | $58.18 | $15.09 | -
Metal and Mining | $33.68 | $15.47 | - | $76.19 | $35.00 | $9.05
Construction | $37.21 | $17.91 | $5.23 | $96.97 | $46.67 | $13.64
Chemical | $34.78 | $18.91 | $7.07 | $82.05 | $44.62 | $16.67
Wood and Paper | $29.36 | $15.05 | $5.05 | $57.14 | $29.29 | $9.82
Electronics | $32.32 | $18.69 | $7.68 | $69.57 | $40.22 | $16.52
Transportation and Utility | $53.33 | $19.17 | - | - | - | $8.57
Wholesale and Retail | $47.06 | $21.47 | $5.44 | - | $97.33 | $24.67