## Slide 1: Commercial Vehicle Congestion Pricing
TRB Applications Conference – Freight Committee
May 7, 2013
Sashank Musti
Anurag Komanduri
Kimon Proussaloglou
Mark McCourt, Redhill Group
Tarek Hatata, SMG Inc.
Annie Nam, SCAG
Lessons Learned

## Slide 2: Motivation and Goals
Los Angeles and Long Beach - largest port in U.S.
Freight traffic set to double in 20 years
Need to understand freight transportation preferences towards pricing
Congestion mitigation strategies assessment necessary
  Reduce congestion
  Reduce fuel consumption and emissions
  Support increased freight demand
  Increase revenue for the region and improve economy

## Slide 3: Impact of Pricing on Passenger Transportation
Freeway pricing
Express lane pricing
Cordon pricing
Mileage-based pricing (VMT)
Parking fees
Strategy | Trip Generation | Trip Distribution | Mode Choice | Time-of-Day Switch | Traffic Assignment
Freeway Pricing |  |  |  |  | 
Express Lane Pricing |  |  |  |  | 
Area/Cordon Pricing |  |  |  |  | 
Mileage-Based Pricing |  |  |  |  | 
Parking Fee |  |  |  |  | 
=Significant impact; =Some impact; =Minimal impact; =No impact |  |  |  |  | 
Source: Wilbur Smith Associates SCAG Passenger Congestion Pricing
Notes: This slide can be hidden

## Slide 4: Impact of Pricing on Freight Transportation
Strategy | Trip Gen | Trip Dist | Mode Choice | Time-of-Day Switch | Traffic Assignment
Freeway Pricing |  |  |  |  | 
Express Lane Pricing |  |  |  |  | 
Area/Cordon Pricing |  |  |  |  | 
Mileage-Based Pricing |  |  |  |  | 
Parking Fee |  |  |  |  | 
=Significant impact; =Some impact; =Minimal impact; =No impact |  |  |  |  | 
Freeway pricing
Express lane pricing
Cordon pricing
Mileage-based pricing (VMT)
Parking fees – Not tested
Notes: Not a recreational trip
Do not use regular parking spots

## Slide 5: Market Segments that were Surveyed
Freight decision making habits classified by
  Trips beginning/ending at facility
  Own/lease trucks
  Commodity flow/service trucks
  Identifiable using NAICS code
Market segments
  Own trucks
    Carriers
    Shippers with trucks
    Receivers with trucks
    Service trucks
  Do not own trucks
    Shippers with no trucks
    Receivers with no trucks
Market Segment | Trips Beginning at Facility | Trips Ending at Facility | Commodity Flow | Unique NAICS Code
Carriers |  |  |  | 
Market Segment | Trips Beginning at Facility | Trips Ending at Facility | Commodity Flow | Unique NAICS Code
Carriers |  |  |  | 
Shippers with Trucks |  |  |  | 
Market Segment | Trips Beginning at Facility | Trips Ending at Facility | Commodity Flow | Unique NAICS Code
Carriers |  |  |  | 
Shippers with Trucks |  |  |  | 
Receivers with Trucks |  |  |  | 
Market Segment | Trips Beginning at Facility | Trips Ending at Facility | Commodity Flow | Unique NAICS Code
Carriers |  |  |  | 
Shippers with Trucks |  |  |  | 
Receivers with Trucks |  |  |  | 
Service Trucks |  |  |  | 
Market Segment | Trips Beginning at Facility | Trips Ending at Facility | Commodity Flow | Unique NAICS Code
Carriers |  |  |  | 
Shippers with Trucks |  |  |  | 
Receivers with Trucks |  |  |  | 
Service Trucks |  |  |  | 
Shippers with no Trucks |  |  |  | 
Market Segment | Trips Beginning at Facility | Trips Ending at Facility | Commodity Flow | Unique NAICS Code
Carriers |  |  |  | 
Shippers with Trucks |  |  |  | 
Receivers with Trucks |  |  |  | 
Service Trucks |  |  |  | 
Shippers with no Trucks |  |  |  | 
Receivers with no Trucks |  |  |  | 
Notes: Sampling plan by market segment, establishment size (#employees), establishment location, land use at origin and destination

## Slide 6: Stated Preference (SP) Surveys
A total of 6,400 “Trade-off” questions
  1200 establishments recruited
  No toll scenarios
  Toll scenarios
    Truck route 1 vs. Truck route 2
    Truck peak vs. Truck off-peak
Increasing order of difficulty in SP experiments
  Adjusted for short vs. long movements
  Adjusted for market segment
Experimental design adjustments made by
  Time-of-day of travel
  Origin/destination
  Routing decision control
  Time-of-day decision control

## Slide 7: Complex Experimental Design
Current Behavior |  |  |  | Behavioral Responses Tested |  |  | 
Travel During Peak | Travel to Key Areas | Control Route | Control TOD | Freeway & Express Lane Pricing Route Choice | Freeway & Express Lane Pricing TOD Choice | Area Pricing TOD Choice | VMT Pricing TOD Choice
 |  |  |  |  |  |  | 
Current Behavior |  |  |  | Behavioral Responses Tested |  |  | 
Travel During Peak | Travel to Key Areas | Control Route | Control TOD | Freeway & Express Lane Pricing Route Choice | Freeway & Express Lane Pricing TOD Choice | Area Pricing TOD Choice | VMT Pricing TOD Choice
 |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 
Current Behavior |  |  |  | Behavioral Responses Tested |  |  | 
Travel During Peak | Travel to Key Areas | Control Route | Control TOD | Freeway & Express Lane Pricing Route Choice | Freeway & Express Lane Pricing TOD Choice | Area Pricing TOD Choice | VMT Pricing TOD Choice
 |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 
Current Behavior |  |  |  | Behavioral Responses Tested |  |  | 
Travel During Peak | Travel to Key Areas | Control Route | Control TOD | Freeway & Express Lane Pricing Route Choice | Freeway & Express Lane Pricing TOD Choice | Area Pricing TOD Choice | VMT Pricing TOD Choice
 |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 
 |  |  |  | Not Recruited |  |  | 
Current Behavior |  |  |  | Behavioral Responses Tested |  |  | 
Travel During Peak | Travel to Key Areas | Control Route | Control TOD | Freeway & Express Lane Pricing Route Choice | Freeway & Express Lane Pricing TOD Choice | Area Pricing TOD Choice | VMT Pricing TOD Choice
 |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 
 |  |  |  | Not Recruited |  |  | 
 |  |  |  |  |  |  | 
Current Behavior |  |  |  | Behavioral Responses Tested |  |  | 
Travel During Peak | Travel to Key Areas | Control Route | Control TOD | Freeway & Express Lane Pricing Route Choice | Freeway & Express Lane Pricing TOD Choice | Area Pricing TOD Choice | VMT Pricing TOD Choice
 |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 
 |  |  |  | Not Recruited |  |  | 
 |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 
 |  |  |  | Not Recruited |  |  | 
 |  or  |  |  or  |  |  |  | 
 |  or  |  |  or  | Not Recruited |  |  | 

## Slide 8: SP Experiment Route Choice – Freeway Pricing
In the future, some of the highways could be tolled for both passenger and commercial vehicles in exchange for faster speeds and more reliable travel times.
Which of the two options would you choose?
Your choices are… | Option A | Option B
Route | Current Route | Alternate Route
Distance | 60 miles | 63 miles
Transit Time | 1 hour 54 minutes | 2 hours 24 minutes
Reliability (on-time delivery) | 97% | 85%
Total Toll | $10 | $0
Option B
Option A
Which of the three options above would you choose? (Please circle one)

## Slide 9: SP Experiment Time-of-Day Choice – Express Lane Pricing
Suppose these were your transportation options to ship your goods for your regular shipment, new Truck-Only Express Lanes that provide faster, more reliable travel times may be constructed
Your choices are… | Option A | Option B | Option C
Time of Day | During Peak Period | Before Peak Period | After Peak Period
Distance | 60 miles | 60 miles | 60 miles
Transit Time | 2 hours 48 minutes | 2 hours 12 minutes | 2 hours 15 minutes
Reliability (on-time delivery) | 90% | 91% | 96%
Total Toll | $0 | $20 | $14
Option B
Option A
Option C
Which of the three options above would you choose? (Please circle one)
Notes:   Tolls varied between 13.3 cents and 50 cents a mile for lane pricing experiments.
  Tolls in freeway pricing experiments varied between 11.7 cents and 43.3 cents per mile.
  In mileage-based pricing experiments, tolls were varied between 2.5 cents and 14 cents per mile.
  However, cordon pricing tolls were varied over a fixed range since they are not dependent on the distance traveled.
On-time performance measures were varied between 83 and 97 percent. Peak period on-time performance measures were considerably lower than off-peak on-time performance measures.
Separate designs were developed for short haul (<300 miles) and long haul (>300 miles) trips. This was implemented to ensure that the toll values for the very long haul trips were capped since these long haul trips are only likely to be tolled for a small segment of their trip.

## Slide 10: Impact of Travel Time Savings
Preference for tolled route increases with travel time savings
Chart: Percentage TT Savings in the Tolled Route
| Under 10% | Between 11 and 20% | Between 21 and 30% | Between 31 and 40% | Between 41 and 50% | Greater than 50%
 | 0.34211 | 0.3625 | 0.36287 | 0.41481 | 0.47826 | 0.49774
Chart: Percentage Travel Time Savings Offered in the Before Peak Period
| 0 to 9% | 10 to 15% | 20 to 35% | >35%
Before Peak | 0.34146 | 0.36199 | 0.43012 | 0.45073
Preference for off-peak periods increase with travel time savings
Chart: Percentage Travel Time Savings Offered in the After Peak Period
| 0 to 10% | 10 to 20% | 20 to 40% | >40%
After Peak | 0.23478 | 0.41695 | 0.46495 | 0.47647

## Slide 11: Impact of Tolls
Chart: 
| 1 to 15 c/mile | 16 to 30 c/mile | 31 to 45 c/mile | >45 c/mile
Tolled Route | 0.4918 | 0.45455 | 0.40292 | 0.2963
Tolls varied from 0 cents/mile to 50 cents/mile
As tolls increase, preference for non-tolled route is greater

## Slide 12: SP Experiment Model Results – Time-of-Day Choice
Toll | Land use is Transportation-warehousing | -0.0721 | -10.8
 | Land use is Manufacturing | -0.0447 | -6.8
 | Land use is Retail | -0.0895 | -6.8
 | Land use is Wholesale | -0.0230 | -3.3
 | All Other Land Uses | -0.0559 | -6.2
 | Coefficient Description | Value | T-Stat
Travel Time (hours) | Land use is Transportation – warehousing | -0.0172 | -3.9
 | Land use is Retail | -0.0135 | -2.7
 | All other land uses | Base | 
 | Coefficient Description | Value | T-Stat
Before Peak Constant | Land use is Transportation-warehousing | 0.358 | 3.7
 | Land use is Manufacturing | 0.243 | 2.0
 | Land use is Retail | 0.415 | 2.7
 | All Other Land Uses | 0.200 | 1.7
On-Time Reliability | Low (<92% on time) | -0.256 | -3.5
 | Medium (92-93% on time) | -0.142 | -2.2
 | High (>93% on time) | Base | 
Model Fit | Value
Pseudo R2 (c) | 0.072
Number of Observations | 3,307
After Peak Constant | Land use is Transportation-warehousing | 0.243 | 2.5
 | Land use is Manufacturing | 0.215 | 1.8
 | Land use is Retail | 0.407 | 2.5
 | All Othe Land Uses | 0.131 | 1.1

## Slide 13: SP Experiment Model Results – Time-of-Day Choice
Toll ($’s) | Land use is Transportation-warehousing | -0.0721 | -10.8
 | Land use is Manufacturing | -0.0447 | -6.8
 | Land use is Retail | -0.0895 | -6.8
 | Land use is Wholesale | -0.0230 | -3.3
 | All Other Land Uses | -0.0559 | -6.2
 | Coefficient Description | Value | T-Stat
Travel Time (hours) | Land use is Transportation – warehousing | -0.0172 | -3.9
 | Land use is Retail | -0.0135 | -2.7
 | All other land uses | -0.0088 | -2.7
 | Coefficient Description | Value | T-Stat
Before Peak Constant | Land use is Transportation-warehousing | 0.358 | 3.7
 | Land use is Manufacturing | 0.243 | 2.0
 | Land use is Retail | 0.415 | 2.7
 | All Other Land Uses | 0.200 | 1.7
On-Time Reliability | Low (<92% on time) | -0.256 | -3.5
 | Medium (92-93% on time) | -0.142 | -2.2
 | High (>93% on time) | Base | 
Model Fit | Value
Pseudo R2 (c) | 0.072
Number of Observations | 3,307
After Peak Constant | Land use is Transportation-warehousing | 0.243 | 2.5
 | Land use is Manufacturing | 0.215 | 1.8
 | Land use is Retail | 0.407 | 2.5
 | All Othe Land Uses | 0.131 | 1.1

## Slide 14: Conclusions
Models allow for multi-strategy testing purposes
Strong preference for non-tolled routes & off-peak periods
Empirical values of time
  Vary from $8/hour to $23/hour
  Vary by land use, distance, pricing strategy & commodity type
Results integrated with planning model
  Test impact on delay, emissions, peak congestion
Study framework can be applied to other regions

## Slide 15
Any Questions?

## Slide 16: Experiments & Alternatives Available
Type | Experiment | Time Period | Same Route + Toll | Same Route + Free | Switch Route + Toll | Switch Route + Free
Route Choice | Freeway Pricing | No Change |  |  |  | 
 | Express Lane Pricing |  |  |  |  | 
Time-of-Day Choice | Freeway Pricing | No Change Shift Earlier Shift Later |  |  |  | 
 | Express Lane Pricing |  |  |  |  | 
 | Area/Cordon Pricing |  |  |  |  | 
 | Mileage-Based Pricing |  |  |  |  | 
Notes: Hide this slide???

## Slide 17: Focus Groups
Very successful – in-depth discussions
Focus group findings
  Slow is ok – but, we need reliable service
  Last mile service works against rail + no control over routing
  Distribution center locations prevent me from moving
  Lot of time (and money) wasted in local moves
  Safety, damage considerations are essential
  Willing to pay for improved service
  Cost, travel time & on-time performance critical
Establishments willing to try other options