## Slide 1: FHWA Traveler ANALYSIS FRAMEWORK
Auto, Air, and Rail Tables
March 18, 2013
Krishnan Viswanathan, CDM Smith
Colin Smith, RSG
Bhargava Sana, RSG

## Slide 2: Agenda
Purpose
Auto
Air
Rail
Geography

## Slide 3: FHWA Traveler Analysis Framework
VMT Forecasting and Analysis Model
Long Distance Passenger Inter-regional Travel Origin Destination Data
National Travel Model
Long distance passenger travel modal choice model
Freight and passenger integration, and multimodal analysis

## Slide 4: Project Objective and Deliverables
To provide foundational information for FHWA, and the U.S. DOT in analyzing national and regional significant projects, corridors, policy initiatives, interstate commerce, and role of Federal programs.
Long-distance inter-regional multimodal passenger travel origin destination matrix for 2008 and 2040
A set of documented and transparent methodologies where other agencies and organizations can gain insight knowledge to expedite future developments

## Slide 5: Project Team
FHWA
Daniel Jenkins, PM
Roger Mingo Associates
Roger Mingo
CDM Smith
Krishnan Viswanathan
Don Vary
RSG, Inc.
Colin Smith
Bhargava Sana

## Slide 6: Data Examined
1995 ATS
2001 NHTS
DK Schifflet (2008)
CA Long Distance Survey (2011)
Ohio Long Distance Survey (2002-2003)

## Slide 7: AUTO

## Slide 8: Data Examination Conclusions
No existing data are readily available to cover the base year of 2008 for the entire nation
Base year 2008 OD data – need to be synthesized
2040 OD data – need to be forecasted (synthesized)
The only national comprehensive data available is the 1995 ATS

## Slide 9: Data Synthesis Method Exploration
Methods desired are ones having the following characteristics:
The least number of input data items needed
Input data items are readily available
Statistically valid

## Slide 10: 2008 and 2040 Trip Production and Attraction
Trip Productions
  Business = 0.47692 x Population (R2 = 0.90)
  Non Business = 2.19893 x Population (R2 = 0.95)
  Population data are from Census for 2008 and from Woods and Poole for 2040
Trip Attractions
  Business = 1.09773 x QCEW Employment (R2 = 0.89)
  Non Business = 6.573 x QCEW Leisure & Hospitality and Service Providing industry Employment (R2 = 0.91)
  QCEW data from BLS for 2008 and Woods and Poole employment data for 2040

## Slide 11: Trip Distribution – Formation of OD Pair
Destination Choice Formulation
  Businessj = 0. 536*(LN(Householdsi) + 2*LN(Employmentj)) -2.81*LN(Distanceij)
  Non Businessj = 0.584*(LN(Householdsi)+2*LN(Employmentj )) - 2.47*LN(Distanceij )
The utilities are applied at the county level to obtain county to county flow table

## Slide 12: Special Generators
National Parks
  Obtain 2008 national park visitors
  Obtain percent of national park visits that come from 100 +miles from NPS surveys (collected between 2003 to 2011)
    Yosemite, Grand Canyon, Shenandoah, Colonial National Historical Park (NHP) (provided mode and resident state information)
    Smoky Mountain, Boston NHP, Congaree (provided resident state information)
  Apply this percent to total 2008 NPS visitors
  Resulting in NPS visitors that come from 100+ miles by auto
  Apply non business destination choice model

## Slide 13: Special Generators
Cross Border Traffic
  Obtain 2008 in bound passengers from BTS
  Calculate percent of long distance trips from Statistics Canada border crossing information
  Apply this percent to total 2008 in bound passenger data
  Resulting in border crossing trips that come from 100+ miles by auto
  Allocate these trips to the county where the border crossing is located
  Apply non business destination choice model

## Slide 14: 2008 Non Business Trip Productions

## Slide 15: 2008 Business Trip Productions

## Slide 16: 2008 Non Business Trip Attractions

## Slide 17: 2008 Business Trip Attractions

## Slide 18: Trip Length Distribution Auto
Distance Bin | Estimated 2008 Auto | 1995 ATS Auto | 2002/2003 Ohio Long Distance Survey | 2008/2011 California Long Distance Survey (Enhanced) | 2008/2011 California Long Distance Survey (Reduced) |  | Estimated 2040 Auto
100 to 200 miles | 52.6% | 54.9% | 59.7% | 59.3% | 60.1% |  | 50.5%
200 to 300 miles | 18.8% | 20.8% | 15.2% | 13.9% | 13.6% |  | 18.0%
300 to 400 miles | 10.1% | 8.9% | 9.7% | 19.6% | 19.2% |  | 9.8%
400 to 500 miles | 6.2% | 4.5% | 5.5% | 6.4% | 6.2% |  | 5.9%
500 to 600 miles | 4.3% | 2.8% | 3.6% | 0.7% | 0.9% |  | 4.1%
600 to 700 miles | 3.1% | 1.8% | 1.9% | 0.1% | 0.1% |  | 3.0%
700 to 800 miles | 2.2% | 1.3% | 1.8% | 0.0% | 0.0% |  | 2.2%
800 to 900 miles | 1.6% | 1.0% | 1.1% | 0.0% | 0.0% |  | 1.7%
900 to 1000 miles | 1.2% | 0.7% | 0.7% | 0.0% | 0.0% |  | 1.3%
More than 1000 miles | 2.6% | 3.3% | 0.8% | 0.0% | 0.0% |  | 3.5%

## Slide 19: Summary Results*
 | Auto | Air | Rail | Bus
Share 1995 | 81.3% | 16.1% | 0.5% | 2.0%
Share 2008 | 82.2% | 14.5% | 0.6% | 2.3%
Share 2040 | 80.1% | 16.7% | 0.6% | 2.2%
Total Growth (1995 to 2008) | 50% | 34% | 81% | 68%
Annual Total Growth (1995 to 2008) | 3.2% | 2.3% | 4.7% | 4.1%
Total Growth (2008 to 2040) | 43% | 69% | 46% | 38%
Annual Total Growth (2008 to 2040) | 1.1% | 1.6% | 1.2% | 1.0%
*We have not included trip numbers because FHWA is currently reviewing the products (and possibly adjusting the bus and geography aggregation). All should be released by the end of the summer.

## Slide 20: From Los Angeles County Destination Zones with more than 500,000 auto trips
BUSINESS
NON BUSINESS

## Slide 21: From Los Angeles County Destination Zones with more than 100,000 auto trips
BUSINESS
NON BUSINESS

## Slide 22: From Los Angeles County Destination Zones with more than 50,000 auto trips
BUSINESS
NON BUSINESS

## Slide 23: From Los Angeles County Destination Zones with more than 10,000 auto trips
BUSINESS
NON BUSINESS

## Slide 24: From Los Angeles County Destination Zones with more than 5,000 auto trips
BUSINESS
NON BUSINESS

## Slide 25: Geography
FAF MSA further separated by State lines
Additional Urban Areas
Further division of the balance of a State (rural area) into geo-contiguous zones

## Slide 26: Geography

## Slide 27: AIR and Rail

## Slide 28: Overview of the approach: 2008 Air and Rail
Objective: develop 2008 county to county air passenger and rail passenger trip tables including access and egress portion of trips
Airport to airport OD from DB1B 10% ticket sample, augmented with T-100 data
Airport access and egress distributions based on either ground access survey data or distribution models estimated using survey data
Station to station OD data obtained from AMTRAK, adjusted to include California Thruway bus passengers
Station access and egress distributions based on models estimated from airport ground access surveys and then calibrated with California survey data

## Slide 29: Methodology for Air* OD Table
Sum OD tables for all airport pairs to derive total county to county trip table
Airport A
Airport B
Origin: County I
Origin: County II
Origin: County III
25%
25%
50%
1,000,000 passengers
Destination: County IV
Destination: County V
50%
50%
OD table for airport pair A to B
DB1B data
Airport access surveys /
trip distribution models
 | Destination: County IV | Destination: County V
Origin: County I | 125,000 passengers | 125,000 passengers
Origin: County II | 250,000 passengers | 250,000 passengers
Origin: County III | 125,000 passengers | 125,000 passengers
*Rail OD table uses a similar approach, with AMTRAK data replacing DB1B data, and different trip distribution models used

## Slide 30: Data Sources
10% sample of airline tickets from reporting carriers (carriers with operating revenues of $20 million or more)
Includes ticket carrier, number of passengers, fare class, flight distance and more
Restricted international data obtained for this project, includes the domestic portion of international itineraries
DB1B
Air Carrier Statistics (Form 41 Traffic) is full enumeration of passenger air travel (not sampled)
Contains domestic and international airline market and segment data
Number of passengers for each reporting carrier by airport pair
T-100
AMTRAK
Full enumeration of AMTRAK tickets from 2008
Boardings and alightings at 518 stations (18,650 station pairs)
Data obtained directly from AMTRAK: detailed data are confidential: permission received for RSG to process
Data consistent with published station boarding and alighting data

## Slide 31: Validation: Trip Length Distribution 2008
Overall trip distribution of DB1B data and county to county trips: results almost identical, confirmation that trip table processing has not introduced errors
Chart: Air Trip Length Distribution
| 0 to 100 | 100 to 200 | 200 to 300 | 300 to 400 | 400 to 500 | 500 to 600 | 600 to 700 | 700 to 800 | 800 to 900 | 900 to 1000 | 1000 to 1100 | 1100 to 1200 | 1200 to 1300 | 1300 to 1400 | 1400 to 1500 | 1500 to 1600 | 1600 to 1700 | 1700 to 1800 | 1800 to 1900 | 1900 to 2000 | 2000 to 2100 | 2100 to 2200 | 2200 to 2300 | 2300 to 2400 | 2400 to 2500 | 2500 to 2600 | 2600 to 2700 | 2700 to 2800 | 2800 to 2900 | 2900 to 3000 | 3000 to 3100 | 3100 to 3200 | 3200 to 3300 | 3300 to 3400 | 3400 to 3500 | 3500 to 3600 | 3600 to 3700 | 3700 to 3800 | 3800 to 3900 | 3900 to 4000 | 4000 to 4100 | 4100 to 4200 | 4200 to 4300 | 4300 to 4400 | 4400 to 4500 | 4500 to 4600 | 4600 to 4700 | 4700 to 4800 | 4800 to 4900 | 4900 to 5000 | > 5000
DB1B | 0.0050599 | 0.015997 | 0.056962 | 0.078186 | 0.066869 | 0.062581 | 0.065386 | 0.059502 | 0.062537 | 0.080545 | 0.071269 | 0.045449 | 0.032205 | 0.02198 | 0.029196 | 0.027192 | 0.01777 | 0.026818 | 0.016566 | 0.018191 | 0.013229 | 0.018514 | 0.017818 | 0.020337 | 0.025127 | 0.02193 | 0.0075062 | 0.0022551 | 0.00092692 | 0.0011519 | 0.00043682 | 0.00028638 | 0.00068067 | 0.00091665 | 0.00031144 | 5.5854e-05 | 0.00016469 | 0.00086006 | 0.00060194 | 0.0005141 | 0.00017882 | 0.00053707 | 0.00065428 | 0.00034847 | 0.00073623 | 0.00026353 | 0.00044177 | 0.00056411 | 0.00088902 | 0.0010509 | 0.00045189
Model | 0.0045847 | 0.014576 | 0.055535 | 0.080673 | 0.066336 | 0.063542 | 0.064467 | 0.061361 | 0.064168 | 0.077799 | 0.070646 | 0.046368 | 0.033333 | 0.023619 | 0.029249 | 0.02496 | 0.019241 | 0.025232 | 0.016841 | 0.018913 | 0.013826 | 0.017585 | 0.017214 | 0.020629 | 0.025006 | 0.020875 | 0.0077433 | 0.002498 | 0.0010787 | 0.0011181 | 0.00045988 | 0.00029828 | 0.00067552 | 0.00094131 | 0.00029381 | 6.0561e-05 | 0.00018033 | 0.00079864 | 0.00059532 | 0.00056217 | 0.00018481 | 0.00055394 | 0.00062804 | 0.00035658 | 0.00069682 | 0.00030743 | 0.00045067 | 0.00057276 | 0.00090525 | 0.00099697 | 0.0004653

## Slide 32: Validation: Air Access Trip Lengths 2008
Air access trip distribution compares well with observed distributions from surveys
Some differences due to differences between incomplete set of survey airports and complete set of airports represented in the model
Airport access is limited to 150 miles except for cases where there are no accessible airports; longer access trips account for ~2% of air trips according to survey data
Chart: Airport Access Trip Length Distribution
| 0-10 | 10-20 | 20-30 | 30-40 | 40-50 | 50-60 | 60-70 | 70-80 | 80-90 | 90-100 | 100-110 | 110-120 | 120-130 | 130-140 | 140-150 | >150
Survey | 0.038217 | 0.048471 | 0.33534 | 0.19901 | 0.11165 | 0.079136 | 0.058203 | 0.019588 | 0.031926 | 0.016406 | 0.015425 | 0.010788 | 0.0069386 | 0.0050284 | 0.0029055 | 0.020966
Model | 0.12224 | 0.094053 | 0.23409 | 0.15512 | 0.086148 | 0.098833 | 0.031331 | 0.066208 | 0.021124 | 0.014491 | 0.014912 | 0.013125 | 0.021388 | 0.012035 | 0.0089973 | 0.0059016

## Slide 33: Validation: Trip Length Distribution 2008
Overall trip distribution of rail county to county trips
Chart: Rail Trip Length Distribution
| 0 to 100 | 100 to 200 | 200 to 300 | 300 to 400 | 400 to 500 | 500 to 600 | 600 to 700 | 700 to 800 | 800 to 900 | 900 to 1000 | 1000 to 1100 | 1100 to 1200 | 1200 to 1300 | 1300 to 1400 | 1400 to 1500 | 1500 to 1600 | 1600 to 1700 | 1700 to 1800 | 1800 to 1900 | 1900 to 2000
StationOD | 0.36963 | 0.3593 | 0.15695 | 0.032059 | 0.018368 | 0.011288 | 0.01074 | 0.017437 | 0.0046325 | 0.0062106 | 0.0027253 | 0.0013612 | 0.0015736 | 0.0020127 | 0.0009065 | 0.00043149 | 0.00084379 | 0.0029613 | 0.00056827 | 0
Model | 0.36277 | 0.35782 | 0.16282 | 0.0346 | 0.01786 | 0.011499 | 0.011049 | 0.017069 | 0.0051887 | 0.0058215 | 0.0028955 | 0.0014649 | 0.0014095 | 0.0019219 | 0.00092423 | 0.00049937 | 0.0010015 | 0.002804 | 0.00058142 | 5.645e-06

## Slide 34: Validation: Rail Access Trip Lengths 2008
Rail access trip distributions match observed data from CHRSA Survey relatively well
Peakiness in the model distribution caused by using intra-county distances from ORNL skim data meaning that all trips from major counties, e.g. Cook, Los Angeles, New York, give same access distance
Chart: Rail Access Trip Length Distribution
| 0-10 | 20-10 | 20-30 | 30-40 | 40-50 | 50-60 | 60-70 | 70-80 | 80-90 | 90-100 | 100-110 | 110-120 | 120-130 | 130-140 | 140-150 | >150
Survey | 0.38292 | 0.30898 | 0.11004 | 0.084507 | 0.048415 | 0.028169 | 0.0096831 | 0.006162 | 0.0035211 | 0.0026408 | 0.0026408 | 0.0017606 | 0.00088028 | 0 | 0 | 0.0096831
Model | 0.35495 | 0.11546 | 0.19149 | 0.11266 | 0.034879 | 0.1005 | 0.023992 | 0.018176 | 0.010762 | 0.0078085 | 0.0075256 | 0.0054633 | 0.0070989 | 0.0052076 | 0.0040168 | 1.4319e-05

## Slide 35: Overview of Approach: 2040 Air OD
Based on 2040 airport to airport demand forecast from FAA
Develop revised airport access distributions using 2040 population, employment and enplanements forecasts
Data sources:
  2040 FAA airport to airport forecast
  2040 forecasts of population and employment by county (W&P CEDDS)
Overall growth 2008 to 2040 is 73%
Chart: 2008 Airport Origin Passengers from DB1B
Growth factor range is large for smaller airports, but narrower for larger airports
50-100% growth

## Slide 36: Overview of Approach: 2040 Rail OD
Approach is generally the same as that to develop the 2040 Air OD tables except for lack of future forecasts of rail activity
Data sources:
  2008 station to station ODs from AMTRAK
  2008 population and employment data by county
  2040 forecasts of population and employment by county(W&P CEDDS)
A catchment county area designated around each station based on 2008 results
Growth factor for each station OD pair calculated using population and employment growth in catchment area
Overall 2008 to 2040 growth is 46%
Growth is not based on any assumptions about investments in new infrastructure, e.g. high speed rail

## Slide 37: Visualization example: air trips from Broward County, Florida

## Slide 38: Next Steps

## Slide 39: Final Products
OD flow data by mode (number of trips by mode) for the identified 226 zones

## Slide 40: Recommendations and Observations
1: The to be released OD data shall be recognized as synthesized data and shall be used as a starting point for any other project and program.
2: Additional verification and analysis are strongly recommended.
3: New national comprehensive passenger flow OD data survey shall be conducted.

## Slide 41: Thank you!