## Slide 1: Tests of Improved Methods of Modeling Demand for Bicycling and Walking in the Seattle Region
Mark Bradley
&
John Bowman

## Slide 2: Acknowledgments
Work done as part of NCHRP 8-78A: Estimating Bicycle and Pedestrian Demand and for Planning and Project Development
  Richard Kuzmyak, others at Renaissance Planning
  Jerry Walters, others at Fehr & Peers
  Keith Lawton, Kara Kockelman, …..
Data provision:
  Stefan Coe and others at PSRC, Seattle
  Jeff Frkonja and others at RSG
  Orion Greene and others at U.Washington

## Slide 3: Objectives
Establish relationships between bicycle and pedestrian demand and….
Infrastructure
  Provision of bike paths and lanes
  Provision of sidewalks
  Street network connectivity
  Other aspects of routes (grade, traffic flow, etc.)
Urban design
  Density of housing and employment
  Variety of land uses (mixed use entropy)
  Provision / location of transit stops
  Local versus regional accessibility

## Slide 4: Research directions…..
In conventional zone-based models, most walk and bike trips are intra-zonal or between adjacent zones >>> very little relevant information to predict choices
Two main directions
Add more detail and Create detailed
data in advanced small-area models
regional forecasting using map-based/
models GIS framework

## Slide 5: Test of methods for advanced regional modeling
Model estimation with parcel-level data
Use of distances from an all-streets network
Use of distance-decay buffering methods
Use of detailed sidewalk data
Use of detailed bike network data, with paths based on SFCTA bike route choice model
These are all methods that can be applied in the PSRC activity-based regional model
(Model estimation data was done using the same Daysim software that can apply the models)

## Slide 6: Use of all-streets network
Calculate shortest-path distances for all pairs of street nodes (intersections) within 2 miles of each other.
  250 million node pairs
  Used DTALite from Univ. of Utah
Use the nearest node for each parcel (also works well with Census block “microzones”)
Use the distances in three ways:
  Calculating distance and time for all short trips
  Calculating walk distance to transit stops
  Buffering land use measures around each parcel

## Slide 7: Buffering
Objective is to get comparable measures of urban design around each parcel, not relying on artificial boundaries
Typical buffering approach is to simply add up all attributes within a fixed radius of any point, using crow-fly distance
Three potential drawbacks of typical approach:
  All attributes are counted the same, regardless of distance
  Boundary effects with parcels at the buffer’s edge
  Crow-fly distance may be very different from true walking/biking distance

## Slide 8: Buffering approach used Distance based on node-to-node shortest path Distance-decay weights based on logistic curves Two buffers – longer one may be better for bike
Chart: 

## Slide 9: Attributes that are buffered
Households
Employment, in 9 different categories
School enrollment, K-12 and university
Paid parking spaces, and average price
Public open space area (parks, etc.)
Transit stops
Street intersections (1, 3, and 4+ nodes)
Avg. percent elevation gain along links
Length of street links, classified by presence of Class 1 and Class 2 bike path/lanes
Length of street links, classified by sidewalk presence / speed limit

## Slide 10: Special data used in buffering
Sidewalk data from U.Washington, for all King County street segments, each side of street:
  Presence of sidewalk (full, partial, none)
  Speed limit (proxy for pedestrian safety risk)
Bike network data, provided by PSRC for King County
  Used in buffering
  Also processed into origin-destination path skims, using the SFCTA Bike Route Choice model

## Slide 11: Bike path attributes
Attributes, across multiple paths, weighted by path selection probability:
  Path distance
  Fraction of distance on Class 1 bike path
  Fraction of distance on Class 2 bike lane
  Fraction of distance wrong-way on one-way links
  Fraction elevation gain along the path
  Number of turns per mile
  A “logsum” (inclusive value) across paths/attributes
Four market segments: male / female x
work / non-work

## Slide 12: Types of models estimated
Tour generation and trip chaining
Tour mode choice, using only origin information (and accessibility across destinations)
Tour mode choice, using origin-to-destination information
  Using separate bike path attributes
  Using bike path logsum
Data from the 2006 PSRC Household Travel Survey

## Slide 13: Tour generation and complexity
Iterative stop/repeat model w/15 alternatives:
  Not make a tour
  Make a tour for one of 14 combinations….
    7 tour purposes
    2 tour types (single stop vs. multiple stop)
Modeled generation of home-based tours for 21,020 person days
  Average 1.1 tours/person day
  43% of tours w/multiple stops
  Range 51% for work to 29% for recreation

## Slide 14: Results
Short distance buffer effects are very strong: People who live very near attractions tend to make more tours for those purposes
Longer-distance accessibility measures also important for most purposes
People who live in areas that are more amenable to walk, bike and transit tend to make more tours, but those tours tend to have fewer stops per tour
  Higher presence of Class 1 bike paths
  Smaller elevation gain along streets
  Shorter distance to transit stops

## Slide 15: Mode choice models
For tours within King County (majority of tours in the Puget Sound region)
Separate models for 5 purposes:
% walk % bike % transit
Home > Work 3 3 12
Home > School 10 2 6
Home > Recreation 14 2 1
Home > Other 11 1 2
Work-based 40 1 2
(unweighted percentages)

## Slide 16: Significance of buffer variables (In terms of t-statistics – red denotes “wrong” sign)
Tour purpose | Work | School | Recre-ation | Other | Work-based
Walk- Street network distance | -9.7 | -9.8 | -13.4 | -14.2 | -7.7
Walk -Buffer 1 net intersection density |  |  |  | 2.0 | 3.6
Walk- Buffer 1 avg. fraction elevation gain | -3.5 | -0.3 | -1.0 | -1.4 | 
Walk- Buffer 1 percent no sidewalk | -1.6 |  | -2.7 | -3.0 | 
Bike- Buffer 2 fraction Class 1 path | 2.9 | 2.2 |  |  | 
Bike- Buffer 2 net intersection density | 4.6 |  |  |  | 
Bike- Buffer 2 avg. fraction elevation gain | -3.0 |  |  |  | 
Transit- Origin buffer 1 transit stops | 5.4 | -1.6 | -1.6 | 1.0 | 
Transit- Destination buffer 1 transit stops | 2.0 | 1.4 | 2.7 | 2.9 | 3.0
Transit- Origin buffer 1 net intersection den | 2.1 |  |  |  | 
Transit- Origin buffer 1 pct. no sidewalk |  | -1.2 |  |  | 
Transit- Destin. buffer 1 pct. no sidewalk |  | -1.1 | -2.6 |  | 

## Slide 17: Significance of bike path variables (In terms of t-statistics – red denotes “wrong” sign)
Tour purpose | Work | School | Recre-ation | Other | Work-based
Distance | -8.9 | -2.1 | -1.7 | -2.7 | -0.8
Fraction Class 1 path | 4.5 | -0.2 | -0.2 | 1.3 | 
Fraction Class 2 lane | 0.0 | -1.0 | -1.2 | 1.2 | 
Fraction wrong way | -0.3 | -0.5 | -1.2 | -0.7 | 
Turns per mile | -1.6 | -0.2 | -0.4 | 1.3 | 
Fraction rise | 2.1 | -1.9 | -0.7 | -0.2 | 
Inclusive logsum | 5.6 | 1.4 | 2.3 | 3.1 | 0.9

## Slide 18: Discussion
Estimated effects are generally in the expected directions, but without much statistical precision or significance.
They are feasible for use in advanced regional or local forecasting models, but there is still much room for improvement.
This has also been an issue with modeling auto vs. transit mode choice > Reaching “consensus” has required decades of RP and SP research.
But, for walk and bike demand, there are additional challenges…

## Slide 19: Data challenges
Collinearity: Detailed spatial data on land use and infra-structure tends to shows high correlation across different variables.
Mutual causality: Cities often put sidewalks where people are already walking, and bike lanes where people are already cycling.
Self-selection: People who walk and/or bike tend to relocate to walkable/bikeable areas.
Scarcity: A lack of systematic count data for calibration and validation.
We need before-and-after panel surveys and count data in areas with substantial land use and/or infrastructure changes

## Slide 20: Other forecasting challenges
Changing context: The design of pedestrian and cycling infrastructure is in a state of rapid evolution. > Difficult to define and collect up-to-date attribute data
Safety is a key issue, and is often related to site-specific details of road and intersection geometry > Difficult to capture in models.
Feedback effects: Actual and perceived safety depends a great deal on the number of cyclists and pedestrians relative to the number of vehicles on the road. (The opposite of capacity constraint.)
Information and experience: For bicycling in particular, few potential cyclists have much experience using local routes, and even fewer have experienced cycling in much safer conditions (e.g. Holland, Denmark).