## Slide 1: Use of Non-Traditional Data in Simulation Model Building
TRB National Planning Applications Conference
Matthew Juckes & Bernard Alpern
Monday, May 6th, 2013
Notes: 1

## Slide 2: Project Goals
I-78 EB Ramp Metering Evaluation
  Phase 1 –Strategy Screening
    Study of various possible lane management programs along the I-78 corridor in New Jersey (AM Peak EB Direction Only)
  Phase 2 – Strategy Testing
    Modeling of Ramp Metering and Variable Speed Programs along a selected section of the I-78 Corridor using traffic simulation
  Phase 3 – Route Diversion
    Testing of the impacts of various strategies on the arterial road systems along I-78

## Slide 3: Innovation
New Data Collection versus Established methods
Planning/Modeling Data needs
Limited staffing needs with large data sets
Current manual methods can result in human error.

## Slide 4: Data Collection Plan
Data Collection Methods
  Bluetooth
  INRIX
  GPS/Laptop Probe Car
  Skycomp
  Manual Lane Counts
  ATR Ramp Counts
  Historic Count

## Slide 5: Data Collection Plan
Data uses
  Bluetooth and INRIX new technologies test bed.
  Probe Car safety net for new technologies
  Skycomp visual aid
  Distribution of travel times to support Stochastic Micro-Simulation

## Slide 6: Bluetooth
10 Bluetooth Units
Side of road installation
  Guiderail
  Light Post
Location #1 / Start

## Slide 7: Bluetooth
Travel times and speeds between any two readers
Origin/Destination Data (Not Tested)
Between Exit 18 and I-287
Between Int 24 and Int 26
Avg Trav. Time
Avg Speed
Hits

## Slide 8: INRIX Real Time Highway Speed Data
Source: INRIX Corporation

## Slide 9: INRIX Real Time Highway Speed Data
Large scale collection of travel speeds
  Probe vehicles (using GPS) through fleet arrangements
  I-95 Corridor Coalition has acquired rights to the data
Typical applications in Real Time
  NJ 511 System
  I-78 Travel Time via Express/Local
  Commercial Providers
Useful By-Product: Archived Travel Speeds
  By State Highway Segment
  Daily files (All segments, 5 minute periods, 2008 to current)

## Slide 10: INRIX Real Time Highway Speed Data

## Slide 11: GPS/Laptop Probe Vehicle
PCtravel
GPS linked laptop in probe vehicles

## Slide 12: Skycomp Aerial Photography
Aerial photo log of the corridor during the peak period

## Slide 13: Traffic Counts
Manual mainline classification counts
ATR ramp counts
Historical state counts

## Slide 14: Data Collection Study Results
Summary
  High Truck Percentage (11-13% AM peak period)
  Bluetooth and INRIX produced usable and comparable data
  Standard Methods (Skycomp and GPS Laptop) confirmed Bluetooth and INRIX quality
  Volumes slightly lower than historical data indicates
  Definite congestion problem along this corridor in the AM peak period
  Problem does not occur during any other period

## Slide 15: Data Collection Results
Alternate Methods Provide for Daily Comparisons
  June 8th and 10th were similar however June 9th had less congestion
  Based on these observations model will be used to show impact of daily variation
Tuesday
Wednesday
Thursday
Avg Trav. Time
Avg Speed
Hits

## Slide 16: Benefits
  Bluetooth
    High Granularity, most vehicles today have at least one Bluetooth signal, providing large complete data set;
    Unique ids throughout the study enabling use for Origin Destination type studies;
    Ease of installation, with ability to create a closed network;
    Low cost;
    Can put it anywhere – not just for vehicles;
  INRIX
    Large Historical Dataset;
    Large coverage area of interstate roads;
    Large user group;
  GPS Based Probe
    Cheap;
    Can be combined with driver/passenger observations;

## Slide 17: Limitations
  Bluetooth
    Point by Point travel time calculation, can produce gaps;
    Data set limited to battery life (about a week)
  INRIX
    Only available on predetermined Interstates and state roads;
    Can be costly;
  GPS Based Probe
    Limited data set;
    For long corridors during peaks multiple probes needed even then can miss critical times.

## Slide 18: Traffic Simulation

## Slide 19: Network Calibration/Validation
Travel Time graphs
  Observed Corridor Travel Time compared to Modeled Travel Time (5 random seeds and average)

## Slide 20: Ramp Metering Alternatives
Pre-Timed Ramp Metering (PRM)
  4 Pre-Timed 2 lane ramps
  1 vehicle per lane per 9 secs
Actuated Ramp Metering (ARM)
  4 Actuated 2 lane ramps
  Mainline Gap controlled
Actuated Ramp Metering + Advanced Lane Management (ALM)
  Actuated Scenario + Mainline Variable Speed Limits tied to volume

## Slide 21: Ramp Metering Alternatives (2010)
Travel Time Comparisons
  PRM - up to 5 minutes of mainline travel time saving
  ARM - up to 10 minutes of mainline travel time savings
  ALM – increased travel times

## Slide 22: Findings
The Bluetooth technology was successful in accurately and inexpensively collecting travel time data. Given the ease of use of this technology, it should be considered for larger studies and even for use in Origin–Destination studies. Also, INRIX real-time data was shown to have promise, with the advantage that it is readily available for all freeways in New Jersey and for a lengthy, multiple-year historical data available.
These data sources greatly aid in the calibration and validation of planning and analysis models.
Microsimulation was able to accurately represent the existing conditions and also to show the potential benefits from implementation of some form of ramp metering along the corridor.

## Slide 23: Questions
Matthew Juckes
Senior Project Manager
Transport Simulation Systems, Inc,
20 West 22nd Street, Suite 612
New York, NY, 10010
matthew.juckes@aimsun.com
Bernard Alpern
Associate Vice President/Transportation Planning
AECOM
605 Third Avenue
New York , NY, 10005
Bernard.aplern@aecom.com