## Slide 1: Innovative Approach to Transit On-board Data Collection
Findings from Twin Cities
TRB Applications Conference
May 6, 2013
Anurag Komanduri & Kimon Proussaloglou (CS) Jonathan Ehrlich & Mark Filipi (MetCouncil) Evalynn Williams (Dikita)

## Slide 2: Metropolitan Council Travel Behavior Inventory
Snapshot of personal travel in Minneapolis-St. Paul
  2010 - ongoing
  Multi-year – multi-mode – multi-everything
Collect and provide quality data
  Support regional initiatives + research
  Perform stand-alone data analytics
Build a fine-grained policy-sensitive model using data
  State of the practice activity-based model
“Create a lasting legacy for the region”

## Slide 3: Metropolitan Council Travel Behavior Inventory Data Collection
Demand Data
Household Travel & Activity
Transit On-board
Supply Data
Highway Counts & Speeds
Transit Operations Data
Supplementary Data
Parking Lot Utilization
Bicycle Data
External & Special Generator

## Slide 4: Metropolitan Council Transit On-board Survey Objectives
Build transit rider profile for modeling
  Transit model validation
  Stand-alone for analytics
Multi-lingual survey instrument design
  English, Spanish, Hmong and Somali
Data collection methodology
  On and off counts
Multi-dimensional weighting
  Disaggregate “route-direction-time-of-day-geography”
Complement 2005 survey effort

## Slide 5: Metropolitan Council Transit On-board Survey Trade-Off Assessment
Utilize budget effectively to meet objectives
  “Do more with less”
Developed options early on in the process
  Collaborative – Met Council, CS, Dikita
Key questions targeted
  Can we complement the 2010 data using 2005 survey data?
  Can we “sample” smarter?
  Can we “assign” crews effectively?
  How do we improve survey QA/QC?
  Ensure “survey data” are representative of rider patterns
Address every area to maximize data quality and value

## Slide 6: Transit On-board Survey Step 1. Maximize Use of 2005 Data
2005 on-board survey – very comprehensive
  Covered all routes and time periods
If data merging must happen…data fields must be same
  2005 survey well thought out
2010 questionnaire built off 2005 questionnaire
  Only income levels changed
Questions adjusted to account for…
  New commuter rail in Minneapolis
  Refined questions to support modeling – “walk access dis.”
  Improve capture of “transferring”

## Slide 7: Transit On-board Survey Step 2. Sample Smarter
Do we survey all routes?
  Even if no change in operations or ridership from 2005
  No change likely in “rider” profile or patterns
Create priority groups – 110 routes
  Northstar (commuter rail) + supporting buses
  High volume corridors – potential AA
  BRT corridors
  Change in volume corridor
  4 priority groups – 80 percent of ridership
Remaining 100 routes – 20 percent of riderhip
  Dropped from 2010 survey – use 2005 data

## Slide 8: Transit On-board Survey Step 3. Allocate Crews Efficiently
Collect usable surveys from at least 5 percent of riders
  Ridership on priority groups = 225,000
  Survey goal = 11,300
Sampling carried out at block-level (vehicle-level)
  Minimizes “wait” times
  Takes advantage of interlining
Prioritized block selection
  Blocks with majority of routes in top 4 priorities
  High ridership blocks
  At least 3 hours
  Minimal layover times between revenue runs

## Slide 9: Transit On-board Survey Step 4. Redesign Survey QA/QC
Focused targeting of routes improved efficiency
Allowed reallocation of resources to QA/QC
Four levels of auditing
  Dikita – in-field to drop “obviously” poor records
  Dikita – in-office to improve data quality
  CS – external auditor – especially of location questions
  Met Council – “local expert”
Three rounds of geocoding – different software
  ArcGIS, TransCAD, Google API
  Tremendous improvement in data quality

## Slide 10: Transit On-board Survey Step 5. Focus on Weighting
Survey data must reflect ridership patterns
  Control for “crowding” effect
  Control for “short trip” effect
Develop disaggregate weighting methodology
  Route, direction, time-of-day, geography
Collected boarding-alighting counts
  Supplement on-board surveys
  Provide raw data for expansion
Multi-dimensional IPF implemented

## Slide 11: Transit On-board Survey Survey Results
Hugely successful survey effort
  21,100 surveys collected (90% over target)
  16,600 surveys usable (50% over target)
  High quality of geocoding
Well distributed by route-direction-ToD
  Impact of “well thought out” sampling plan
Completion rates as percentage of total ridership
  30 percent on commuter rail – long rides
  20 percent on express bus
  10 percent on light rail
  5 percent on local bus – close to target

## Slide 12: Transit On-board Survey Survey Results
Combined with 2005 data for low-priority routes
  Over 5,500 records from 2005 (100 routes)
  22,400 usable records
Detailed expansion implemented
  Step 1 – control for non-participants (route-direction-ToD)
  Step 2 – control for non-surveyed routes
  Step 3 – control for “boardings-alightings” (geography)
  Step 4 – control for transfers (linked trip factors)
Three weighted datasets prepared
  Retain all records – “socio-demographic” profile of riders
  Records with “O-D” – critical to support modeling
  Records with O-D and trip purpose – even more detailed

## Slide 13: Transit On-board Survey Survey Results
Time of Day | Boarding Superdistrict | Count Distribution | Pre-Geo. Expansion Distribution | Post-Geo. Expansion Distribution
AM Peak Period (6–9 AM) | 101 | 10.79% | 12.24% | 12.36%
 | 102 | 13.15% | 17.67% | 12.97%
 | 103 | 0.68% | 0.22% | 0.51%
 | 104 | 18.10% | 21.36% | 17.87%
 | 201 | 4.08% | 6.17% | 3.92%
 | 202 | 0.77% | 0.83% | 0.79%
 | 301 | 17.96% | 18.37% | 18.18%
 | 401 | 34.01% | 22.44% | 32.86%
 | 701 | 0.41% | 0.70% | 0.40%

## Slide 14: Transit On-board Survey Lessons Learned
Selective surveying is beneficial
  MPO knowledge critical – identify routes to survey
  Data-driven (ridership) approach possible
  Budget allocation benefits
Periodic counts can provide data about rider patterns
  Determine whether routes need to be surveyed
  Changes in ridership by route, time-of-day, direction
Careful allocation of resources – huge impact
  Cleaning + weighting as important as collecting
On-board survey data – rich stand-alone dataset
  Counts help measure crowding + volume build up