## Slide 1: GIS-based Road Network Information in Travel Demand Modeling
Ahmed Mohideen
Abishek Komma
Vipul Modi

## Slide 2: Agenda
Data Sources and Vendors  Motivation?
  Navteq
  TomTom
  OpenStreetMaps
  Google Transit Feed
Conversion tools (raw data to modeling networks)
  Build Network from Shape file (BNFS)
  Custom applications for additional control and flexibility
Successful Applications @
  Macro-scopic
  Meso-scopic
  Micro-scopic

## Slide 3: Motivation
Increasing trend towards GIS-based networks
  True shape networks
  Time and cost savings for MPOs  collect, compile & update
  Scalable information
  Reliable source of consistent and accurate information?
  Avoid collection from multiple sources?
Sample information available:
  Basic network characteristics
  Speed profiles
  Heavy vehicle restrictions
  Turn prohibitions
  HOV\HOT lane availability by time-of-day

## Slide 4: Data Sources: NAVTEQ (1/2)
Chicago based provider of GIS data and navigable maps
Why is this important?
Key features/attributes
  Geometry Information
    Link Attributes – access (type of vehicles) and display (for routing) characteristics
    Node Attributes – Z level (relative elevation)
  Navigation Information
    Roadway Functional Classes (FC1, FC2, FC3, FC4, FC5)
    One-way/direction of travel
    Speed Information – speed limits, special speed limits
    Lane Information – number of lanes
    Time of Day, Turn restrictions
Accessibility: Shapefile (.shp), ASCII file formats, etc.

## Slide 5: Data Sources: TomTom (2/2)
Netherlands based provider for navigation and location-based services
Why is this important?
Key features/attributes
  Network Information
    Functional Road Class (FRC)
    Route Directional – including Oneway information
    Relative elevation (F_Level and T_Level)
    Ramp
    Speed – Speed Category, dynamic speed
  Junction data
    Junction type
    Elevation
Accessibility: Shapefiles (.shp)

## Slide 6: Conversion Tools: BNFS (1/3)
Requirements:
  Polyline shape file of links
  Node# information: A, B
  Directionality
  Pre-processing: Filtering
Output:
  Create network links based on feature topology and attributes
  Retain spatial information
  Binary network or
  Feature-class in a geodatabase
Cleanup tools:
  Generate true shape equivalencies
  Copy shape from another layer
  Batch mode: BNFS from script

## Slide 7: Conversion Tools: Custom Navteq App (2/3)
NAVTEQ street centerline data  Modeling Network
Z-level data  Handle over-passes, under-passes
Options to scale the level of data  Include/Exclude link-classes
Add network attributes (speed, #lanes, distance)
Creates turn penalty data from NAVTEQ restrictions
Consolidate data for optimization

## Slide 8: Case Study 1
Mountain View, CA
Realistic travel patterns in Mountain View
  Meso-scopic simulation in Cube Avenue
  Further, Caltrans count data  Dynamic OD Estimation in Cube Analyst Drive
Network based on Navteq center line  Modeling Network
  78 Zones
  9000 Links
  4000 Nodes
Used the custom Navteq application to create the modeling network

## Slide 9: Example: Mountain View, CA: Model Network

## Slide 10: Closer View

## Slide 11: Conversion Tools: Custom TomTom App (3/3)
Highway network
  - Speed Profile
  - Heavy vehicle bans
Turn Prohibitions
Roadway Functional classes
  Motorway, freeway or other major Road
  Major road less important than a motorway
  Other major road
  Secondary road
  Local connecting road
  Local road of high importance
  Local road
Link Consolidation

## Slide 12: Custom TomTom App – Input Files
Network links (_nw)
Junction (_jc)
Maneuvers (_mn)
Maneuvers Path Index (_mp)
Speed Profile (_hsnp)
Logistics restrictions (_lrs)
Logistics Maneuvers (_lmn)
Maneuvers Path Index (_lmp)
T_JNCTID
F_JNCTID
ID
ID
ID
JNCTID
ID
ID
ID
JNCTID
ID
ID
ID
NETWORK_ID
ID
ID

## Slide 13: Custom TomTom App - Steps
4. Create turn prohibitions
2. Update link data with speed profile date and heavy vehicle bans
3. Build network
1. Set-up network node numbers
5. Consolidate Network

## Slide 14: Case Study 2
Milan, Italy
Functional class  0-6
Link Consolidation 19 network attributes
Before Consolidation
  288,330 Nodes
  556,323 Links
After Consolidation
  212,772 Nodes
  417,313 Links

## Slide 15: Case Study 2: Milan, Italy

## Slide 16: Case Study 2: Speed Profile Data

## Slide 17: Case Study 2: Observations
Data quality  Good network coverage, accuracy, topology and connectivity
Navigation data  complex turn movements and lane configurations
  Manual post processing of highway network
Functional Class  few and aggregated
  Further dis-aggregation using additional attributes such as speed categories, divided/undivided highways
Link Consolidation  highly segmented links.
  Limit consolidation to limited number of attributes such as functional class, number of lanes

## Slide 18: Future Efforts
Streamline the tools further
  Incorporate more data elements like Toll information
  Tools to integrate OpenSteetMap data
  Tools to integrate Google Transit data
  Tools to integrate open count data like Caltrans
Case study for Microscopic simulation

## Slide 19
Thank you!
Questions?