## Slide 1: Modeling Every Hill, Bus, Traffic Signal, and Car How San Francisco Collaboratively Built a Citywide Dynamic Traffic Assignment Model
Elizabeth Sall, Greg Erhardt, Lisa Zorn, Daniel Tischler, Renee Alsup, & Neema Nassir
TRB Planning Applications Conference
May 5th, 2013

## Slide 2: Why DTA? (recap)
Better representation of the real world
Queues spill back to adjacent links
Signals & intersection design matter
Transit and cars interact
Less messy spreadsheet work
Less subjectivity
Fewer typos/errors

## Slide 3: An additional tool in the toolbox - DTA
SF-CHAMP
Dynamic Traffic
Assignment
Traffic
Microsimulation
Time-dependent user equilibrium
with realistic, but simplified vehicle simulation
Regional static user equilibrium within an
activity-based model
Highly realistic simulation of vehicle behavior and interactions

## Slide 4: Why Collaboration?
Why not just ask for a “product”?
We have to own it in the end
Shared ownership / credit makes more people care and understand situation
Cool Project – Let lots of interested and smart people take part and learn!
“I don’t care, that’s what’s in the scope
“We just don’t have the budget to get to that calibration target
“This code is inscrutable!”
“How do I do Validation or actually run a scenario?”
We work with planners on real projects in SF every day.
“Shoot, Well what I really hoped DTA would be able to capture was…”
“These results don’t make any sense. I thought DTA was supposed to be useful!
See Lisa Zorn present “The Codebase IS the Deliverable” Monday 10:30

## Slide 5: DTA Model Development Objectives (for now)
Have a working DTA model with results that make sense for the PM Peak period in San Francisco
Have seamless process from SF-CHAMP to DTA results:
  Little human intervention
  Reduce human error
  Use SF-CHAMP demand directly
    Behaviorally consistent
Allow SF-CHAMP to take advantage of all fixes

## Slide 6: DTA Model Development Approach
Write code when possible for repeated human tasks
  Don’t re-write code that exists in our DTA package
  Develop in an open source environment
Use as much ‘real’ data as possible
Fix all issues “at the source” if possible

## Slide 7: Where we were starting from in SF-CHAMP
Every transit stop
Every transit line
Every street
Every Hill
981 Zones in SF

## Slide 8: DTA Anyway CodeBase & INPUT Development
Input
Codebase
Calibration

## Slide 9: DTA Anyway for Automation
DTA Anyway Python Module
Static Network
Python Scripts
DTA Network
Static Network
+ Projects
DTA Network + Projects
Notes: DTA anyway is there to convert what already exists and add new stuff. We want to automate this, so we can repeat it each time we do a new SF-CHAMP run.

## Slide 10: DTA Anyway Capabilities
DTA Anyway Can
Read Cube Networks / text-based static networks
Read/Write Dynameq ASCII files
Write GIS shapefiles
typical network edits
DTA Anyway Cannot
Visualize anything directly
Read/Write DTA networks for other DTA software (but designed to make this easily implementable)

## Slide 11: DTA Inputs
New!
New!
New!
Improved!
http://dta.googlecode.com
Notes: What are the basic inputs needed for a DTA model? (networks, transit routes, signals, stop signs, demand, counts)

## Slide 12: Input Development (alongside codebase development)
Signals
1,100 signals
Actuated signals approximated to fixed
Source: SFMTA-defined Excel files
Transit
236 Lines
Source: SF-CHAMP Cube Files
Stops
1,845 AWSC
919 TWSC
Source: SFMTA GIS
Demand
CHAMP Demand
620k vehicles 2:30-7:30 PM
976 zones + 22 Exts
Time profile f(counts)

## Slide 13: Calibration AND VALIDATION

## Slide 14: Model Calibration Approach
  “Model Calibration involves the identification of a set of DTA model inputs and parameters that results in model outputs that are reasonably close to those field observations.”
  - DTA Primer
Inputs for a Specific Scenario
Model Parameters
Measured Reality for that Scenario
Hopefully extrapolates to another scenario!
+

## Slide 15: Model Calibration Approach
Source: DTA Primer
VS
Downstream
Upstream

## Slide 16: Model Calibration Approach
  Ensure quality inputs
  Measure anything that can be measured
  Evaluate the results qualitatively
  Evaluate the results quantitatively
  Make defensible adjustments
  What factors that affect driver behavior are missing from the model?
For detailed “Adventures in Calibration”:
Dta.googlecode.com Webinar Presentation Slides 25-29
Notes: Where is the documentation?
Most of papers are focused on changing demand.
Easy to do one-off calibrations…hard to do sustained.

## Slide 17: Traffic Flow Parameter Estimation
Param. FT | Free-flow Speed | Saturation Flow | Response Time | Jam Density
 | PeMS | PeMS | PeMS | Inferred from CBD arterials
Arterials | SFMTA speed surveys | CBD saturation headway observations | CBD queue dissipation observations | CBD arterial queue length observations
Locals & Collectors | Limited SFMTA speed surveys & supplemental observations | Mostly inferred from CBD arterials | Mostly inferred from CBD arterials | Mostly infer red from CBD arterials
Red text = data limitations
  Data sources for parameter estimation

## Slide 18: Final Calibration Parameters
Additional reading material!
  Final generalized cost expression
    Travel Time, Tolls, Turn Penalties
    Distance tried, didn’t work well
  Response times
    Function of uphill and downhill slopes
  Signalized turning movement capacity:
    Function of asserted pedestrian densities
  Read all about the details:
    http://www.sfcta.org/dta

## Slide 19: Validation Data - Counts
97 | 15-minute link counts
22 | 60-minute link counts
864 | 15-minute movement counts
160 | 5-minute movement counts
Count Dracula is SFCTA’s traffic counts database
Recent (2009-2011) midweek (Tue/Wed/Thu) counts queried from Count Dracula API for DTA Validation
For more CountDracula
Lisa Zorn presents:
“Sharing Is Caring”
Wednesday, 1:30 PM
https://github.com/sfcta/CountDracula

## Slide 20: Validation Data – Travel Times
Spring 2011 Level of Service Monitoring
272 Summary Segments

## Slide 21: Validation Results Convergence & Performance
Convergence Plot for Final Model
  DTA shows stable convergence for ~20 iterations
  Mean Relative Gap: 2.7%
  109 50ish hours computing
  Max waiting vehicles ~ 350 (1%)
  Demand clears in reasonable time
  No observed gridlock

## Slide 22: Validation Results Link Volumes
  Total volume ~13% low.
  55% total RMSE. 40% RMSE for links >500 vph.
  75% of arterials within Caltrans maximum desirable deviation guidelines
What are some good standards? We couldn’t find any and neither could our peer review panel.

## Slide 23: Validation Results Segment Travel Times
Chart: Observed vs. Simulated Travel Times
  Travel times are reasonable on average
  A few outliers drive differences

## Slide 24: Validation Results Citywide Flow Patterns
Map of Total PM Peak Flow from DTA
Map of Total PM Peak Flow from Static Assignment
  Overall flow pattern logical, and similar to static model

## Slide 25: Sensitivity & Scenario Testing
Random Number Seeds
Small Network Change
Future Demand
Congestion Pricing
Bus Rapid Transit

## Slide 26: Congestion Pricing Application Test
SAN FRANCISCO COUNTY TRANSPORTATION AUTHORITY
26
Added a $3 fee to anyone crossing the cordon to manage congestion in downtown San Francisco

## Slide 27: Congestion Pricing Application Test – Static vs. DTA Flow Maps
DTA Model shows a much clearer diversion to paths outside the cordon
Static model shows some odd shifts that in the Northern region including increases in EB traffic going toward the CBD
Map of Flow Change from Static Pricing Test (Red links – flow loss of at least 250 vehicles, Blue links – flow gain of at least 250 vehicles)
Map of Flow Change from DTA Pricing Test (Red links – flow loss of at least 250 vehicles, Blue links – flow gain of at least 250 vehicles)
Static
DTA
Notes: The DTA model showed a much more clear and expected pattern of flow shifting away from the CBD. The demand change resulted in 8% fewer auto trips and 24% fewer truck trips, so there was almost no congestion in the DTA network due to much lower demand levels. Note the lack of the giant-blue exit ramp form US-101 to Cesar Chavez. Also, generally smoother loadings and diversions.

## Slide 28: Congestion Pricing Application Test – Static vs. DTA Speed Maps
DTA Model shows more widespread impacts on speed with faster speeds in most of the CBD.
Using the static model results could greatly underestimate the potential travel time impacts in the CBD.
Map of Speed Change from Static Pricing Test (Red links – speed loss of at least 5 mph, Blue links – speed increase of at least 5 mph)
Map of Speed Change from DTA Pricing Test (Red links – speed loss of at least 5 mph, Blue links – speed increase of at least 5 mph)
Static
DTA
Notes: Given the large changes in flow levels between the two models, the fact that there is little to no speed change in most of the Static network is problematic. If the static results were used as feedback, the impacts on travel times would likely be greatly underestimated. The fact that the static model predicts less travel time savings may also lead to the demand model predicting fewer people to pay the toll. If the DTA model were used for feedback to the demand model, it may indicate higher demand levels and more people willing to pay the toll to balance out the travel time savings they would get.

## Slide 29: Credit where it is due…
SFCTA
Elizabeth Sall – Conductor
Lisa Zorn – Code Cowgirl
Daniel Tischler – Calibration Hero
Neema Nassir – Traffic Model Data
Collection Dynamo
John Urgo – Willing data collector
Annie Chung & Matthew Chan – Courageous count coders
Parsons Brinckerhoff
Gregory Erhardt – Consultant PM
Renee Alsup – Calibration Hero
[Michalis Xynatarakis] – the one who had done this before
Jim Hicks & Joel Freedman – Parental Supervision
Peer Review Team
Joe Castiglione
Bruce Griesenbeck
Vassilis Papayannoulis
David Stanek
Xuesong Zhou
Keeping Us Sane
Michael Mahut – INRO
Brian Gardner -- FHWA
www.sfcta.org/dta dta.googlecode.com

## Slide 30: Credit where it’s due….
www.sfcta.org/dta dta.googlecode.com
Greg Erhardt (PB) – Consultant PM
Lisa Zorn (SFCTA) –Codebase Lead + CountDracula
Daniel Tischler (SFCTA) – Traffic Flow Calibration Lead
Renee Alsup (PB) – Calibration + Sensitivity Testing
Neema Nassir (SFCTA/U of Arizona) – Traffic Flow Model
Michalis Xyntarakis – Early codebase development

## Slide 31: Traffic Flow Parameter Measurement

## Slide 32: Future Work & ONGOING Research

## Slide 33: Future Work: Deployment
Examine stochasticity
  Useful tool for finding ranges
Work with local consultants and agencies
Use with real projects!

## Slide 34: Future Work: Development
Improve pedestrian/bike
interaction representation
Represent actual parking locations
Improve demand in SF-CHAMP

## Slide 35: Research: Person-based Transit Assignment FAST-TrIPs
See: Khani, Zorn and Sall, 2013 TRB Annual Meeting
Update transit vehicles’ dwell time f(FAST-TrIPs boarding and alightings)
Simulate individual riders, individual buses based on DTA trajectories (or GTFS)
FAST-TrIPs
DTA
Why?
  Bus Bunching
  Transit reliability
  Capacities
  Actual schedules

## Slide 36: Research: Person-based Transit Assignment FAST-TrIPs
Route 38 - Geary Blvd, Vehicle Trip Starting at 5:47PM
See: Khani, Zorn and Sall, 2013 TRB Annual Meeting

## Slide 37: Research: Transit Reliability / FAST-TrIPs Development
More FAST-TrIPs/DTA Integration
  Convergence methodologies
FAST-TrIPs/CHAMP Integration
  Use static assignment
  Skimming
  Sensitivity tests
Develop Reliability Metrics in FAST-TrIPs
  As function of demand profiles
  As function of network and service characteristics

## Slide 38: Convert Static Network  Dynamic
Define Scenario: vehicle types and classes, generalized cost
Import Cube network data, defining DTA attributes in terms of Cube attributes
Add all movements, prohibiting most U-Turns, explicitly naming some where geometry is confusing
Read GIS shapefile for road curvature
Add virtual nodes/links between centroids and road nodes
Move centroid connectors from intersections to midblock nodes
Handle overlapping and short links
15,000 | Nodes
37,000 | Links
109,000 | Movements

## Slide 39: Import Transit Routes
Reads Cube-formatted transit line files and converts into DTA transit lines
Use shortest-path to connect links that may have been split
Where LRT lines go off the DTA network (underground or on separated ROW), they are split into segments (discarding those not on the DTA network)
Movements are explicitly allowed for transit if previously prohibited
236 | Transit Lines

## Slide 40: Import Signals
Reads signal card data from Excel files in a SFMTA-defined format
We search for the section specifying the weekday PM peak plan
For errors and unique circumstances encountered (and there were many), responses could be:
  Update signal card itself
  Update signal-card reading code
  Update static network
We approximate the few actuated signals with their fixed time version
Signal-reading code is not very re-usable
1,100 | Signal Time Plans

## Slide 41: Import Stop Signs
Stop signs are coded as (GIS point, street name, cross street name, and direction the stop sign is facing)
Signal data takes precedence
Mark as all-way stops when # of stop signs for a node matches the # of incoming links
Otherwise, mark as two-way
Custom priorities for two-way stops where facility types tie
1,845 | All-way stop nodes
919 | Two-way stop nodes
1,020 | Custom priority stop nodes

## Slide 42: Import Demand
Auto and truck tables are imported from SF-CHAMP MD, PM, EV demand tables
535.2k auto trips, 84.2k truck trips loaded 2:30-7:30p
The DTA network uses same TAZ structure is used as SF-CHAMP because the zones are small (976 within SF, plus 22 external stations)
The PM (3:30p-6:30p) demand is peaked slightly towards 5-6p based on traffic counts
Notes: Better graphic? Maybe the crazy Dynameq demand graphic with all the little bar charts?

## Slide 43: Future Work - Development