## Slide 1: A Data Driven Approach to Transit Forecasting for New Starts and Small Starts
Smith Myung, Cambridge Systematics
Sean McAtee, Cambridge Systematics

## Slide 2: Overview
Background
Description of Procedures
Base Year Validation
Conclusions
Questions

## Slide 3: Why Data Driven?
What is a Data Driven approach? Simplified forecasting approach based on existing conditions
VIA Urban Corridor Alternative Analysis as case study
Data availability: 2010 VIA On-board survey data
Existing transit service; relatively mature area
Focus efforts on transit components
SA-BC MPO model updates not ready

## Slide 4: New Start and Small Starts
FTA has supported data driven approaches -
  Transparent
  Reliable
  Good for short-term (< 10 yrs)
Federal regulations are changing
Client undecided about New Starts/Small Starts
Maintain all options – use good modeling practice!

## Slide 5: Background
Location:
San Antonio CBD bounded by I-35,
I-10, and I-37
Existing Service:
Rubber-tired streetcar routes (3)
Serve major attractions
Travel time: 9 to 15 min.
10/15 minute headway
2010 avg. wkdy ridership of 2,300
Context:
San Antonio Urban Corridor AA

## Slide 6: Existing Streetcar Routes

## Slide 7: Major Attractions
  Alamodome – seats 65,000
  Henry B. Gonzalez Convention Center
  Pearl Brewery Urban Neighborhood
  H-E-B Corporate Headquarters
  CPS Energy Corporate Headquarters
  City of San Antonio administrative offices
  Bexar County administrative offices and Courthouse
  University of Texas at San Antonio Downtown Campus – 6,400 students
  San Antonio Riverwalk
  River Center Mall
  Market Square

## Slide 8: Description of Procedures

## Slide 9: On-board Survey Processing
Collected via personal interviews with handheld computers (high quality data)
Survey processing (16,832 records)
  Clean records, reweight, confirm control totals by route and TOD
Trip Purpose | Boardings | No. of Responses
HBW | 46,840 | 5,940
HNW | 64,430 | 8,958
NHB | 15,670 | 2,271
Grand Total | ~127,000 | 16,719

## Slide 10: Transit Path Checking
Compare transit paths from survey to model skims
  Is multi-path necessary?
  Use Prediction Success table to compare reported transfers to skim tables

## Slide 11: Transit Path Checking
Multi-path test (observed OD pairs)
  Analysis of survey responses
  Many route options into San Antonio CBD
 | Walk - Bus
Interchange with at least 3 or more observations | 786
Interchange with more than 1 path | 500
Percent of zone pairs with more than 1 path | 66.7%

## Slide 12: Transit Path Checking
Route 1, 10 minutes 30-minute headway
Route 2, 12 minutes 30-minute headway
A
B
Single Path: 10 minute IVTT, 30-minute headway

## Slide 13: Transit Path Checking
Route 1, 10 minutes 30-minute headway
Route 2, 12 minutes 30-minute headway
A
B
Multi-Path: 11 minute IVTT, 15-minute headway

## Slide 14: Transit Path Checking
Example: Prediction Success Spot-Check
  Survey: 1 transfer; TransCAD: no transfers
Walk
Bus

## Slide 15: Transit Path Checking
Example: Prediction Success Spot-Check
  Survey: No transfers; TransCAD: 1 transfer
Walk
Bus 1
Bus 2
Geocoded Location

## Slide 16: Transit Path Checking
Multi-path checking can be challenging
  Geocoded locations, coarseness of zones and networks
Verify networks are accurate
Multi-pathbuilder may select paths that are non-intuitive
Worked around limitation by programming logic in script

## Slide 17: Incremental Structure
Choice
Auto
Transit

## Slide 18: Incremental Structure
Binary structure is adequate
  No sub-mode competition (bus vs. rail)
  Model by market
    Trip purpose
    HH income for home-based trips
  Model coefficients (from SA-BC MPO model)
      Out-of-vehicle travel time: -0.0625
      In-vehicle travel time: -0.0250

## Slide 19: Incremental Structure
Base transit mode shares
  Expanded on-board survey
  Motorized person trips from
  SA-BC MPO model
District structure used
  Survey will be sparse at TAZ
  Grouped “like” TAZs into
  8 districts
  Minimized 0% and >100%
  shares – checked shares for
  reasonability

## Slide 20: Base Year Validation

## Slide 21: Bus Run Times

## Slide 22: Assignment Results
Systemwide Boardings (expanded trip table)
Model matches observed 1.41 average boardings per trip
 | Observed | Modeled | % Error
Metro & Frequent | 113,303 | 113,013 | -0.3%
Express & Skip | 11,348 | 12,394 | +9.2%
Rubber-Tire Streetcar | 2,248 | 2,213 | -1.6%
Systemwide | 126,898 | 127,620 | +0.6%
Study Area Total | 27,738 | 28,174 | +1.6%

## Slide 23: Assignment Results
Existing Rubber Tire Streetcar Boardings (expanded trip table)
Results are impressive – akin to validating collectors in a regional model
 | Observed | Modeled | % Error
Red Route | 779 | 693 | -11%
Yellow Route | 967 | 931 | -4%
Blue Route | 502 | 589 | 17%
Total | 2,248 | 2,213 | -2%

## Slide 24: Assignment Results
Systemwide Boardings by Route

## Slide 25: Assignment Results
Activity by Stop

## Slide 26: Assignment – Suggestions
Validation specified with initial boarding penalty of 10 minutes
Allows for flexibility in accommodating fixed-guideway benefits (i.e. span of service, station amenities, etc.)

## Slide 27: Conclusions

## Slide 28: Conclusions
Good on-board survey data are critical!!!!
Multi-path validation is important & can be challenging
Survey data will be sparse at TAZ level; apply model at district level
Suitable for areas with existing transit service; relatively mature land uses
Relatively cost-effective; focus on validating transit components; schedule acceleration or at least, on time!

## Slide 29: Questions