## Slide 1: Model Calibration & Estimation Input Data Validation Checks…
14th TRB Planning Applications Conference
So, How Do You Know Those Travel Times Are Reasonable, Anyway?
May 7, 2013
David Kurth

## Slide 2: Co-authors & Contributors
Cambridge Systematics
  Marty Milkovits
  Dan Tempesta
  Jason Lemp
  Anurag Komanduri
  Ramesh Thammiraju
AECOM
  Pat Coleman

## Slide 3: Presentation Overview
Quick review of Travel Model Validation and Reasonableness Checking Manual – Second Edition
  Aggregate & disaggregate validation checks of input model skims
Updates / New Techniques for Disaggregate Checks
  Transit prediction success with transit multipath builders
    SEMCOG
  Transit route profiles
    Minneapolis-St. Paul & Denver
  Highway travel skims
    Houston & Denver

## Slide 4: Validation of Input Data
Important for Trip-Based and Activity/Tour-Based Models
  In a word – GIGO
Appropriate Approaches
  Aggregate Models → Aggregate Checks
    Larger outliers that impact model calibration
  Disaggregate Models → Aggregate & Disaggregate Checks
    Larger outliers that skew models
    Individual outliers that impact coefficient estimates & statistics

## Slide 5: Travel Model Validation and Reasonableness Checking Manual – Second Edition
Highway Network Path Building Aggregate Checks
  Speed interchange frequency distributions

## Slide 6: Travel Model Validation and Reasonableness Checking Manual – Second Edition
Highway Network Path Building Aggregate Checks
  Speed interchange frequency distributions
  Travel time plots

## Slide 7: Travel Model Validation and Reasonableness Checking Manual – Second Edition
Highway Network Path Building Disaggregate Checks
  “no applicable disaggregate checks of highway network skim data…”

## Slide 8: Travel Model Validation and Reasonableness Checking Manual – Second Edition
Highway Network Path Building Disaggregate Checks
  “no applicable disaggregate checks of highway network skim data…”
  …will be addressed in this presentation.

## Slide 9: Travel Model Validation and Reasonableness Checking Manual – Second Edition
Transit Network Path Building Aggregate Checks
  Trip length frequency distributions
    In-vehicle time
    Out-of-vehicle time
    Number of transfers
    Costs

## Slide 10: Travel Model Validation and Reasonableness Checking Manual – Second Edition
Transit Network Path Building Aggregate Checks
  Trip length frequency distributions
    In-vehicle time
    Out-of-vehicle time
    Number of transfers
    Costs
  Comparison to auto travel times

## Slide 11: Travel Model Validation and Reasonableness Checking Manual – Second Edition
Transit Network Path Building Aggregate Checks
  Trip length frequency distributions
    In-vehicle time
    Out-of-vehicle time
    Number of transfers
    Costs
  Comparison to auto travel times
  Assign observed transit trips and compare modeled to observed boardings by route
Line | Observed Boardings | Assigned Boardings | Difference | Percent Difference
1 | 913 | 698 | -215 | -24%
2 | 645 | 723 | 78 | 12%
3 | 7,944 | 7,510 | -434 | -5%
4 | 1,414 | 1,587 | 173 | 12%
5 | 4,208 | 4,271 | 63 | 1%
6 | 1,172 | 1,001 | -171 | -15%
7 | 12,466 | 13,067 | 601 | 5%
… | … | … | … | …
Total | 149,562 | 144,285 | -5,277 | -4%

## Slide 12: Travel Model Validation and Reasonableness Checking Manual – Second Edition
Transit Network Path Building Disaggregate Checks
  Prediction-success tables comparing modeled to reported boardings
 |  | Modeled |  |  |  |  | Summary | 
 |  | 0 | 1 | 2 | 3 | 4 | Path Match | Percent
Reported | 1 | 0.2% | 24.9% | 9.0% | 0.7% | 0.0% | 0 Modeled Paths | 1.0%
 | 2 | 0.5% | 12.2% | 31.2% | 6.9% | 0.0% | Reported > Modeled | 22.6%
 | 3 | 0.4% | 2.8% | 7.6% | 3.5% | 0.2% | Reported < Modeled | 16.9%
 | 4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | Reported = Modeled | 59.5%

## Slide 13: Prediction-Success with Transit Multipath Builders – SEMCOG
Issue
  Transit path-builders construct multiple paths
    Average number of boardings per interchange reported
    Respondents report integer number of boardings
    So, when the model shows 1.53 average boardings for a respondent reporting 1 boarding…

## Slide 14: Prediction-Success with Transit Multipath Builders – SEMCOG
Issue
  Transit path-builders construct multiple paths
    Average number of boardings per interchange reported
    Respondents report integer number of boardings
    So, when the model shows 1.53 average boardings for a respondent reporting 1 boarding…
…is that success or failure?

## Slide 15: Prediction-Success with Transit Multipath Builders – SEMCOG
2010 On-board Survey Boardings by Access Mode
Observed Prevalence of Multiple Paths
Boardings | Walk Access | Drive Access
1 | 5,802 | 960
2 | 4,797 | 257
3 | 1,262 | 46
4 | 203 | 9
Total | 12,064 | 1,272
Boardings / Linked Trip | 1.4 | 1.2
 | Walk Access | Drive Access
Interchanges with 3 or more observations | 244 | 14
Interchanges with respondents reporting different numbers of boardings |  | 
Number | 79 | 0
Percent | 32% | 0%

## Slide 16: Prediction-Success with Transit Multipath Builders – SEMCOG
Prediction-Success Tables Must Allow for:
  Multiple paths
  Different numbers of transfers
Prediction-Success Implementation Procedure
  Build true/false tables
    Build paths multiple times with “Maximum Number of Transfers” set to 0, 1, 2, or 3

## Slide 17: Prediction-Success with Transit Multipath Builders – SEMCOG
Prediction-Success Implementation Procedure
  Initial paths
    Maximum Number of Transfers = 0
    If path exists, “one-boarding” matrix cell = “True”; else “False”
    Save average number of transfers for each matrix cell
  Second set of paths
    Maximum Number of Transfers = 1
    If path exists and average number of boardings > value for “one-boarding” matrix
      Mark “two-boarding” matrix cell = “True” and save average number of transfers
  Repeat above for Maximum Number of Transfers = 2, 3
  If no paths for Maximum Number of Transfers = 3
    “No transit” = True

## Slide 18: Prediction-Success with Transit Multipath Builders – SEMCOG
Prediction-Success Implementation Procedure (continued)
  For each on-board survey observation
    Set prediction-success to true if the reported number of transfers matched one of the true/false tables
SEMCOG Results
 |  | Modeled |  |  |  |  | Summary | 
 |  | 0 | 1 | 2 | 3 | 4 | Path Match | Percent
Reported | 1 | 0.8% | 41.2% | 5.9% | 0.2% | 0.0% | 0 Modeled Paths | 2.4%
 | 2 | 1.0% | 8.6% | 29.4% | 0.7% | 0.0% | Reported > Modeled | 17.3%
 | 3 | 0.5% | 3.2% | 3.9% | 2.8% | 0.0% | Reported < Modeled | 6.9%
 | 4 | 0.1% | 0.7% | 0.7% | 0.1% | 0.1% | Reported = Modeled | 73.4%

## Slide 19: Prediction-Success with Transit Multipath Builders – SEMCOG
Key Findings / Changes
Finding | Found During Aggregate Validation | Found During Disaggregate Validation
Illogical walk egress distances in survey data | No | Yes
Maximum walk egress distance | Not determined | 36 Minutes
Transfer penalty | 6 minutes | 3 minutes

## Slide 20: Transit Route Profiles – Minneapolis-St. Paul
Use the correct data to check model accuracy
Supply Side Inputs – Transit Networks
  Accurate service frequency and stop spacing impact model outputs
  Custom database built by MetCouncil – NCompass
    Most up-to-date transit network information
    Updated regularly
Demand Side Inputs – On-board Survey Data
  Proper geocoding
  Proper survey expansion

## Slide 21: On-board Survey Geocoding – Minneapolis-St. Paul
Geocoding of 4 locations – “O-B-A-D”
  O-D most critical for model validation tests
  16,500+ surveys = ~65,000 locations
Three rounds of geocoding
  ArcGIS, TransCAD, Google API
Test for “accuracy” – mostly commonsense rules!
  Walk to transit < 1 mile from bus route (access and egress)
  Boarding and alighting locations “close” to bus route
  Manual cleaning for records that “fail” criteria = better input data

## Slide 22: On-board Survey Geocoding – Example from OKI On-Board Survey

## Slide 23: On-board Survey Weighting – Minneapolis-St. Paul
Proper expansion impacts accuracy
Collected detailed boarding-alighting count data
  Supplements on-board survey data
  Same bus trips as on-board survey
Performed disaggregate weighting procedures
  Step 1 – control for non-participants (route-direction-ToD)
  Step 2 – control for non-surveyed trips (sampling)
  Step 3 – control for “boarding-alighting” patterns (geo) IMPORTANT!
  Step 4 – control for transfers (linked trip factors)

## Slide 24: On-board Survey Weighting – Minneapolis-St. Paul
Time of Day | Boarding Superdistrict | Count Distribution | Pre-Geographic Expansion Distribution | Post-Geographic Expansion Distribution
AM Peak Period (6–9 AM) | 101 | 10.8% | 12.2% | 12.4%
 | 102 | 13.2% | 17.7% | 13.0%
 | 103 | 0.7% | 0.2% | 0.5%
 | 104 | 18.1% | 21.4% | 17.9%
 | 201 | 4.1% | 6.2% | 3.9%
 | 202 | 0.8% | 0.8% | 0.8%
 | 301 | 18.0% | 18.4% | 18.2%
 | 401 | 34.0% | 22.4% | 32.9%
 | 701 | 0.4% | 0.7% | 0.4%

## Slide 25: Transit Route Profiles – Minneapolis-St. Paul & Denver
Validation procedure includes
  Prediction-success tables
  Matching route profiles by line
Other data considerations
  Availability of data from Automated Passenger Counters (APCs)
  Transit on-to-off surveys being recommended by FTA
Possibly most useful for corridor studies

## Slide 26: Transit Route Profiles – Minneapolis-St. Paul & Denver
Minneapolis-St. Paul On-Board Survey
Denver West Line Light Rail “Before Survey”
  Before survey for FTA New Starts project (opened April 26, 2013)
  Included collection of boarding TO alighting counts by stop group
Denver Colfax Corridor Alternatives Analysis
  Corridor study with “traditional” on-board survey expanded to boardings by time-of-day and direction by line (2008)
  Detailed APC data

## Slide 27: Transit Route Profiles – Minneapolis-St. Paul & Denver

## Slide 28: Highway Travel Times – Houston
Background
  Work performed for development of H-GAC Activity-Based Model
  Highway network validated using aggregate methods
    Comparison of modeled to observed speeds

## Slide 29: Highway Travel Times – Houston
Background
  Work performed for development of H-GAC Activity-Based Model
  Highway network validated using aggregate methods
    Comparison of modeled to observed speeds
    Travel time plots

## Slide 30: Highway Travel Times – Houston
Issues for Activity-Based Model Development
  Network speeds were reasonable
  Selected interchange travel times were reasonable
    But, what about the 1000s of “unchecked” interchanges?

## Slide 31: Highway Travel Times – Houston
Issues for Activity-Based Model Development
  Network speeds were reasonable
  Selected interchange travel times were reasonable
    But, what about the 1000s of “unchecked” interchanges?
Approach to investigate the 1000s of unchecked interchanges
  Compare modeled (skimmed) travel times to reported travel times

## Slide 32: Highway Travel Times – Houston
Analysis Procedure
  Post modeled TAZ  TAZ time on auto driver records from household survey
    added terminal times to modeled times
  Calculated travel time difference for each auto driver record
  Summarized and plotted travel time differences in histograms

## Slide 33: Highway Travel Times – Houston
Expectations
  Normal-like distribution
    Mean & median ≈ 0
    Little skew
  Variation due to:
    Clock face reporting
    Normal variation in observed traffic
      E.g. survey respondent delayed on travel day by congestion due to traffic accident
    It’s a model – we will be never “perfect”
Image s downloaded from http://www.dreamstime.com/royalty-free-stock-photo-histogram-normal-distribution-image13721055

## Slide 34: Highway Travel Times – Houston

## Slide 35: Highway Travel Times – Houston
Implications of results
  Skimmed travel times tend to overestimate reported times  modeled speeds too slow
  No huge outliers identified
Other findings
  Analysis of results useful in identifying outliers
    Observations with obvious reporting problems
    Removed from model estimation dataset
  Adjusted terminal times
Mean = -0.11 minutes
SD = 13.9 minutes
Median = -1.9 minutes
Reported time < skimmed = 60.7%
Reported time >= skimmed = 39.3%

## Slide 36: Highway Travel Times – Denver

## Slide 37: Highway Travel Times – Denver
Implications of results
  Skimmed travel times tend to underestimate reported times  modeled speeds too fast
  No huge outliers identified
Other findings
  Analysis of results useful in identifying outliers
    Observations with obvious reporting problems
    Removed from model estimation dataset
  Adjusted terminal times
Mean = 0.8 minutes
SD = 7.6 minutes
Median = -0.2 minutes
Reported time < skimmed = 50.2%
Reported time >= skimmed = 49.8%

## Slide 38: Summary
Demonstrated Several New Validation Checks
  Disaggregate or semi-disaggregate in nature
  Easy to apply
  Provide information regarding quality of observed data being used for activity-based model estimation
    Removal of outliers from estimation data sets