## Slide 1: Dynamic Traffic Assignment Approaches for Statewide Transportation Planning And Operations: Maryland Case
S. Erdogan1, K. Patnam2, X. Zhou3, F.D. Ducca4, S. Mahapatra5, Z. Deng6, J. Liu7
1, 4, 6 University of Maryland, National Center for Smart Growth Research and Education
2 AECOM, Arlington, VA
3, 7 Arizona State University, School of Sustainable Engineering and the Built Environment
15th TRB National Transportation Planning Applications Conference
May 19, 2015, Atlantic City, New Jersey

## Slide 2: Motivation- Why Statewide DTA
Time of day issues
Congestion, queue buildup and dissipation
Long distance trips which span multiple time periods
Refined input for sub-area / corridor analysis
Scenario analysis capability

## Slide 3: Two Methods
Analytical Approach – TRANSIMS
  VDF for link MOEs
Simulation-based Approach – DTALite
  VDF, Point/Spatial-Queue, or Newell’s Kinematic Wave Model for link MOEs

## Slide 4: Input Data
Given MSTM CUBE Model
Network:
  MTSM 2007 network
    ~167,000 links, ~68,000 nodes, 1739 zones
Demand:
  MSTM 2007 demand input by
    6 purposes, 5 incomes categories, 4 TOD
  2007 HTS survey for diurnal distributions
Generate Nationwide and Subarea Models

## Slide 5: ANALYTIC APPROACH:TRANSIMS

## Slide 6: MSTM TRANSIMS Models
Level 2
Statewide
  21,748 Nodes
  31,116 Links
  1,811 Zones
Level 1
Nationwide
68,243 Nodes
87,785 Links
1,739 Zones
TRANSIMS Version 6 Router Applications
6
Demand
Network
Speeds/Flows*
Paths*
* = Optional
Dynamic Traffic Routing
AON Routing /
En-route Diversion
Paths
Speeds/Flows+
Dynamic User Equilibrium
In-memory iterations
Convergence
Paths
Speeds/Flows
Paths+
Speeds/Flows+
+ = Converged

## Slide 8: Validation –Link Level
Freeway
Major Arterial
Minor Arterial
Local

## Slide 9: I-95 S between MD-24 and MD-543
Volume (vph)
I-95 S between MD-24 and MD-543
Capital Beltway–Inner Loop between MD-295 and MD-450
Volume (vph)

## Slide 10: Time-Dependent Performance Measures
Congested Segment
Change in Average Travel Time by Departure Time
Chart: Avg. OD Travel Time (min)
| 000_100 | 100_200 | 200_300 | 300_400 | 400_500 | 500_600 | 600_700 | 700_800 | 800_900 | 900_1000 | 1000_1100 | 1100_1200 | 1200_1300 | 1300_1400 | 1400_1500 | 1500_1600 | 1600_1700 | 1700_1800 | 1800_1900 | 1900_2000 | 2000_2100 | 2100_2200 | 2200_2300 | 2300_2400
Travel Time | 44.5981 | 44.5981 | 44.5981 | 44.5981 | 44.5981 | 44.5981 | 44.8815 | 47.6885 | 50.4798 | 47.6879 | 45.6513 | 45.5401 | 47.7097 | 50.3333 | 49.4411 | 49.6016 | 52.3278 | 56.0443 | 50.9839 | 45.4078 | 44.6242 | 44.5981 | 44.5981 | 44.5981
Chart: Average Speed by TOD
| 000_100 | 100_200 | 200_300 | 300_400 | 400_500 | 500_600 | 600_700 | 700_800 | 800_900 | 900_1000 | 1000_1100 | 1100_1200 | 1200_1300 | 1300_1400 | 1400_1500 | 1500_1600 | 1600_1700 | 1700_1800 | 1800_1900 | 1900_2000 | 2000_2100 | 2100_2200 | 2200_2300 | 2300_2400
Speed | 56.0667 | 56.0667 | 56.0667 | 56.0667 | 56.0667 | 56.0476 | 51.5714 | 44.3857 | 43.1476 | 48.0952 | 49.8476 | 50.3381 | 48.9333 | 49.0667 | 47.0524 | 47.1952 | 47.5 | 47.919 | 54.019 | 55.9524 | 56.0476 | 56.0619 | 56.0667 | 56.0667
Chart: Volume by TOD
| 000_100 | 100_200 | 200_300 | 300_400 | 400_500 | 500_600 | 600_700 | 700_800 | 800_900 | 900_1000 | 1000_1100 | 1100_1200 | 1200_1300 | 1300_1400 | 1400_1500 | 1500_1600 | 1600_1700 | 1700_1800 | 1800_1900 | 1900_2000 | 2000_2100 | 2100_2200 | 2200_2300 | 2300_2400
Volume | 15121.8 | 18076.4 | 18173.4 | 22464.9 | 36463.6 | 61413.5 | 126678.8 | 162251 | 167290.9 | 149454.6 | 144134.5 | 142017.7 | 148180.5 | 147881.4 | 154426.4 | 153876 | 151797.1 | 150092.7 | 112326.3 | 76991.6 | 64166 | 53764 | 40462.5 | 26489.8

## Slide 11: Simulation-based APPROACH:DTA-Lite

## Slide 12: MSTM DTA-Lite Model
Dynamic traffic assignment:
Calibrate model parameters – e.g. flow capacity, jam density (for congestion propagation)
Traffic count-based dynamic OD demand calibration
Validate to screenlines, major corridors, ground counts by facility type

## Slide 13: Preliminary Daily Link Volume Comparison
Daily link volume
DTALite-BPR vs. MSTM
Daily link volume DTALite-PQM vs. MSTM
Chart: DTALite-PQM
Chart: DTALite-BPR

## Slide 14: Visualization Examples
Bottleneck
Queue Duration
3D Volume

## Slide 15: Highlights
Tight integration with CUBE
  Allow BPR function, point/spatial queue and simplified kinematic wave model in traffic simulation
  Direct interface for reading CUBE shape files and demand file
Tight integration with sensor data
  Built-in OD demand calibration model that accepts sensor density, flow, and speed data
Future work
  Calibration of road capacity and dynamic OD demand matrix
  Tolling scenarios for detour management
  Activity based model + DTA integration, more behavior-driven model for evaluating emerging traffic management scenarios
  Automated evaluation tool for a large number of road capacity improvement strategies
  Google Transit capability to add transit capability

## Slide 16: THANKS! Q &A
For more information:
http://www.smartgrowth.umd.edu/
E-mail :
fducca@umd.edu Fredrick W. Ducca, TPRG Director
serdogan@umd.edu Sevgi Erdogan, Research Associate
Address:
Suite 1112, Preinkert Field House
University of Maryland
College Park, Maryland 20742
301.405.6788