## Slide 1
Lei Zhang, Ph.D.
Associate Professor
Director, National Transportation Center
Department of Civil and Environmental Engineering
University of Maryland
        301-405-2881, lei@umd.edu
Liang Tang, Nicholas Ferrari, Mingyang Ji
Graduate Research Assistant
University of Maryland
Eric Beckett, Subrat Mahapatra, and Greg Slater
Office of Planning and Preliminary Engineering
Maryland State Highway Administration
MOSAIC – Model Of Sustainability And Integrated Corridors: A Comprehensive Tool for Multimodal Sustainable Corridor Planning
Presentation at the 2015 TRB Planning Applications Conference
Atlantic City, NJ, May 17~21, 2015

## Slide 2: Research Objectives
        Define sustainability indicators for SHA’s Sustainability Initiative and Comprehensive Highway Corridors (CHC) program;
        Provide a user-friendly tool for analyzing the impact of multimodal highway corridor improvements on mobility, safety, socioeconomics, energy and environment, natural resources, and cost;
        Improve current SHA processes related to long-range planning, highway needs inventory, project planning/screening, and environmental stewardship;
        Help SHA save money and time.
MOSAIC

## Slide 3
Select a Corridor
Alternative Improvements
Corridor Data from eGIS
MOSAIC
Impact of Each Candidate Improvement Scenario on:
Sustainability Indicators
Mobility
Energy&Environment
Natural Resource
Cost
Socioeconomics
Safety
MOSAIC Tool Overview

## Slide 4: Sustainability Indicators
MOSAIC

## Slide 5
MOSAIC
MOSAIC Improvement Options
GEOMETRIC IMPROVEMENTS | MULTIMODAL IMPROVEMENTS
Add General Purpose Lanes | Add High Occupancy Vehicle (HOV) Lane
Remove Lanes (Road Diet) | Add High Occupancy Toll (HOT) Lane
Convert At-grade Intersection to Grade Separated Interchange | Add Express Toll Lane (ETL)
 | Add Bus Only Lane / Bus Rapid Transit
 | Add Truck Only Lane
 | Add Light Rail Transit (LRT)
Through the multi-improvement analysis framework, MOSAIC also allows users to apply combinations of geometric improvement and multimodal improvement options to a corridor section at the same time

## Slide 6: Modeling Framework
MOSAIC

## Slide 7: Mode choice models
        Changes to Existing Highway/Transit Services
          Pivot-point Mode Choice Model
        Data needs
  Current market shares of each mode;
  Proposed changes of the Level of Service (LOS) variables for each alternative.
        New Transit Service
          Extended Incremental Logit Model
        Data needs
  Current market shares of each mode;
  Proposed changes of the Level of Service (LOS) variables between the proposed and existing transit mode.
MOSAIC

## Slide 8: MOBILITY
MOSAIC

## Slide 9: SAFETY
MOSAIC

## Slide 10: SOCIO-ECONOMIC IMPACT
Transit Implementation Scores
Facilities’ Compatibility
Aesthetics
Economic Benefits
Livability
Noise
Land Use Attractive
Historical Road and Sites Protection
Visual Appealing
Transportation Factors
Other Factors
Effective
Densities
Travel Time Between Zone Pairs
Costs of Travel/Time
GDP
Number of Employees
Employment Allocation
Categorizing Land-use Pattern & Defining Corresponding Noise Metric Criteria
Estimating Project Noise Exposure
Travel Time Scores
Land-use Mix Scores
MOSAIC

## Slide 11: NATURAL RESOURCES
        Cultural/Historical Sites,
        Steep Slopes,
        Highly Erodible Soils,
        Wetlands, Waterways, Springs/Seeps,
        Floodplains
        Forests,
        Critical Areas,
        Bedrock/Geology Areas,
        Natural Species,
        Storm Water Facilities, etc.
MOSAIC

## Slide 12: ENERGY AND EMISSIONS
MOSAIC

## Slide 13: COST -- Roadway
        General Purpose Lanes
MOSAIC

## Slide 14: Demo: US 29 CASE STUDY
Section 1 (A to B)
IS70 to MD175
Freeway with full access control
Section 2 (B to C)
MD175 to Montgomery Line
Freeway with full access control
Section 3 (C to D)
Montgomery Line to Dale DR
Freeway with traffic signals
Section 4 (D to E)
Dale DR to DC Line
Arterial street with traffic signals
MOSAIC

## Slide 15: 2010 Base Case Traffic Condition
MOSAIC

## Slide 16
Highway and Multimodal Improvement Alternatives
Improvement Alternatives
MOSAIC

## Slide 17
Evaluation Scores
MOSAIC

## Slide 18
Comparison of Alternatives

## Slide 19
MOSAIC Output
Indicators
eGIS
Users
MOSAIC Input Data
MOSAIC Models
Mobility
Natural Resources
Energy and Environment
Socio-Economic
Safety
Cost
Numerical Results
Graphical Results
Summery Reports
construct an eGIS-based system (widget) to select MOSAIC model parameters (spatial & non-spatial),
execute the MOSAIC models, and
create graphic & tabular reports.
Integrating MOSAIC and eGIS

## Slide 20
MOSAIC Widget in eGIS

## Slide 21: Thank you!
        Comments and suggestions are welcome.
Lei Zhang
Associate Professor
Director, National Transportation Center
Department of Civil and Environmental Engineering
University of Maryland
        301-405-2881, lei@umd.edu
MOSAIC