## Slide 1: A Caution on GPS Truck Data
Presented at
15th Applications Conference
Atlantic City May 2015
William G. Allen, Jr., PE
Consultant, Windsor, SC

## Slide 2: Observed Truck Data
Very difficult to obtain
Surveys are expensive, unreliable
GPS data is available via ATRI
  American Transportation Research Institute
  part of American Trucking Association
  a cost-effective option
  probably available nationwide
  Jeff Short, jshort@trucking.org, (703) 838-1966
Notes: The biggest challenge to modelling trucks is getting good observed data. I’ve pretty much given up on conventional surveys. GPS data is a relatively new source of data that can be useful, if you’re careful.
A major source of this data is the A-T-R-I, pronounced “ATRI”. For more information on this data, you can contact Jeff Short at the address shown here.

## Slide 3: What Is It?
Large trucking fleets carry GPS units
  Latitude/longitude and time stamp
    ATRI geocodes to your TAZ system
  Tens of millions of records
  Available for most urban areas
  Every day for a couple of months
Notes: The trucks of most large intercity fleets carry GPS units that record their exact location and time, every few seconds. The fleet owners use this to keep track of their trucks and optimize their routing. Some of this data is provided to the American Trucking Association, who sells it to planning agencies. In theory, it’s a very good source of data on truck locations.

## Slide 4: My Experience
Four-step truck model
  Kansas City
Tour-based truck models
  Atlanta
  Birmingham
Notes: I’ve used the ATRI data three times, in the development of new trip-based and tour-based truck models.

## Slide 5: The Good News
Good data on location, time, speed
  valuable for trip distribution, time of day
Data for multiple days is helpful
Less expensive than surveys
Notes: First, the good news...
This data provides good information on truck locations and speeds. It seems like it’s well-suited for development of a trip distribution model because you can get an observed trip length frequency distribution. The time data should also help with a time of day model.
It is also helpful to have information on multiple days, which lets you better understand the day-to-day variability in truck activity. This variation is typically greater than for personal travel. Finally, this data is a lot less expensive than surveys, which is always attractive.

## Slide 6: The Bad News
Challenge of big data
No data on truck type or operator
  confidentiality is a problem
Only certain trucking companies included
  mostly long-haul
  no owner-operators
  skewed sample
Difficult to expand to the universe
Notes: Now for the bad news.
ATRI imposes very strict confidentiality on this data. I understand why this is important, but I believe they take this a little farther than necessary. You can’t identify the truck size or the type of operator. Also, you can’t find out what kind of carriers are included. They will tell you that it’s fleet trucks that do mostly long-haul travel, so it’s clear that it’s not a completely representative sample. Without additional data, you can’t fully understand the sample that you have and it’s nearly impossible to expand that sample to any kind of universe.

## Slide 7: More Bad News
GPS pings are random
Many data anomalies
  movement but no elapsed time
  elapsed time but no movement
Multi-day files may include same truck
Geocoding is problematic
  internal OK
  external is difficult
Notes: More bad news...
The GPS pings are not uniform with respect to time or location – they seem to be random. This really complicates the data processing.
And there are some odd things about the data that don’t make sense, like discrepancies between time and space.
Often, you see the same truck on different days. This can be helpful for some analyses, but mostly, it’s a problem.
ATRI does not provide the raw latitude/longitude data, due to confidentiality. They will do an automated geocoding to your zone system. This works pretty well for internal zones, but not so well for movements that are outside the modelled cordon. So it’s difficult to identify external and through trips correctly.

## Slide 8: Processing Big Data
Size of database dictates processing methods
Must process carefully to identify trips or tours
  various algorithms exist
  no standardization
  software differences
Notes: One of the new buzz words in information technology these days is “big data”. I’d say it’s accurate to call this “big data”. The data files come as very large flat ASCII files. You can’t open them in Excel. You have to be proficient in database software or a programming language to work with this data.
The data must be processed very carefully to make sense of it. So far, there’s no standardization of the processing software or the algorithms. Everything is custom-written. This means that you need skills in handling large datasets, in understanding the trucking business, and how truck trips are modelled.
Lots of little issues pop up: Do you want to exclude weekends and holidays? How do you combine the data for different days? How to handle records which span multiple days? And so on...

## Slide 9: What is a “Stop”?
If speed < 3 mph, truck is probably stopped
Maybe truck moved a little but didn’t leave the zone – drayage or bad data?
How long can a stop last?
Is origin of trip X always the same as destination of trip X-1?
Notes: Maybe the biggest challenge in working with any GPS data is: how do you define a stop? If all you know is time and location, how can you identify whether the truck has stopped to load or unload cargo, or whether it is stuck in traffic, or the driver is having lunch or refueling the truck? It turns out that it takes a lot of programming to figure out if the truck is really stopped or not.
One example of this involves “drayage”, which is the movement of goods over a very short distance, such as from an unloading area near a ship to a nearby warehouse. Typically, that occurs within a zone and we would not normally consider it to be a real trip. However, without the original lat/long data, it’s hard to know if that is what is happening.
You have to make a lot of assumptions with this data.

## Slide 10: So What?
Truck GPS data can be useful and cost-effective
Can’t build an entire model with it
Difficult to process
  a variety of skills needed
Not a perfect solution -- tread carefully
Notes: I’m really not trying to scare anyone away from using truck GPS data. Just be careful and allow enough time and budget to handle the unknowns. Go into it with your eyes wide open.
Remember that you can’t build a complete model with this data. You need to combine it with other kinds of information. But it can be very useful for trip distribution and time of day models.
I also recommend that you not leave the processing to a data expert. It really should be a transportation planner who knows data handling and who knows something about the trucking business.

## Slide 11: Questions?
(803) 270-7114
wgallen@isp.com
www.williamgallen.com