## Slide 1: Application Experience of Multiple Discrete Continuous Extreme Value (MDCEV) Model for Activity Duration and Trip Departure Prediction in the Jerusalem ABM
Gaurav Vyas, Peter Vovsha (Parsons Brinckerhoff)
Danny Givon, Yehoshua Birotker (Jerusalem Transportation Master Team)

## Slide 2: Modeling Trip Departure Time: Why?
Trip Departure Time Models:
  Important component of Travel Demand Models
  Directly impact temporal distribution of flows in the network
  Essential for integration with Dynamic Traffic Assignment (DTA)

## Slide 3: Modeling Trip Departure Time: Existing Methods
Sequence of regression or hazard duration models:
  For activity duration and trip departure time
  Pros:
    Continuous time
  Cons:
    Scheduling decisions for activities are strictly sequential w/o forward thinking and necessary time reservations

## Slide 4: Modeling Trip Departure Time: Existing Methods
Discrete choice approach:
  Joint activity departure time model for all stops on tour
  Discretized time by departure time/duration bins
  Pros:
    Joint scheduling decision for all stops
  Cons:
    Number of alternatives explodes when the number of duration bins and/or stops increase

## Slide 5: Desired features
Model trip departure and activity duration jointly for all stops on the tour
Incorporate continuous time preferred for a seamless ABM-DTA integration
  Crude discrete departure time results in “lumpiness” of trip loadings for DTA
  Post randomization is arbitrary and violates individual schedule consistency

## Slide 6: Problem Statement
The information known for the tour (example):
  Activities set  {Shopping, Maintenance, Eat Out}
  Sequence: Home  Shopping  Maintenance  Eat Out  Home
  Location of activities
  Tour start and end time

## Slide 7
Home
Shopping
Maintenance
Eat Out
Dep 5:00 PM
Dep ?,
Arr ?
Arr 9:00 PM
Dep ?,
Arr ?
Dep ?,
Arr ?

## Slide 8: Problem Statement
Trip mode is not known at 1st iteration:
  2 min/mile as preliminary estimate of travel time
Trip mode known for 2nd and subsequent iteration:
  Simulated travel time

## Slide 9
Home
Shopping
Maintenance
Eat Out
Dep 5:00 PM
Act Dur?
Arr 9:00 PM
Act Dur?
Act Dur?
Travel time
Travel time
Travel time
Travel time

## Slide 10: Problem Statement
Allocate total activity time on the tour among different activities/stops:
  Given the travel time, activity durations fully define trip departure times
O
Home
Shopping
Maint.
Eat-out
Home
D
Travel time
Activity time
Trip Departure time

## Slide 11: Methodology
Time budget allocation problem
A few budget allocation models in the literature
Model used  Multiple Discrete Continuous Extreme Value (MDCEV) by Bhat (2008)

## Slide 12: What is MDCEV?
Selects from available alternatives (discrete component) and allocates provided budget/time (continuous component) among chosen alternatives
For instance:
  Monday, TPAC 2015
  Time frame  8:30 AM – 5:00 PM
  Given the limited time frame, what sessions one wants to join (discrete component) and for how long (continuous component)

## Slide 13: MDCEV
Generic form of the utility function for activity duration
3 important parameters:
  : Base line utility for alternative k
  : Satiation parameter for alternative k
  : Translation parameter for alternative k

## Slide 14: Why MDCEV?
Satiation effects: Diminishing marginal utility that leads to multiple discrete choices
Chart: Duration, hours
0.25 hrs

## Slide 15: Model Application: Classic MDCEV
Defines activity participation set (discrete component)
Defines duration of chosen activities (continuous component)
Non-chosen alternatives have zero duration

## Slide 16: Model Application: Tour Context
The activity participation set is already known (discrete component is fixed)
A minimum value of activity duration (~5 min) allocated to each stop
MDCEV then applied for the rest of activity time on the tour
MDCEV serves as time allocation model

## Slide 17: HTS Jerusalem 2010
100% GPS-Prompted Recall
Population Sector | Number of households | Average household size
Secular | 4,887 | 3.19
Orthodox | 2,119 | 5.07
Arab | 1,224 | 5.62
Total | 8,230 | 4.03

## Slide 18: Estimation and Application Results for Long (daily) Non-Mandatory Tour (constants only)
Chart: Duration, hours
Activities | Time allocated (hrs)
1=Escorting | 0.5
2=Shopping | 0.9
3=Maintenance | 1.3
4=Breakfast | 0.9
5=Lunch | 1.9
6=Dinner | 3.0
7=Visiting | 2.4
8=Discretionary | 1.1
Total | 12.0

## Slide 19: Estimation Results (key findings)
Explanatory variables | Escorting | Shopping | Maint. | Breakfast | Lunch | Dinner | Visiting | Discretionary (base)
Individual effects |  |  |  |  |  |  |  | 
Orthodox female | High |  |  |  |  |  |  | 
Secular female |  | High |  |  |  |  |  | 
Full-time worker |  |  |  |  | High |  |  | 
Part-time worker | High |  |  |  |  |  |  | 
Age | Decreases with age |  |  |  |  |  |  | 
Household effects |  |  |  |  |  |  |  | 
Lower income |  |  | High |  | High |  | High | 
Tour characteristics |  |  |  |  |  |  |  | 
If activity is primary on the tour | High |  |  |  |  |  |  | 

## Slide 20: Model Application
Time allocation to activities on the tour (MDCEV)
Trip mode choice
Adjusted total activity time after account for known travel time
Total activity time in the tour for MDCEV = Tour end – tour start – total distance * (2 minute per mile) – 5 (mins/activity) * # stops
Highway and Transit Assignment
Known travel time

## Slide 21: Conclusion
Trip departure time for all stops on the tour should be modeled jointly
Continuous time is preferred for ABM-DTA integration
MDCEV is a valuable tool for the problem statement
Further testing of the model in the equilibrium context with DTA is needed