## Slide 1: Evaluating GPS Technology Used for Household Surveys
Kathy Yu, Arash Mirzaei, Behruz Paschai
North Central Texas Council
of Governments (NCTCOG)
15th TRB Conference on
Transportation Planning Applications
Atlantic City, NJ
May 18, 2015

## Slide 2
Background
  NCTCOG was interested in understanding how technologies could be used in household surveys and what was known about the GPS technologies.
  Before we use technologies in a survey, it is important to know the methods fully including accuracy, and strengths/weaknesses.

## Slide 3: Study Design
  Three Technologies Demonstrated
    GPS Logger
    Smart Phone App
    Cell Phone Triangulation
  Each technology was required to work passively.
  Data collection of all technologies would be conducted simultaneously.

## Slide 4
Study Design
  Participants were divided into 3 waves.
  During the data collection, participant was asked to do the following:
  Complete a week long data collection period.
  Carry 1, 2, or 3 technologies during the week.
  Complete a travel diary for the first 24 hours.

## Slide 5: Study Steps
  NCTCOG recruits participants.
  Consultants conduct data collection.
  NCTCOG processes travel diary while Consultants process technology data.
  NCTCOG compares technology locations with travel diary locations.
  NCTCOG investigates non-matches.

## Slide 6
Habitual Locations Form
  The consultants and NCTCOG designed a Habitual Locations form which records:
  Home Location
  Primary and Secondary Workplace Locations
  School Location
  Up to 3 Additional Locations Visited Most Often.
  Other Information Requested:
  Preferred Survey Dates
  Preferred Technologies
  Mobile Phone Model, O/S, Carrier.

## Slide 7
Habitual Locations Form Excerpt

## Slide 8
Travel Diary Form
  The Consultants and NCTCOG designed a Travel Diary to record the following:
  Place Name/Address at 3 a.m.
  Successive Locations
    Place Name and Address
    Arrival and Departure Time
    Mode of Access
    Activity at Location

## Slide 9
Travel Diary Form Excerpt

## Slide 10
Participant Details
NCTCOG Status | Percent
COG Employee | 58%
Other | 42%
Home State | Percent
Texas | 88%
Other | 12%
Gender | Percent
Male | 45%
Female | 55%

## Slide 11
Technology Used | Count | Pct.
Logger Only | 25 | 17%
Smart Phone App Only | 12 | 8%
Triangulation Only | 7 | 5%
TOTAL | 149 | 100%
Technology Used | Count | Pct.
Logger Only | 25 | 17%
Smart Phone App Only | 12 | 8%
Triangulation Only | 7 | 5%
Logger and Smart Phone App | 16 | 11%
Logger and Triangulation | 19 | 13%
Smart Phone App and Triangulation | 12 | 8%
TOTAL | 149 | 100%
Technology Usage Breakdown
Technology Used | Count | Pct.
Logger Only | 25 | 17%
Smart Phone App Only | 12 | 8%
Triangulation Only | 7 | 5%
Logger and Smart Phone App | 16 | 11%
Logger and Triangulation | 19 | 13%
Smart Phone App and Triangulation | 12 | 8%
All Technologies | 58 | 39%
TOTAL | 149 | 100%

## Slide 12
Wave Breakdown
Wave | # Logger Users | # Smart Phone App Users | # Triangulation Users | Total Users
May 15 | 35 | 27 | 23 | 44
June 5 | 42 | 35 | 34 | 53
June 21 | 41 | 36 | 39 | 52
TOTAL | 118 | 98 | 96 | 149

## Slide 13
 | GPS Logger | Smart Phone App | Triangulation
Registered Participants | 118 | 98 | 96
 | GPS Logger | Smart Phone App | Triangulation
Registered Participants | 118 | 98 | 96
Did not return a travel diary | 12 | 21 | 17
 | GPS Logger | Smart Phone App | Triangulation
Registered Participants | 118 | 98 | 96
Did not return a travel diary | 12 | 21 | 17
Had no GPS data for travel day | 21 | 19 | 5
Participants with Data To Compare
 | GPS Logger | Smart Phone App | Triangulation
Registered Participants | 118 | 98 | 96
Did not return a travel diary | 12 | 21 | 17
Had no GPS data for travel day | 21 | 19 | 5
# Participants with Data to Compare | 85 | 58 | 74
% Registered Participants with Data to Compare | 72% | 59% | 77 %

## Slide 14
Location Match Results
  A match was defined as the technology matching the diary location within 15 min. and 0.25 miles.
 | GPS Logger | Smart Phone App | Triangulation
# Travel Diary Location Records |  |  | 
# Technology Location Records |  |  | 
# Diary Matches |  |  | 
% Match against Total |  |  | 
 | GPS Logger | Smart Phone App | Triangulation
# Travel Diary Location Records | 585 |  | 
# Technology Location Records | 566 |  | 
# Diary Matches | 476 |  | 
% Match against Total | 81% |  | 
 | GPS Logger | Smart Phone App | Triangulation
# Travel Diary Location Records | 585 | 398 | 
# Technology Location Records | 566 | 328 | 
# Diary Matches | 476 | 261 | 
% Match against Total | 81% | 66% | 
 | GPS Logger | Smart Phone App | Triangulation
# Travel Diary Location Records | 585 | 398 | 520
# Technology Location Records | 566 | 328 | 484
# Diary Matches | 476 | 261 | 84
% Match against Total | 81% | 66% | 16%

## Slide 15
Person Match Results
 | GPS Logger | Smart Phone App | Triangulation
% People-50% diary match | 94% | 78% | 27%
% People-75% diary match | 79% | 50% | 8%
% People-100% diary match | 48% | 24% | 5%
  Considering only the people with at least one location match with the corresponding technology.

## Slide 16: Unmatched Travel Diary Records
For the GPS Logger and Smart Phone App:
  NCTCOG reviewed the technology stops and raw data during the time of a missed travel diary record.
  NCTCOG tried to determine a reason for each missed stop, and notice any patterns or common issues.
  NCTCOG did not have any details about algorithms used by consultants.

## Slide 17: Analyze Non-Match: Logger
Non-Match Reason | # Records | % Records
Match Made | 476 | 81%
TOTAL | 585 | 100%
Non-Match Reason | # Records | % Records
Match Made | 476 | 81%
No logger data existed for all/part of corresponding trip. | 62 | 11%
TOTAL | 585 | 100%
Non-Match Reason | # Records | % Records
Match Made | 476 | 81%
No logger data existed for all/part of corresponding trip. | 62 | 11%
Short or Rolling Stops–(2-3 min)* | 34 | 6%
TOTAL | 585 | 100%
Non-Match Reason | # Records | % Records
Match Made | 476 | 81%
No logger data existed for all/part of corresponding trip. | 62 | 11%
Short or Rolling Stops–(2-3 min)* | 34 | 6%
Possible Diary Issue | 9 | <2%
Other | 4 | <1%
TOTAL | 585 | 100%
* 24% of Short Trips corresponded to Habitual Locations.

## Slide 18: Analyze Non-Match: Smartphone
* 29% of Short Trips corresponded to Habitual Locations.
Non-Match Reason | # Records | % Records
Match made | 261 | 66%
TOTAL | 398 | 100%
Non-Match Reason | # Records | % Records
Match made | 261 | 66%
No Smartphone Data existed for all/part of corresponding trip | 89 | 22%
Short or Rolling Stops–(2-3 min)* | 14 | 4%
TOTAL | 398 | 100%
Non-Match Reason | # Records | % Records
Match made | 261 | 66%
No Smartphone Data existed for all/part of corresponding trip | 89 | 22%
Short or Rolling Stops–(2-3 min)* | 14 | 4%
Stop Not Identified, but Raw Data shows at location | 20 | 5%
TOTAL | 398 | 100%
Non-Match Reason | # Records | % Records
Match made | 261 | 66%
No Smartphone Data existed for all/part of corresponding trip | 89 | 22%
Short or Rolling Stops–(2-3 min)* | 14 | 4%
Stop Not Identified, but Raw Data shows at location | 20 | 5%
Possible Diary Issue | 6 | <2%
Other | 8 | 2%
TOTAL | 398 | 100%

## Slide 19: Unmatched Technology Records
Did the technology capture stops that the user made but did not record in the diary?
NCTCOG looked at longitude/latitude of unmatched technology records to determine:
  if it was a valid location
  is it a reasonable stop given the rest of the user’s travel diary stops.

## Slide 20
Classification | Number of Records | % of New Records Found
Total Unmatched Logger Locations | 91 | 100%
Classification | Number of Records | % of New Records Found
Match to Street/Intersection | 28 | 31%
Duplicate of Existing Diary Record | 10 | 11%
Miscellaneous | 19 | 21%
Total Unmatched Logger Locations | 91 | 100%
Classification | Number of Records | % of New Records Found
New Valid Location | 32 | 35%
New Diary Match (user did not specify location well) | 2 | 2%
Match to Street/Intersection | 28 | 31%
Duplicate of Existing Diary Record | 10 | 11%
Miscellaneous | 19 | 21%
Total Unmatched Logger Locations | 91 | 100%
Unmatched Logger Records

## Slide 21
Classification | Number of New Records | % of New Records Found
Total Unmatched Smartphone Locations | 70 | 100.00%
Classification | Number of New Records | % of New Records Found
Duplicate of Existing Diary Record | 16 | 23%
Match to Street/Intersection | 9 | 13%
Created New Location from inconsistent points | 9 | 13%
Miscellaneous | 19 | 27%
Total Unmatched Smartphone Locations | 70 | 100.00%
Classification | Number of New Records | % of New Records Found
New Valid Location | 17 | 24%
Duplicate of Existing Diary Record | 16 | 23%
Match to Street/Intersection | 9 | 13%
Created New Location from inconsistent points | 9 | 13%
Miscellaneous | 19 | 27%
Total Unmatched Smartphone Locations | 70 | 100.00%
Unmatched Smartphone Records

## Slide 22: Feedback Questionnaire
  After participating in the survey, a feedback questionnaire was sent to all participants, which contained 17 questions.
  Allowed consultants to get feedback on use of their technology.
  95 people responded.

## Slide 23: Feedback – Future Survey Format
  If asked to participate in a household travel survey in the future, I would be willing to use (check all that apply):
Answer Option | % Selected
Travel Diary | 51%
GPS Logger | 72%
Smartphone App | 53%
Triangulation | 57%

## Slide 24: Feedback – Diary or Technology
  What is your preference for using a paper travel diary and using a GPS/location-based technology?
I prefer using … | % Respondents
GPS technology ONLY | 69%
Paper travel diary AND GPS technology TOGETHER | 14%
Paper travel diary ONLY | 5%
No preference | 12%
TOTAL | 100%

## Slide 25: Observations
  Travel Diary times and locations were subject to user error.
  Almost 2/3rd of the diary trip ends are habitual locations that were asked before the diary survey.
  Contractors’ algorithms were fairly successful in differentiating signals from real end points of trips.

## Slide 26: Improvement Areas
  Short trip stops are hard to capture. Habitual Locations may be useful.
  For logger and smartphone app, many missed locations were due to the lack of recorded data.
  Further testing can be done on teaching people to use technology correctly to minimize user error.

## Slide 27: Conclusions
  Continued refinement of algorithms can improve results.
  The feedback survey showed 83% preferred using technology in a future survey. Only 5% preferred travel diary only.
  Technology methods may not be appropriate for all survey participants.

## Slide 28
Contact Information
  Kathy Yu kyu@nctcog.org
  Arash Mirzaei amirzaei@nctcog.org
  Behruz Paschai bpaschai@nctcog.org