## Slide 1: Evaluation of Advanced Driver Assistance Systems: Data and Planning Implications
Krishnan Viswanathan, CDM Smith
Roberto Miquel, CDM Smith
Chris Edmonston, Florida DOT
Ed Hutchinson, Florida DOT

## Slide 2: Agenda
Purpose
Study Design
Technology
User Interface
Data Processing
Results
Performance Measures
Summary and Next Steps

## Slide 3: purpose
Study Level 0 Automation
Evaluate impacts of Advanced Driver Assistance System (ADAS)
Measure changes in driver behavior in face of driver feedback technology
Measure performance improvements as a result of feedback
Incorporate performance improvements into the Planning Process

## Slide 4: study design
Instrument 100 vehicles in Florida DOT District 7
Vehicles from Florida DOT and local transit agencies
100 vehicles have GeoTab devices
50 vehicles have Mobileye devices
Study duration is 1 year
Installs completed in August
Data collection underway

## Slide 5: Technology - geotab
Provides vehicle diagnostics information
Real time data on vehicle exceptions and performance
Data transmitted via cellular signals
Dashboard to visualize data

## Slide 6: Technology - mobileye
Daylight Pedestrian Collision Warning, including Bicycle Detection
Forward Collision Warning, both in Highway and Urban areas, including Motorcycle Detection
Lane Departure Warning
Headway Monitoring and Warning

## Slide 7: User interface

## Slide 8: User interface

## Slide 9: User interface

## Slide 10: Data processing
Daily stream of data
  Mobileye exceptions
  Geotab exceptions
Data arrives with lat/long information, time of day, and vehicle id for each type of Mobileye or Geotab exception
Data converted into R data.table for processing and analysis
ArcGIS used to spatially locate data

## Slide 11: Results ODOMETER READINGS
 | Sep 2014 | Oct 2014 | Nov 2014 | Dec 2014 | Jan 2015 | Feb 2015 | Mar 2015
Min | 47 | 68 | 13 | 104 | 1 | 1 | 1
Max | 18,001 | 21,382 | 22,440 | 19,634 | 23,968 | 13,820 | 12,838
Median | 3,896 | 4,049 | 3,189 | 3,216 | 3,388 | 3,203 | 2,765
Mean | 4,461 | 4,812 | 4,301 | 4,301 | 4,414 | 4,274 | 3,863

## Slide 12: Results Monthly mileage by vehicle
Chart: 

## Slide 13: Results distance, speed, trip duration

## Slide 14: Results Mobileye exceptions
 | Mobileye Events |  |  |  |  |  | 
Type of Warning | Sep-14 | Oct-14 | Nov-14 | Dec-14 | Jan-15 | Feb-15 | Mar-15
 | Number | Number | Number | Number | Number | Number | Number
ME Forward Collision Warning | 1,107 | 1,034 | 189 | 179 | 218 | 180 | 162
ME Headway Warning (Tailgating) | 69,967 | 65,401 | 8,310 | 7,547 | 11,860 | 10,077 | 8,283
ME Left Lane Departure | 14,124 | 10,653 | 1,743 | 2,140 | 2,233 | 2,290 | 1,815
ME Pedestrian Collision Warning | 645 | 433 | 164 | 144 | 178 | 127 | 75
ME Right Lane Departure | 29,617 | 21,816 | 7,504 | 7,517 | 9,069 | 8,778 | 7,728
ME Urban Forward Collision Warning | 2,204 | 724 | 432 | 345 | 544 | 338 | 361
Total | 117,664 | 100,061 | 18,342 | 17,872 | 24,102 | 21,790 | 18,424
Chart: Mobileye Warning Over Time
| 41883 | 41913 | 41944 | 41974 | 42005 | 42036 | 42064
ME Forward Collision Warning | 0.009 | 0.01 | 0.01 | 0.01 | 0.009 | 0.0083 | 0.0088
ME Headway Warning (Tailgating) | 0.595 | 0.654 | 0.453 | 0.422 | 0.492 | 0.4625 | 0.4496
ME Left Lane Departure | 0.12 | 0.106 | 0.095 | 0.12 | 0.093 | 0.1051 | 0.0985
ME Pedestrian Collision Warning | 0.005 | 0.004 | 0.009 | 0.008 | 0.007 | 0.0058 | 0.0041
ME Right Lane Departure | 0.252 | 0.218 | 0.409 | 0.421 | 0.376 | 0.4028 | 0.4195
ME Urban Forward Collision Warning | 0.019 | 0.007 | 0.024 | 0.019 | 0.023 | 0.0155 | 0.0196

## Slide 15: Results Mobileye events by vehicle type
Chart: 
| Car | Large Bus | Pickup | Small Bus | Truck | Van
ME Forward Collision Warning | 0.020052 | 0.012534 | 0.0050271 | 0.0082144 | 0.003247 | 0.0088623
ME Headway Warning (Tailgating) | 0.5875 | 0.4734 | 0.79047 | 0.64746 | 0.39901 | 0.76275
ME Left Lane Departure | 0.18385 | 0.11939 | 0.064054 | 0.11374 | 0.13895 | 0.10663
ME Right Lane Departure | 0.19271 | 0.3577 | 0.13266 | 0.20223 | 0.45813 | 0.11305
ME Pedestrian Collision Warning | 0.00052083 | 0.010365 | 5.5243e-05 | 0.005347 | 0.00018379 | 0.00031936
ME Urban Forward Collision Warning | 0.015365 | 0.02661 | 0.007734 | 0.023009 | 0.00049011 | 0.0083832

## Slide 16: Results GEOTAB exceptions
 | Sep-14 | Oct-14 | Nov-14 | Dec-14 | Jan-15 | Feb-15 | Mar-15
Speeding | 19,380 | 23,176 | 17,707 | 16,966 | 16,846 | 14,448 | 16,517
Hard Acceleration | 1,423 | 1,195 | 986 | 1,199 | 1,042 | 1,166 | 1,120
Harsh Cornering | 570 | 877 | 622 | 757 | 717 | 688 | 906
Harsh Braking | 106 | 264 | 125 | 242 | 268 | 110 | 194
Total | 21,479 | 25,512 | 19,440 | 19,164 | 18,873 | 16,412 | 18,737

## Slide 17: Results Comparisons of vehicles with and without mobileye
Chart: Anchor Towing
| Oct 2014 | Nov 2014 | Dec 2014 | Jan 2015 | Feb 2015 | Mar 2015
Anchor Towing, Administrative, Pickup - Standard | 100 | 95.733 | 87.368 | 87.4102 | 54.1191 | 43.7262
Anchor Towing, Administrative, Pickup - Standard, Mobileye | 100 | 88.33 | 65.0149 | 24.0089 | 49.7522 | 69.7225
Chart: FDOT D7 Car
| Oct 2014 | Nov 2014 | Dec 2014 | Jan 2015 | Feb 2015 | Mar 2015
FDOT District 7, Administrative, Car | 100 | 47.1721 | 76.5343 | 55.4753 | 114.9218 | 119.3742
FDOT District 7, Administrative, Car, Mobileye | 100 | 55.0107 | 68.0171 | 57.3561 | 102.5586 | 126.9723
Chart: HART Large Bus
| Oct 2014 | Nov 2014 | Dec 2014 | Jan 2015 | Feb 2015 | Mar 2015
HART, Administrative, Bus - Large, HART Maintenance, HART Safety | 100 | 66.9151 | 80.4769 | 57.7943 | 66.8554 | 56.006
HART, Administrative, Bus - Large, HART Maintenance, HART Safety, Mobileye | 100 | 80.2408 | 90.577 | 83.022 | 68.0365 | 96.181
Chart: HART Small Bus
| Oct 2014 | Nov 2014 | Dec 2014 | Jan 2015 | Feb 2015 | Mar 2015
HART, Administrative, Bus - Small, HART Maintenance, HART Safety | 100 | 82.3478 | 67.5794 | 96.621 | 72.2983 | 68.3367
HART, Administrative, Bus - Small, HART Maintenance, HART Safety, Mobileye | 100 | 47.5614 | 45.8882 | 43.7522 | 78.6757 | 97.7216

## Slide 18: Precipitation Effects
0.5 in or more rain measured
Exception Type | 10-Nov | 17-Nov | 18-Nov
ME Forward Collision Warning | 7 | 8 | 6
ME Headway Warning (Tailgating) | 434 | 205 | 326
ME Left Lane Departure | 151 | 100 | 86
ME Pedestrian Collision Warning | 4 | 5 | 6
ME Right Lane Departure | 637 | 300 | 519
ME Urban Forward Collision Warning | 23 | 18 | 14
Total | 1256 | 636 | 957

## Slide 19: Results Total mobileye exceptions densities

## Slide 20: Results forward collision exceptions densities

## Slide 21: Some performance measures
Driver safety metrics
  Lateral Vehicle Control – such as lane positioning
  Longitudinal Vehicle Control – such as speed maintenance
Overall roadway safety
  Number of collisions averted
  No. of accidents

## Slide 22: Summary and next steps
Noticeable change in driver behavior by number of incidents
  Reduced number of incidents
However, don’t notice statistically significant changes in the vehicles with and without Mobileye
Critical to know context of operations
Develop performance measures to quantify change due to these devices

## Slide 23: CONTACT
Krishnan Viswanathan
CDM Smith
viswanathank@cdmsmith.com
850-386-9500