## Slide 1
18 May 2015
Kelly J. Clifton, PhD *
Patrick A. Singleton*
Christopher D. Muhs*
Robert J. Schneider, PhD†
* Portland State Univ. † Univ. Wisconsin–Milwaukee
Development of a Pedestrian Demand Estimation Tool: a Destination Choice Model
CC Glenn Dettwiler, Flickr

## Slide 2: Background
Why model pedestrian travel?
health & safety
new data
mode shifts
greenhouse gas emissions
plan for pedestrian investments
& non-motorized facilities

## Slide 3: Project overview
Metro: metropolitan planning organization for Portland, OR
Two research projects
travel demand estimation model
pedestrian demand estimation model
pedestrian scale
pedestrian environment
destination
choice
mode
choice

## Slide 4: Current method
Trip Distribution or Destination Choice (TAZ)
Mode Choice (TAZ)
Trip Assignment
Pedestrian Trips
All Trips
Pedestrian Trips
Vehicular Trips
TAZ = transportation analysis zone
Trip Generation (TAZ)

## Slide 5: New method
TAZ = transportation analysis zone
PAZ = pedestrian analysis zone
Trip Generation (PAZ)
Trip Distribution or Destination Choice (TAZ)
Mode Choice (TAZ)
Trip Assignment
Pedestrian Trips
Walk Mode Split (PAZ)
Destination Choice (PAZ)
I
II
All Trips
Pedestrian Trips
Vehicular Trips

## Slide 6: Pedestrian analysis zones
TAZs
PAZs
Home-based work trip productions
1/20 mile = 264 feet ≈ 1 minute walk
Metro: ~2,000 TAZs  ~1.5 million PAZs

## Slide 7: Pedestrian environment
Pedestrian Index of the Environment (PIE)
PIE is a 20–100 score total of 6 dimensions, calibrated to observed walking activity:
People and job density
Transit access
Block size
Sidewalk extent
Comfortable facilities
Urban living infrastructure

## Slide 9: Walk mode split
Probability(walk) = f(traveler characteristics, pedestrian environment)
I
Walk Mode Split (PAZ)
Pedestrian Trips
Vehicular Trips
Data: 2011 OR Household Activity Survey: (4,000 walk trips) ÷ (50,000 trips) = 8% walk
Model: binary logistic regression

## Slide 10: Walk Mode Split Results
Household characteristics
I
+ positively related to walking | – negatively related to walking
number of children | age of household
 | vehicle ownership
Chart: Increase in odds of walking
 | 0.036 | 0.044 | 0.054
home–work trips
home–other trips
other–other trips
Pedestrian environment
+ positively related to walking
  + 1 point PIE
  associated with:

## Slide 11: Destination choice
Prob(dest.) = function of…
  network distance
  size ( # of destinations )
  pedestrian environment
  traveler characteristics
Data: 2011 OHAS (4,000 walk trips)
Method: multinomial logit model
random sampling
Spatial unit: super-pedestrian analysis zone
Models estimated for 6 trip purposes
II
Pedestrian Trips
Destination Choice (PAZ)

## Slide 12: DC Model Specification
Key variables
Impedance
Attractiveness
Ped supports
Ped barriers
Traveler attributes
Add’l variables
Network distance btw. zones
Employment by category (within ln)
PIE
Slope, x-ings, fwy

## Slide 13: Destination choice results
 | HB Work | HB Shop | HB Rec | HB Other | NHB Work | NHB NW
Sample size | 305 | 405 | 643 | 1,108 | 732 | 705
Pseudo R2 | 0.45 | 0.68 | 0.42 | 0.53 | 0.59 | 0.54

## Slide 14: Results : key variables
 | HB Work | HB Shop | HB Rec | HB Other | NHB Work | NHB NW
Distance (mi) |  |  |  | -1.94** | -1.43** | -1.45**
Distance * Auto (y) | -1.35** |  |  |  |  | 
Distance * Auto (n) | -0.96** |  |  |  |  | 
Distance * Child (y) |  | -2.29** | -1.76** |  |  | 
Distance * Child (n) |  | -1.54** | -1.52** |  |  | 
Size terms (ln) | 0.50** | 0.88** | 0.05* | 0.41** | 0.36** | 0.39**
(‘ = p < 0.10, * = p < 0.05, ** = p < 0.01) |  |  |  |  |  | 

## Slide 15: Results : key variables
 | HB Work | HB Shop | HB Rec | HB Other | NHB Work | NHB NW
Distance (mi) |  |  |  | -1.94** | -1.43** | -1.45**
Distance * Auto (y) | -1.35** |  |  |  |  | 
Distance * Auto (n) | -0.96** |  |  |  |  | 
Distance * Child (y) |  | -2.29** | -1.76** |  |  | 
Distance * Child (n) |  | -1.54** | -1.52** |  |  | 
Size terms (ln) | 0.50** | 0.88** | 0.05* | 0.41** | 0.36** | 0.39**
(‘ = p < 0.10, * = p < 0.05, ** = p < 0.01) |  |  |  |  |  | 
Distance has the most influence on destination choices
Auto ownership and children in HH moderate effects

## Slide 16: Results : key variables
 | HB Work | HB Shop | HB Rec | HB Other | NHB Work | NHB NW
Distance (mi) |  |  |  | -1.94** | -1.43** | -1.45**
Distance * Auto (y) | -1.35** |  |  |  |  | 
Distance * Auto (n) | -0.96** |  |  |  |  | 
Distance * Child (y) |  | -2.29** | -1.76** |  |  | 
Distance * Child (n) |  | -1.54** | -1.52** |  |  | 
Size terms (ln) | 0.50** | 0.88** | 0.05* | 0.41** | 0.36** | 0.39**
(‘ = p < 0.10, * = p < 0.05, ** = p < 0.01) |  |  |  |  |  | 
No. of destinations inc. odds of choosing particular zone
# Retail destinations dominates shopping purpose

## Slide 17: Results : ped variables
 | HB Work | HB Shop | HB Rec | HB Other | NHB Work | NHB NW
PIE (avg) | 0.03** | n.s. | n.s. | 0.03** | 0.02* | 0.02**
Avg. slope (°) | n.s. | -0.20* | n.s. | -0.42** | -0.16** | n.s.
Major-major xing (y) | n.s. | 0.60** | 0.42’ | n.s. | n.s. | n.s.
Freeway (y) | n.s. | -0.95** | n.s. | n.s. | n.s. | 0.27’
% Industrial jobs | -1.00* | -1.82** | n.s. | -0.40’ | -1.66** | n.s.
(‘ = p < 0.10, * = p < 0.05, ** = p < 0.01) n.s. = not significant |  |  |  |  |  | 

## Slide 18: Results : ped variables
 | HB Work | HB Shop | HB Rec | HB Other | NHB Work | NHB NW
PIE (avg) | 0.03** | n.s. | n.s. | 0.03** | 0.02* | 0.02**
Avg. slope (°) | n.s. | -0.20* | n.s. | -0.42** | -0.16** | n.s.
Major-major xing (y) | n.s. | 0.60** | 0.42’ | n.s. | n.s. | n.s.
Freeway (y) | n.s. | -0.95** | n.s. | n.s. | n.s. | 0.27’
% Industrial jobs | -1.00* | -1.82** | n.s. | -0.40’ | -1.66** | n.s.
(‘ = p < 0.10, * = p < 0.05, ** = p < 0.01) n.s. = not significant |  |  |  |  |  | 
Ped supports: PIE increases odds of dest choice for many trip purposes

## Slide 19: Results : ped variables
 | HB Work | HB Shop | HB Rec | HB Other | NHB Work | NHB NW
PIE (avg) | 0.03** | n.s. | n.s. | 0.03** | 0.02* | 0.02**
Avg. slope (°) | n.s. | -0.20* | n.s. | -0.42** | -0.16** | n.s.
Major-major xing (y) | n.s. | 0.60** | 0.42’ | n.s. | n.s. | n.s.
Freeway (y) | n.s. | -0.95** | n.s. | n.s. | n.s. | 0.27’
% Industrial jobs | -1.00* | -1.82** | n.s. | -0.40’ | -1.66** | n.s.
(‘ = p < 0.10, * = p < 0.05, ** = p < 0.01) n.s. = not significant |  |  |  |  |  | 
Ped barriers:
Slope, major crossings, and presence of freeways have mixed impacts

## Slide 20: Results : ped variables
 | HB Work | HB Shop | HB Rec | HB Other | NHB Work | NHB NW
PIE (avg) | 0.03** | n.s. | n.s. | 0.03** | 0.02* | 0.02**
Avg. slope (°) | n.s. | -0.20* | n.s. | -0.42** | -0.16** | n.s.
Major-major xing (y) | n.s. | 0.60** | 0.42’ | n.s. | n.s. | n.s.
Freeway (y) | n.s. | -0.95** | n.s. | n.s. | n.s. | 0.27’
% Industrial jobs | -1.00* | -1.82** | n.s. | -0.40’ | -1.66** | n.s.
(‘ = p < 0.10, * = p < 0.05, ** = p < 0.01) n.s. = not significant |  |  |  |  |  | 
Ped barriers:
Ratio of industrial jobs to total jobs suggests industrial uses deter ped destination choices

## Slide 21: Some Interpretation
miles

## Slide 22: Some Interpretation
PIE = 75
PIE = 85
miles

## Slide 23: Conclusions
One of the first studies to examine destination choice of pedestrian trips
Pedestrian scale analysis w/ pedestrian-relevant variables
Distance and size have the most influence on ped. dest. choice
Supports and barriers to walking also influence choice
Traveler characteristics moderate distance effect

## Slide 24: Future work
Model improvements
  Choice set generation method & sample sizes
  Explore non-linear effects & other interactions
Model validation & application
Predict potential pedestrian paths
Test method in other region(s)
Incorporation into Metro trip-based model

## Slide 25: Questions?
Project report/info: http://otrec.us/project/510
http://otrec.us/project/677
Kelly J. Clifton, PhD kclifton@pdx.edu
Christopher D. Muhs muhs@pdx.edu
Patrick A. Singleton patrick.singleton@pdx.edu
Robert J. Schneider, PhD rjschnei@uwm.edu

## Slide 26: Destination choice results
 | HB Work | HB Shop | HB Rec | HB Oth | NHB Work | NHB NW
Distance (mi) |  |  |  | -1.94** | -1.43** | -1.45**
Distance * Auto (y) | -1.35** |  |  |  |  | 
Distance * Auto (n) | -0.96** |  |  |  |  | 
Distance * Child (y) |  | -2.29** | -1.76** |  |  | 
Distance * Child (n) |  | -1.54** | -1.52** |  |  | 
Size terms (ln) | 0.50** | 0.88** | 0.05* | 0.41** | 0.36** | 0.39**
Retail Jobs (#) |  | + | + |  | + | +
Finance Jobs (#) |  |  |  |  | + | 
Gov’t jobs (#) |  |  | + |  |  | +
Retail + gov’t jobs (#) |  |  |  | + |  | 
Ret + fin + gov’t jobs (#) | + |  |  |  |  | 
Other jobs (#) | + | + | + | + | + | +
Households (#) |  |  | — | — |  | +
Park in zone (y) |  |  | 0.48** | n.s. |  | 
PIE (avg) | 0.03** | n.s. | n.s. | 0.03** | 0.02* | 0.02**
Avg. slope (°) | n.s. | -0.20* | n.s. | -0.42** | -0.16** | n.s.
Major-major xing (y) | n.s. | 0.60** | 0.42’ | n.s. | n.s. | n.s.
Freeway (y) | n.s. | -0.95** | n.s. | n.s. | n.s. | 0.27’
% Industrial jobs | -1.00* | -1.82** | n.s. | -0.40’ | -1.66** | n.s.
Sample size | 305 | 405 | 643 | 1,108 | 732 | 705
Pseudo R2 | 0.45 | 0.68 | 0.42 | 0.53 | 0.59 | 0.54
Coefficients with #s are significant (‘ = p < 0.10, * = p < 0.05, ** = p < 0.01), others are not significant (p > 0.10). |  |  |  |  |  |