## Slide 1: Spatial Resolution in SANDAG Activity-Based Model: How Much More Detail Is Enough?
15th TRB National Transportation Planning Applications Conference, Columbus OH
May 18th, 2015
Wu Sun, Gregor Schroeder & Matt Keating
San Diego Association of Governments (SANDAG)
Notes: My topic today is---READ
Question try to address is- READ
I want to acknowledge:
SANDAG co-authors--Names
PB, RSG, and Hood Transportation Consulting who worked on various parts of the model.

## Slide 2: Background
SANDAG Activity-Based Model (ABM) and Active Transportation (AT) Model
ABM/AT model applications
Spatial resolution in models
Notes: SANDAG’s ABM was completed in early 2013. In the past two years, many improvements to the ABM. One of the improvement is the addition of AT model.
Starting from late 2013, we have been using integrated ABM and AT model in SANDAG RTP applications. The new RTP is named San Diego Forward.
For the first time, AT is included in the RTP similar to highway and transit transportation.
The introduction of AT model makes finer spatial resolution important. As it is widely believed, because non-motorized modes tend to have shorter trips, a small zonal system is necessary in order to model AT properly.
In my presentation, I will share some insight of the impact of spatial resolution from the experience we have in San Diego.

## Slide 3: Integrated ABM & AT Model
Enhanced ABM
CTM
Trans. System
Trans. Policy
Traffic
Assignment
System
Performance
Environmental
Impact
Economic
Analysis
LU Models
Special Models
bicycle & Ped
Route Choices
Improved NM Impedance
Improved Mode Choices
AT Model
Notes: Let me start with a brief overview of the integrated ABM-AT model structure.
ABM flow chart with AT included.
Inputs: READ.
Core: ABM.
Enhancement:
  NM impedance
  Mode choice
  Bike route choice
Outputs: READ.
The components in the circle are within the AT scope.

## Slide 4: Spatial Resolution
MGRA (gray lines)
23002 MGRA
4996 TAZs
MGRA: Master Geographic Reference Area (Grey Lines)
TAZ: Transportation Analysis Zone (Orange Line)
Notes: In the SANDAG model, we have two level of spatial resolutions:
TAZ-5K
MGRA (Master Geographic Reference Area)-think a MGRA as a micro zone-23K
Orange and gray boundaries.

## Slide 5: What Are Affected by Spatial Resolutions?
Land use inputs
Synthetic population
Non-motorized impedances
  MGRA-MGRA walk
  MGRA-MGRA bike
Transit impedances
  MGRA-TAP walk
Highway impedances?
Vary by scenario
Notes: To understand the impact of spatial resolution, let’s take a look at what are affected by spatial resolutions.
Land use inputs:
Income
Employment
School enrollment
PopSyn is tied to zones.
Affect NM impedances
Affect walk to transit impedances
Does it affect highway impedance? Answer is yes. But, there is a but……. In highway skimming and assignment, we still use TAZ based system.
In this study, we keep land use and synthetic population constant. We create two scenarios with different spatial resolutions, and vary NM and transit impedances.

## Slide 6: A Base Scenario
Path between zone 1 and 2
1
2
Notes: This is the base scenario.
Consider this as a simplified TAZ-based geography
Path between zone 1 and 2. The path is the main factor affects impedances between zone 1 and 2, and in turn the whole model chain.

## Slide 7: A Scenario with Smaller Zones
Path between zone 1 &1a and 2
1
2
1a
Notes: This is a scenario with smaller zones.
Consider this as a simplified MGRA-based geography (click one, first show)
Path between zone 1 and zone 2 is longer. Path between zone 1a and zone 2 is shorter
Now the question is: how smaller zones affect model results?

## Slide 8: How Spatial Resolutions Affect the Model?
Demand side
  Location choices: tour, trip, and parking locations
  Other choices?
Supply side
  Skimming: walk, bike, transit, and highway.
  Highway assignment?
  Transit assignment?
Notes: In any models there is a demand side and a supply side.
The demand side includes tour generation, mode choice, location choice, TOD choice, etc.
The supply side includes skimming and traffic assignment over the network.
Other choices? Yes. We include logsums as a independent variable in the utility functions of many models, such as mode choice, even auto ownership choices. Impedance between zones is a big part of logsum, and spatial resolution definitely has direct impact on impedance and in turn logsums.
Read supply side
We ran our model on a base scenario and a scenario with smaller zones, and here are some results:

## Slide 9: Result Analysis Walkability
Chart: 
| Base | Small Zones
 | 8718313 | 9028357
Chart: 
| Base | Small Zones
 | 128974 | 132712
Walkable zone pairs
Walkable zone-TAP pairs
Notes: Let’s first take a look at the walkable zone pairs and walkable zone to TAP pairs.
We treat zone pairs less than 3 miles as walkable zones, and zone to TAP pairs less than 1 mile as walkable.
TAP-transit access point, consider it as a transit hub.
Number of walkable zone pairs:
Base: 8.72 mil
Small: 9.03 mil
Increase: 3.6%
Number of walkable zone-TAP pairs:
Base: 128,974
Small: 132,712
Increase: 2.9%
Smaller zones improve walkability

## Slide 10: Result Analysis Avg Walk Distance Btw Zones
Chart: 
| Avg_Walk_Dist | Avg_WalkTransit_Dist
Base | 1.9247 | 0.65401
Small Zones | 1.9252 | 0.64834
Notes: We also looked at average walk distance between zones.
Avg walk distance between zones:
Base: 1.9247
Small: 1.9252
Barely change
Avg walk distance between zone-TAP pairs:
Base: 0.654
Small: 0.648
Barely change
Small zones don’t have too much impact on walk distance between zones.
However, if you look at bike distance, it tells us a different story.

## Slide 11: Result Analysis Avg Bike Distance Btw Zones
Chart: 
| Base | Small Zones
 | 15.8645 | 11.5779
Notes: Avg walk distance between zones:
Base: 15.86
Small: 11.58
A 27% decrease !!!!
Why the avg walk distance didn’t change much, while bike distance decreased significantly in the small zones scenario?
We think it is because walkable zones tend to be in urban areas, where TAZ is ALREADY small. As a matter of fact, a lot of TAZs in urban area have only one MGRA in them. So, transition from TAZ to MGRA doesn’t have too much impact on walk distance.
On the other hand, the bikeable threshold is 20 miles, a lot of large rural zones are bikable. Changing from TAZ to MGRA in rural area, will have much more impact than in urban area.
Above, we have talked about the spatial resolution impact on model inputs. Now let’s take a look at its impact on model output, more specifically mode share and trip distance.

## Slide 12: Result Analysis Trips by Mode
 | Trips |  |  | Mode Shares |  | 
Mode | Base | Small Zones | Diff | Base (%) | Small Zones (%) | Diff %
Auto | 8,944,716 | 8,938,479 | -6237 | 85.40 | 85.35 | -0.06%
Walk | 1,063,005 | 1,065,769 | 2764 | 10.15 | 10.18 | 0.27%
Bike | 101,848 | 114,498 | 12650 | 0.97 | 1.09 | 12.43%
Walk to Transit | 202,856 | 192,762 | -10094 | 1.94 | 1.84 | -4.96%
Other Transit | 19,506 | 19,410 | -96 | 0.19 | 0.19 | -0.48%
Other | 142,582 | 142,384 | -198 | 1.36 | 1.36 | -0.13%
Total | 10,474,513 | 10,473,302 |  | 100.00 | 100.00 | 
Notes: Total trips: barely changed, good.
Auto trips: the absolute auto trip reduced by 6200 trip in the small geography scenario, percentage wise it is small less than 0.1% reduction.
Walk trips: 2700 more, a 0.26% increase
Bike trips: 12,650 more, a significant 12.4% increase
Walk to transit trips: 10,000 less, a 5% decrease. This is counter intuitive. We think it might be related the fact that transit routes are mostly in urban areas, where TAZs are small already, so the smaller geography doesn’t matter much. Why the walk to transit trips actually decreased? It might the result of competition from walk and bike trips.
Overall, auto trips decreased by 6000 trips per day, and non-motorized trips increase by 15000 trips per day.

## Slide 13: Result Analysis Avg Walk Trip Distance
Chart: 
| Avg_Walk_Dist | Avg_WalkTransit_Dist
Base | 0.79371 | 0.38294
Small Zones | 0.82993 | 0.36579
Notes: Avg walk trip distance
Base: 0.79
Small: 0.83
Didn’t change much
Avg walk to transit distance
Base: 0.38
Small: 0.37
Didn’t change much

## Slide 14: Result Analysis Avg Bike Trip Distance
Chart: 
| Base | Small Zones
 | 2.1748 | 2.3748
Notes: Avg bike trip distance:
Base: 2.17
Small: 2.37
A 9.2% increase.
We think it is because as we have seen a lot more zones are bikeable in small zone scenario, and it resulted in significantly more bike trips (12.6K), the newly added trips tend to be longer trips previously not within the 20 mile bike threshold. Overall, it push the average bike distance longer.

## Slide 15: Conclusions
Finer spatial resolution
  Improve walkability
  Non-motorized trips increase and auto trips decrease
  Impact on bike trips more significant than on walk trips
How much more detail is enough?
  What is important to you?
  Other things to consider
Notes: Does spatial resolution matter? Yes, it matters.
Walkability: number of walkable zone pairs and zone to TAP pairs increase by 3-4%.
Auto trips decreases and non-motorized trips increase, particularly bike trips.
Smaller zones have bigger impact on bike trips than walk tips, in terms of both volumes and average trip distance.
How much more detail is enough?
It depends on what is important to you, or what kind of policy questions you are trying to address. Introducing smaller zones will not change your overall mode shares, for example. After all bike and walk modes are much smaller than auto modes, even a significant change in bike and walk mode will not have a big impact on the large picture.
However, if you use your model in bike projects. Then, using smaller zones does make a big difference. Not only we have seen the overall bike volume increased, but also bike trip distance changed significantly.
So, is it always better to use smaller zones? It is a tough question, as you have to balance many aspects of the model. For example, there are other things you need to consider.
Going with smaller zones will present challenges to your land use inputs.
  Accuracy
  Forecastable?
Going with smaller zones will also present challenges to your software performance
  Model runtime
  Memory footprint

## Slide 16: Questions?
Contact: Wu Sun
619-6995757
Wu.Sun@sandag.org