## Slide 1
Praveen Pasumarthy, P.E., PTOE, CDM Smith
Chris Edmonston, AICP, FDOT
Paul Fang, FDOT
Innovative Methodology to Identify Congested Roadways and Bottlenecks
15th TRB National Transportation
Planning Applications Conference

## Slide 2: Introduction
Background
Study Purpose
Scope of Study
Study Findings
Next Steps

## Slide 3: Background
Notes: Strategic Intermodal System (SIS) was created in 2003
  Designate facilities and services of statewide significance
  Serve the mobility needs of citizens, businesses, and visitors
  Help Florida to
  become a worldwide economic leader,
  enhance economic prosperity and competitiveness,
  enrich quality of life, and
  reflect responsible environmental stewardship.

## Slide 4: Study Purpose
Identify bottlenecks on Strategic Intermodal System (SIS)
Use the data available with FDOT
Identify bottlenecks at statewide and district level
Present the results in easy to understand format

## Slide 5: Scope of the Study
Activity 1: Data review
  Data available with FDOT
  Vehicle probe data
Activity 2: Methodology to identify bottlenecks
  Research efforts in the field of congestion and bottlenecks
  Contemporary practices by DOTs, MPOs, etc.
  Develop the methodology
Activity 3: Identify bottlenecks
  Analyze the data
  Prepare maps/graphics

## Slide 6: Data Sources
Existing FDOT Data Sources
  Roadway Characteristics Inventory (RCI)
  Traffic Monitoring Program
    Telemetered Traffic Monitoring Sites (TTMSs)
    Portable Traffic Monitoring Sites (PTMSs)
Vehicle Probe Data
  INRIX’s Vehicle Probe Data – Phase I
  FHWA’s NPMRDS from HERE – Phase II

## Slide 7: FHWA’s NPMRDS on NHS

## Slide 8: FHWA’s NPMRDS on SIS

## Slide 9: Coverage of FHWA’s NPMRDS
Passenger Data
Freight Data

## Slide 10: Coverage of FHWA’s NPMRDS
Daily
Hourly
Monthly
Chart: Observations (in millions)
| 0 | 1.0416666666666667 | 8.3333333333333495E-2 | 0.125 | 0.16666666666666699 | 0.20833333333333401 | 0.25 | 0.29166666666666702 | 0.33333333333333398 | 0.375000000000001 | 0.41666666666666702 | 0.45833333333333398 | 0.500000000000001 | 0.54166666666666796 | 0.58333333333333404 | 0.625000000000001 | 0.66666666666666796 | 0.70833333333333504 | 0.750000000000001 | 0.79166666666666796 | 0.83333333333333504 | 0.875000000000002 | 0.91666666666666796 | 0.95833333333333504
Count(TMC) | 1035539 | 885380 | 841109 | 941587 | 1292891 | 2024305 | 3008111 | 3493362 | 3658332 | 3789750 | 3819575 | 3864035 | 3867858 | 3874993 | 3882974 | 3881997 | 3649107 | 3413406 | 2993377 | 2588617 | 2360260 | 1718736 | 1467154 | 1229271
Chart: Observations (in millions)
| 0 | 1.0416666666666667 | 8.3333333333333495E-2 | 0.125 | 0.16666666666666699 | 0.20833333333333401 | 0.25 | 0.29166666666666702 | 0.33333333333333398 | 0.375000000000001 | 0.41666666666666702 | 0.45833333333333398 | 0.500000000000001 | 0.54166666666666796 | 0.58333333333333404 | 0.625000000000001 | 0.66666666666666796 | 0.70833333333333504 | 0.750000000000001 | 0.79166666666666796 | 0.83333333333333504 | 0.875000000000002 | 0.91666666666666796 | 0.95833333333333504
405530 400945 423417 478729 554119 631632 723697 773751 830393 921670 969471 979961 968070 954341 947152 912868 870941 812772 735807 646673 574632 517014 466485 426270 | 405530 | 400945 | 423417 | 478729 | 554119 | 631632 | 723697 | 773751 | 830393 | 921670 | 969471 | 979961 | 968070 | 954341 | 947152 | 912868 | 870941 | 812772 | 735807 | 646673 | 574632 | 517014 | 466485 | 426270
Chart: Observations (in millions)
| Mon | Tue | Wed | Thu | Fri | Sat | Sun
Count(TMC) | 10473328 | 10707428 | 10204994 | 10119351 | 10346783 | 6586883 | 5142959
Chart: Observations (in millions)
| Mon | Tue | Wed | Thu | Fri | Sat | Sun
Count(TMC) | 2796521 | 3019947 | 2832035 | 2772100 | 2649048 | 1523355 | 1333334
Chart: 
| Jul | Aug | Sept | Oct | Nov | Dec
 | 10359823 | 10953801 | 10033175 | 11060103 | 10433620 | 10741204
Chart: 
| Jul | Aug | Sept | Oct | Nov | Dec
 | 3091866 | 1008875 | 3046938 | 3312594 | 3171653 | 3294414
Passenger
Freight

## Slide 11: Methodology to identify bottlenecks
Summary of research efforts in the field of congestion and bottlenecks
Contemporary practices
  National performance reports
  State DOT practices
  MPO/Local government practices
Recommended methodology to identify bottlenecks on SIS network

## Slide 12: Congestion
FHWA defines congestion as “an excess of vehicles on a roadway at a particular time resulting in speeds that are slower - sometimes much slower - than normal or free flow speeds”
Recurring and non-recurring congestion
Chart: 
| Bottlenecks | Traffic Incidents | Work Zones | Bad Weather | Poor Signal Timing | Special Events
 | 0.4 | 0.25 | 0.1 | 0.15 | 0.05 | 0.05

## Slide 13: Bottleneck
Bottleneck can be defined as “a localized section of highway that experiences reduced speeds and inherent delays due to a recurring operational influence or a nonrecurring impacting event”
Recurring and non-recurring bottlenecks
Bottleneck occurs on a subordinate segment of a facility
Bottleneck certainly constitutes congestion, but congestion is often more than a bottleneck

## Slide 14: Bottleneck

## Slide 15: Recommended methodology
STEP 1:
Determine the purpose
STEP 2:
Develop a plan based on the uses and users
STEP 3:
Collect and process required data
STEP 4:
Calculate performance measures and identify bottleneck & congestion
STEP 5:
Communicate in a meaningful way

## Slide 16: Recommended methodology
  Primary purpose would be for planning purposes
  Bottlenecks should be identified using maps
  Resulting product should be easy to understand and interesting to read
STEP 1:
Determine the purpose
STEP 2:
Develop a plan based on the uses and users
STEP 3:
Collect and process required data
STEP 4:
Calculate performance measures and identify bottleneck & congestion
STEP 5:
Communicate in a meaningful way

## Slide 17: Recommended methodology
  Bottlenecks identified for auto and truck mode
  Bottlenecks identified based on weekday travel patterns
  Travel time reliability measures are used
  Yearly trends will be reported
  Statewide and district-level measures will be reported
STEP 1:
Determine the purpose
STEP 2:
Develop a plan based on the uses and users
STEP 3:
Collect and process required data
STEP 4:
Calculate performance measures and identify bottleneck & congestion
STEP 5:
Communicate in a meaningful way

## Slide 18: Recommended methodology
  Vehicle probe data from FHWA will be used
  FDOT data will be used for mapping purposes
STEP 1:
Determine the purpose
STEP 2:
Develop a plan based on the uses and users
STEP 3:
Collect and process required data
STEP 4:
Calculate performance measures and identify bottleneck & congestion
STEP 5:
Communicate in a meaningful way

## Slide 19: Recommended methodology
  Process FHWA NPMRDS data
  Identify performance measures
  Define and identify bottlenecks
STEP 1:
Determine the purpose
STEP 2:
Develop a plan based on the uses and users
STEP 3:
Collect and process required data
STEP 4:
Calculate performance measures and identify bottleneck & congestion
STEP 5:
Communicate in a meaningful way

## Slide 20: Recommended methodology
  Display results in easy-to-understand tables and graphics
  Present the yearly trends
  Present results statewide and by district
STEP 1:
Determine the purpose
STEP 2:
Develop a plan based on the uses and users
STEP 3:
Collect and process required data
STEP 4:
Calculate performance measures and identify bottleneck & congestion
STEP 5:
Communicate in a meaningful way

## Slide 21: Quantify Congestion/Bottleneck
NCHRP Report 398: Quantifying Congestion (1997)
Presented methods to measure congestion
Difficult to conceive of a single value to describe congestion
Four components in a congested roadway system
  Duration – amount of time congestion affects the travel system
  Extent – number of people or vehicles or geographic area affected by congestion
  Intensity – severity of the congestion
  Reliability – variation in the other three elements

## Slide 22: Quantify Congestion/Bottleneck
Phase I Methodology
Duration:
Extent:
Intensity:
Reliability:
Frequency of Congestion
None
None
Planning Time Index
Phase II Methodology
Duration:
Extent:
Intensity:
Reliability:
Frequency of Congestion
Vehicle Miles Traveled
Vehicle Hours of Delay
Planning Time Index

## Slide 23: Statewide sis Bottlenecks

## Slide 24: Next Steps
Phase II of the study is underway to identify the causes of top bottlenecks and suggest corrective actions
Incorporate the bottlenecks in FDOT’s Strategic Investment Tool
Update the list of top bottlenecks every two years
Update methodology using advancements in and coverage of vehicle probe data

## Slide 25: CONTACT
Praveen Pasumarthy, PE, PTOE
CDM Smith
pasumarthyvs@cdmsmith.com
850-386-9548